## Slide 1: Role of interface A in the IEEE 802.19.1 specification
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-07-16
Authors:

## Slide 2: Abstract
This presentation discusses the role of the interface A (WSO-CE interface) in the IEEE 802.19.1 specification.
We believe the specification must not impose anything on the WSO. This means also in our mind that the interface A must not be imposed.
The objective of this presentation is to convince the TG1 to agree to adopt the approach in which the IEEE 802.19.1 specification doesn’t contain any normative text on the interface A and its use.

## Slide 3: Role of the interface A
Interface A is informative and not binding
  The TG1 has agreed not to touch WSO and not to set requirements to WSOs and related RAT specifications
  We may not assume an interface to be mandatory for one side only. Thus the interface A can’t be mandatory for a CE either
Coexistence Enabler (CE) is a logical entity of the IEEE 802.19.1 coexistence system which has been designed to be the interface element for a WSO
A CE represents one WSO via thoroughly specified interface B1

## Slide 4: What we can’t say in our spec with respect to the interface A and why not?
We must not state something like follows:
  A CE shall issue a XYZ.request primitive to the WSO...
  A CE shall wait for a XYZ.response primitive from the WSO...
These kind of statements in the specification assume the interface A to be mandatory
In other words, these kind of statements assume the WSO to implement the interface A
We should focus on making it absolutely clear what is expected and required behavior over the exposed interfaces (B1, B2, B3) and leave integration of a WSO and a CE to vendors

## Slide 5: What the interface A and the COEX_MEDIA_SAP are then?
They are primarly in the specification to ”make the picture more complete”
  Might help readers and vendors to understand how a WSO and CE are expected to interact
  Might be considered as a design guideline for actual integration of a WSO and a CE
We may have as detailed specification of the COEX_MEDIA_SAP as wanted but we need to understand and bear in mind that implementation may be entirely different

## Slide 6: Summary
As device and device entity vendors we don’t want to see the IEEE 802.19.1 to fall into a trap of setting requirements to a WSO implementation
WSO vendor needs to have liberty to pick up any kind of WSO-CE integration as long as the CE operates properly as a part of the coexistence system
The IEEE 802.19.1 may still specify the interface A and the COEX_MEDIA_SAP with all the possible details. We just want to make sure the implementation may be entirely different and that’s up to the WSO and the CE vendor.

## Slide 7: Straw polls
The IEEE 802.19.1 specification doesn’t set any requirements to a WSO implementation
  Yes: , No: , Abstain:
The IEEE 802.19.1 specification doesn’t force implementation of the interface A
  Yes: , No: , Abstain:
The IEEE 802.19.1 specification doesn’t force a CE to use the COEX_MEDIA_SAP primitives
  Yes: , No: , Abstain:

## Slide 8: Motions
The IEEE 802.19.1 specification shall not set requirements to a WSO
  Yes: , No: , Abstain:
The IEEE 802.19.1 specification shall not mandate implementation of the interface A
  Yes: , No: , Abstain:
The IEEE 802.19.1 specification shall not force a CE to use the COEX_MEDIA_SAP primitives
  Yes: , No: , Abstain: