## Slide 1: How to accommodate different CE-CM interaction approaches in IEEE 802.19.1?
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-07-17
Authors:

## Slide 2: Abstract
This presentation contains a proposal to accommodate both pull and indication based approaches to the IEEE 802.19.1 specification for CE-CM interaction
The proposal is intended to help the TG1 to get forward in discussions on entity responsibilities

## Slide 3: The two approaches on table
Two approaches have been debated in the TG1 in context of a CE which is subscribed to the information service
  Pull based approach
    A CE may request the CM to provide an up to date coexistence report whenever needed
    A CM doesn’t send unsolicited coexistence reports
  Indication based approach
    A CM shall send a coexistence report update whenver there is a change in the report
The TG1 has not yet discussed how to satisfy the both approaches; our intent with this proposal is to have a solution which satisfies proposers of both approaches

## Slide 4: The proposal – Introduction
Specify profiles for the CE-CM interaction which determine which of the approaches is supported and used
  Profiles are specified for CE and CM
    In CM case the profile applies to behavior to the direction of a CE only
    In CE case the profile applies to the entire CE
  Profiles determine which of the procedures are mandatory and which are optional
  The profile is reflected in PICS as conditional feature support
    Feature support is conditional on profile

## Slide 5: The proposal – Two profiles
The proposal is to specify two profiles for the two approaches which have been debated lately
  Pull_Profile
    Support of this profile means that coexistence report delivery from a CM to a CE is based on requests from the CE
  Push_Profile
    Support of this profile means that coexistence report deliver from a CM to a CE is based on unsolicited announcements from the CM
Each CE and CM shall support at least one of the profiles
A CE may be served only by a CM which supports the profile the CE supports

## Slide 6: Two profiles in procedure support
Pull_Profile
  CE
    The CE shall support the obtaining coexistence report procedure specified in 5.2.4.2
    The CE may support the providing coexistence report procedure specified in 5.2.4.4
  CM
    The CM shall support the obtaining coexistence report procedure specified in 5.2.4.2
    The CM may support the providing coexistence report procedure specified in 5.2.4.4
Push_Profile
  CE
    The CE may support the obtaining coexistence report procedure specified in 5.2.4.2
    The CE shall support the providing coexistence report procedure specified in 5.2.4.4
  CM
    The CM may support the obtaining coexistence report procedure specified in 5.2.4.2
    The CM shall support the providing coexistence report procedure specified in 5.2.4.4

## Slide 7: What does this mean?
Profiles allow for a CE vendor to decide whether it wants to implement a CE based on the pull or push approach or whether to support both
Profiles allow for a CM vendor to decide whether it wants to implement a CM based on the pull or push approach or whether to support both
A CE may be registered only to a CM with same profile support
The profiles have no implications to CM-to-CDIS or CM-to-CM interactions

## Slide 8: Further remarks
This proposal concentrates on the issue of two approaches related to use of the information service
  How a CE gets the coexistence report from the CM to which it is registered?
Consequently the profiling is limited only to the few procedures which relate to the delivery of the coexistence report
If there are similar kind of differences in the CE-CM interaction design, the profiles can be extended to those issues as well if needed

## Slide 9: Summary
A proposal to accommodate both pull and push based coexistence report delivery procedures in the IEEE 802.19.1 specification is provided
The proposal is to specify profiles for both CE and CM to allow for a vendor to decide on which approach to support in the implementation
The profile approach can be extended to apply to other procedures as well in the CE-to-CM interaction
We believe the CM-CM and CM-CDIS interactions should be unified and kept free from profiles to avoid split into multiple coexistence systems