## Slide 1: How to accommodate different CE-CM interaction approaches in IEEE 802.19.1?
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-07-17
Authors:

## Slide 2: Abstract
This presentation contains a proposal to accommodate both pull and indication based approaches to the IEEE 802.19.1 specification for CE-CM interaction
The proposal is intended to help the TG1 to get forward in discussions on entity responsibilities
This version of the presentation contains an alternative proposal based on discussion of the r0 of the proposal during San Diego meeting

## Slide 3: The two approaches on table
Two approaches have been debated in the TG1 in context of a CE which is subscribed to the information service
  Pull based approach
    A CE may request the CM to provide an up to date coexistence report whenever needed
    A CM doesn’t send unsolicited coexistence reports
  Indication based approach
    A CM shall send a coexistence report update whenver there is a change in the report
The TG1 has not yet discussed how to satisfy the both approaches; our intent with this proposal is to have a solution which satisfies proposers of both approaches

## Slide 4: The proposal
A CM shall send an unsolicited announcement whenever there is a change in the coexistence report
  The unsolicited announcement may contain the up to date coexistence report
A CE which receives an unsolicited announcment may send a coexistence report request to the CM
  A CE may not send unsolicited coexistence report requests

## Slide 5: Summary
A revised proposal to accommodate both pull and push based approaches in the coexistence system specification is provided
The proposal does provide a CE vendor liberty to use either the pull based method or the push based method
The proposal does provide guarantee that there will be no unnecessary really frequent requests from CEs to CMs
The proposal doesn’t require implementation of profiles in the specification