## Slide 1: How to accommodate different CE-CM interaction approaches in IEEE 802.19.1?
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-07-17
Authors:

## Slide 2: Abstract
This presentation contains a proposal to accommodate both pull and indication based approaches to the IEEE 802.19.1 specification for CE-CM interaction
The proposal is intended to help the TG1 to get forward in discussions on entity responsibilities
This version of the presentation contains an alternative proposal based on discussion of the r0 of the proposal during San Diego meeting

## Slide 3: The two approaches on table
Two approaches have been debated in the TG1 in context of a CE which is subscribed to the information service
  Pull based approach
    A CE may request the CM to provide an up to date coexistence report whenever needed
    A CM doesn’t send unsolicited coexistence reports
  Indication based approach
    A CM shall send a coexistence report update whenver there is a change in the report
The TG1 has not yet discussed how to satisfy the both approaches; our intent with this proposal is to have a solution which satisfies proposers of both approaches

## Slide 4: The proposal
Basic procedures for coexistence report delivery are as specified now in the draft
  Obtaining coexistence report specified in 5.2.4.2 (”pull”)
  Providing coexistence report specified in 5.2.4.4 (”push”)
A new procedure to be specified with which a CE can configure how often a CM may transmit unsolicited coexistence reports
  A CE transmits to a CM a configuration request in which it indicates the minimum interval for unsolicited coexistence reports from the CM
  The CM transmits unsolicited coexistence reports only when the report has been changed since the previous transmission of the report and as per the configuration from the CE
The same new procedure will be available for a CM to configure how often a CE may transmit coexistence report requests
  A CM transmits to a CE a configuration request in which it indicates the minimum interval for coexistence report requests from the CE
  The CE transmits coexistence report requests as per the configuration from the CM