## Slide 1: TG1 Draft Topics
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-09-19
Authors:

## Slide 2: Abstract
This presentation contains discussion material on TG1 draft topics which are proposed to be the basis of the TG1 agenda during the September 2012 interim meeting in Indian Wells, CA.
The proposal is to have the topics discussed in the meeting with the objective to have an agreement in the TG on solutions which are intended to end up to the draft.

## Slide 3: Introduction
Each topic contains originally just a set of remarks and questions which the contributor believes are open and need to be resolved for the draft.
The intention is to have the TG to discuss the topics openly and extensively during the September 2012 meeting and agree on answers to the questions. The answers are expected to end up becoming solution descriptions on which draft normative text can be prepared for new updated TG1 draft.
Motions are planned on the results of topic discussions

## Slide 4: Topic list
Connection setup and security
Configuration of pull and push methods
Protocol description for section 5
Mandatory and optional features
What is mandatory in a CE and in a CM?
What is mandatory in a CDIS?
Inside CDIS
Update to sections 6, 7 and 8

## Slide 5: Topic 1: Connection setup and security
IEEE 802.19.1 system builds upon use of IP and protocols on top of the IP
  All the 802.19.1 messages are carried over IP
Before one can run the coexistence protocol, one needs to have IP configured
  We have description as the resolution of comment #11 on how entities determine IP addresses (port numbers etc.) to be used
There has been questions on whether the authentication mechanism currently in the draft is enough

## Slide 6: Topic 1: Connection setup and security (cont.)
A proposal is to have the following text added to the draft to describe how entities interconnect in order to start exchanging coexistence system protocol messages
  IEEE 802.19.1 entities may be co-located or they may be located anywhere on the internet. In order to communicate efficiently and in a secure fashion, the communications are made through ssh tunnels.
  When an entity wishes to communicate with another entity (CE to CM, CM to CM or CM to CDIS) it first seeks for an existing connection to this entity. If the connection does not exist, it creates a connection using a username@IPaddress with password combination or a username@IPaddress alone when a pre-shared private/public key set exists.
  When entities are co-located, they may use IPaddress 127.0.0.1. Alternatively, if the interface between the two co-located entities is not exposed, any other internal mechanism may be used to communicate between the entities.
  Entities may also use alternative pre-arranged ports to communicate (default is port 22). If an entity wishes to maintain a connection open, is should create activity in the connection at least once per minute. If an entity senses a connection has stayed inactive for more than 2 minutes, it may presume the connection is no longer needed and may close it.

## Slide 7: Topic 1: Connection setup and security (cont.)
The IEEE 802.19.1 system shall communicate using TCP/IP
  Moved by: Ivan Reede
  Seconder: Jinho Kim
  Vote: Unanimous

## Slide 8: Topic 1: Connection setup and security (cont.)
TLS vs SSH
 | TLS | SSH
Pros | Aligned with PAWS | Smaller implementation
Cons | Server authentication is optional Requires PKI, X.509, certificates Inherintely vulnerable to man in the middle attacks | Less scalable than PKI
Notes | More recent than the SSH | 

## Slide 9: Topic 2: Configuration of pull and push methods
During the July 2012 plenary the TG agreed that both methods are needed
The TG also agreed that we need to have ways to control transmissions of unsolicited announcements and requests
The TG didn’t agree on solution

## Slide 10: Topic 2: Configuration of pull and push methods (cont.)
One solution is to have the TCP/IP to manage the issue of too frequent announcements and requests

## Slide 11: Topic 3: Protocol description for section 5
The section 5 is called ”Procedures and protocols” with the sub-section 5.2 describing procedures and the sub-section 5.3 describing messages
Is the message definitions enough on the protocol or should we have something added?
  Entity identifiers should be specified somewhere, the question is whether section 5 is the right place

## Slide 12: Topic 4: Mandatory and optional features
Does an entity need to support parameters labeled as optional in the message description?
Does an entity need to support all the procedures of the spec?
Does the spec mandate specific implementation of interface A?

## Slide 13: Topic 4: Mandatory and optional features (cont.)
  A CDIS shall be able to provide coexistence discovery service to any type of CM
  A CM shall be able to exchange information with any other type of CM
Approach 1
  A CM shall support all CE profiles
Approach 2
  A CM doesn’t have to be able to serve all CE profiles, a CM shall be able to support at least one CE profile

## Slide 14: Topic 4: Mandatory and optional features (cont.)
Approach 1 vs. Approach 2
 | Approach 1 | Approach 2
Pros | Usage simplicity since a CE can work with any CM | Enable fast and simple implementation of CM and CE, feature/cost competition, allow market to select
Cons | Design complexity, IP traps | Need to match CE and CM
Notes |  | 

## Slide 15: Topic 5: What is mandatory in a CE and in a CM?
The following shall be supported by each CE
  Basic procedures (authentication, subscription, registration)
  A CE shall support at least one profile
    A profile determines which procedures are mandatory and which are optional. A profile covers also the basic procedures.
    A profile determines which messages, parameters and functions are mandatory and which are optional.
  A CE shall support at least management service or information service or may support both. Its support may be dependent on the WSO it interfaces
  A CE shall interface a WSO to a CM

## Slide 16: Topic 5: What is mandatory in a CE and in a CM? (cont.)
The following shall be supported by each CM
  Basic procedures (authentication, subscription, registration)
  A CM shall be able to exchange information with any other type of CM
  A CM shall support at least one profile
    A profile determines which procedures are mandatory and which are optional. A profile covers also the basic procedures.
    A profile determines which messages, parameters and functions are mandatory and which are optional.
  A CM shall support both management service and information service

## Slide 17: Topic 6: What is mandatory in a CDIS?
The following shall be supported by each CDIS
  Basic procedures (authentication, subscription, registration)
  A CDIS shall be able to provide coexistence discovery service to any type of CM

## Slide 18: Topic 7: Inside CDIS
TBD

## Slide 19: Topic 8: Update to sections 6, 7 and 8
TBD