## Slide 1: LTE-U Coexistence Mechanisms
Date: 2014-05-07
Authors:

## Slide 2: Abstract
This is an overview of two potential LTE-U coexistence mechanisms operating in a non-coordinated manner.

## Slide 3: Listen Before Talk (LBT)
Channel access attempted at pre-assigned TXOP
  Sense the channel on a subframe boundary
    Perform multi-subframe DL if the channel is available
    Do not transmit if energy (above a threshold) is detected
      Channel switch if too many unsuccessful attempts are made
  Leave coexistence gap following DL transmission

## Slide 4: Coexistence Gap (CG)
LTE transmission includes gap periods to provide opportunities for other networks to operate.
  A Coexistence Gap is an LTE “off” period.
  Following a CG, LTE begins transmission without assessing channel availability.

## Slide 5: CG Interference Scenarios

## Slide 6: Dynamic Coexistence Gaps
CG may be dynamically updated to account for loads on the WiFi and LTE side.
  e.g. High LTE load, few secondary WiFi users → short CG
    Maximum LTE duty cycle allows for WiFi beacon

## Slide 7: Simulations
Scenario 1:
  Configuration
    High interference scenario, LBT and CG effect on both LTE and WiFi
      Dense deployment of 4 APs (each with 3 STAs), 3 eNBs (each with 3 UEs)
      No fading/shadow, only free space pathloss
      WiFi detection threshold for LTE 20 dB higher than for other WiFi
      Parameters chosen so both LBT and CG result in 50% LTE channel usage
  Results
    LTE LBT throughput gain 18% over CG
    WiFi LBT throughput gain 6.3% over CG

## Slide 8: Simulations
Scenario 2 Configuration:
  LBT and CG effect on WiFi performance
    Modify parameters to get various duty cycles
    WiFi nodes sense and defer to all LTE transmissions (higher sensitivity)
    Less dense deployment than Scenario 1
  No hidden nodes
  RTS/CTS enabled
  1500 byte MPDU
  WiFi loads of 4 & 9 Mbps
  LTE: full buffer

## Slide 9: Scenario 2 Results

## Slide 10: Conclusions
Both LBT and CG methods can be tuned to work reasonably well and in most cases offer similar performance.
LBT out-performs CG in highly congested channels (note that LBT is more complex to implement).
  The performance advantage of LBT shown is an upper bound and may in practice be smaller than shown.
Medium WiFi traffic load is not impacted if the LTE duty cycle is 50% or lower

## Slide 11: References
M. Beluri et al., "Mechanisms for LTE Coexistence in TV White Space," in Proceedings of IEEE International Symposium on Dynamic Spectrum Access Networks (DySPAN), Bellevue, WA, United States, 16-19 Oct. 2012.