## Slide 1: LTE-U Coexistence Mechanisms
Date: 2014-05-07
Authors:

## Slide 2: Abstract
This contribution contains an overview of the current state of work in 3GPP in license exempt bands. Included is an overview of two potential LTE-LAA* coexistence mechanisms operating in a non-coordinated manner.
*LTE-U is now LTE-Licensed Assisted Access

## Slide 3: LTE-LAA (LTE-U) Update (1/2)
Chair’s Notes [6] indicate:
Focus on 5 GHz band, indoor and outdoor
Licensed-Assisted Dual Connectivity
Stand-alone operation not currently in the works
Nokia [4]:
“LAA on unlicensed band is always combined with licensed band LTE”
Shows good performance (fairness) with listen-before-talk
Qualcomm [5]:
Unlicensed as a complement to the licensed band
Some performance (throughput) results using listen-before-talk

## Slide 4: LTE-LAA (LTE-U) Update (2/2)
Huawei [3]:
Operator controlled non-residential scenarios
Non stand-alone deployments
  Both co-located and non-co-located
Requirements:
  Hotspot offloading
  Unified management
  Co-existence
Ericsson [2]:
Some regions require listen-before-talk
Proposes timeline for the WI/SI

## Slide 5: Summary from the Update
No stand-alone operation (any time soon)
  Carrier aggregation with the primary in licensed bands
3GPP will not require changes to 802.11 to work
Likely to see LBT/CCA along with some kind of CG

## Slide 6: Listen Before Talk (LBT)
Channel access attempted at pre-assigned TXOP
  Sense the channel on a subframe boundary
    Perform multi-subframe DL if the channel is available
    Do not transmit if energy (above a threshold) is detected
      Channel switch if too many unsuccessful attempts are made
  Leave coexistence gap following DL transmission

## Slide 7: Coexistence Gap (CG)
LTE transmission includes gap periods to provide opportunities for other networks to operate.
  A Coexistence Gap is an LTE “off” period.
  Following a CG, LTE begins transmission without assessing channel availability.

## Slide 8: CG Interference Scenarios

## Slide 9: Dynamic Coexistence Gaps
CG may be dynamically updated to account for loads on the WiFi and LTE side.
  e.g. High LTE load, few secondary WiFi users → short CG
    Maximum LTE duty cycle allows for WiFi beacon

## Slide 10: Simulations
Scenario 1:
  Configuration
    High interference scenario, LBT and CG effect on both LTE and WiFi
      Dense deployment of 4 APs (each with 3 STAs), 3 eNBs (each with 3 UEs)
      No fading/shadow, only free space pathloss
      WiFi detection threshold for LTE 20 dB higher than for other WiFi
      Parameters chosen so both LBT and CG result in 50% LTE channel usage
  Results
    LTE LBT throughput gain 18% over CG
    WiFi LBT throughput gain 6.3% over CG

## Slide 11: Simulations
Scenario 2 Configuration:
  LBT and CG effect on WiFi performance
    Modify parameters to get various duty cycles
    WiFi nodes sense and defer to all LTE transmissions (higher sensitivity)
    Less dense deployment than Scenario 1
  No hidden nodes
  RTS/CTS enabled
  1500 byte MPDU
  WiFi loads of 4 & 9 Mbps
  LTE: full buffer

## Slide 12: Scenario 2 Results

## Slide 13: Conclusions
Both LBT and CG methods can be tuned to work reasonably well and in most cases offer similar performance.
LBT out-performs CG in highly congested channels (note that LBT is more complex to implement).
  The performance advantage of LBT shown is an upper bound and may in practice be smaller than shown.
Medium WiFi traffic throughput is not impacted if the LTE duty cycle is 50% or lower

## Slide 14: References
[1] M. Beluri et al., "Mechanisms for LTE Coexistence in TV White Space," in Proceedings of IEEE International Symposium on Dynamic Spectrum Access Networks (DySPAN), Bellevue, WA, United States, 16-19 Oct. 2012.
[2] 3GPP Tdoc RP-140770 “Study on Licensed-Assisted Access using LTE”
[3] 3GPP Tdoc RP-140786 “Motivation of the New SI Proposal: Study on License-Assisted Access using LTE”
[4] 3GPP Tdoc RWS-140002 “LTE in Unlicesnsed Spectrum: European Regulation and Co-existence Considerations”
[5] 3GPP Tdoc RWS-140008 “Extending the benefits of LTE to unlicensed spectrum”
[6] 3GPP Tdoc RWS-140029 “Chairman Summary”