## Slide 1: Fair Spectrum Sharing in Unlicensed Spectrum
Date: 2014-09-18
Authors:

## Slide 2: Background
Extending the technologies that have conventionally used licensed spectrum to the unlicensed bands are changing the ecosystem in the unlicensed spectrum.
  The medium access techniques used by these technologies are based on the assumption that no other system is operating in the same channel and hence no need for spectrum sharing.
  802 systems, on the other hand, have built-in mechanisms to share the spectrum with other similar or dissimilar systems (e.g., CCA mechanism in 802.11 or Adaptive Frequency Hopping in 802.15.1)
  Extremely unfair spectrum sharing scenarios could arise when these systems operate in the same band (see the contribution 802.19-14/0037r2)
So far, there is not a clear definition of “fairness” in unlicensed bands.
This presentation attempts to provide an answer to the question that “How would fair spectrum sharing among multiple systems operating in an unlicensed band look like?”
  This presentation does not propose a solution to achieve this fairness.

## Slide 3: Coexistence Requirements
The coexistence requirements must ensure an equitable share of wireless resources* in the long run for each of the networks sharing the unlicensed spectrum.
The coexistence requirements must ensure that each network receives a minimum amount of wireless resources in the short run.
  Each network may use this to make sure that the KPI requirements for the services designed for it are met.
The coexistence metric must be oblivious to the spectral and system efficiency of each network (i.e., how efficiently a given system utilizes its resources).
* Wireless resources= Time × Bandwidth

## Slide 4: Notations
Assume n systems share an unlicensed band with a total of B units of bandwidth.
For any time t, denote the bandwidth used by system i (1≤i≤n) at time t as Bi(t).
Assume that system i (1≤i≤n), has possible signal bandwidths which are less than B:
  Example: For B=100 MHz, an 802.11ac system has 3 signal bandwidths less than 100 MHz (i.e., 20, 40 and 80 MHz)
For any time t, sum of the bandwidths used by the n systems must be less than or equal to B.

## Slide 5: Long Run Fairness Requirement based on Time-Bandwidth product metric
Denote the resource (time-bandwidth product) demand of system i during the long run (time interval of length for an appropriate ) as
Denote the set indices of systems that demand less than an equal share of wireless resources in the long run as , i.e.,
We must have
where |Λ| denotes the cardinality (number of elements) in set Λ.

## Slide 6: Short Run Requirement
For some appropriate and , each system must be allocated a minimum amount of resources during the time intervals of length

## Slide 7: Maximum Delay (derived from the short run requirement)
The maximum possible delay is on the order of
(See below)
For the acceptable level of delay equal to , we must have
t
B

## Slide 8: Example Spectrum Sharing Scenario
n=2, B=100 MHz
System 1: 802.11ac
System 2: LTE-A
Both systems demand more than half the wireless resources
  Both systems must receive half of the wireless resources in the long run
B1(t) ∈ {0, 20 MHz, 40 MHz, 80 MHz}
B2(t) ∈ {0, 20 MHz, 40 MHz, 60 MHz, 80 MHz, 100 MHz}
Tl=10 sec
δ= 40 msec, Ts=20 msec, Δ=20 MHz × 10 msec
2(Ts-Δ/B)=36 msec < δ=40 msec
✔

## Slide 9: Example Fair spectrum sharing satisfying the proposed requirements
System 1 (802.11ac)
System 2 (LTE-A)
100
40
10000
t (msec)
BW (MHz)
80
20
20
60
60
The same pattern repeats
10
30
50
70
80
40

## Slide 10: References
  [1] 802.19-14/0037r2: Impact of LTE in Unlicensed Spectrum on WiFi
  [2] A. Babaei, J. Andreoli-Fang and B. Hamzeh, “On the Impact of LTE-U on Wi-Fi Performance,” in Proceedings of IEEE PIMRC 2014 conference.