## Slide 1: Report from ETSI TC BRAN#81
Date: 2015-01-12
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
This document contains information and opinions of the author, from the ETSI TC BRAN#81 meeting that took place in Las Palmas, Gran Canaria December 16-19, 2015, with a focus on EN 301 893 comment resolution and revision.

## Slide 3: BRAN Agenda Items
New Work Items (WI)
  ETSI Technical Report (TR) on Coexistence with EESS in 5 GHz
  ETSI TR on Coexistence with ITS and Road Tolling in 5 GHz
  ETSI TR on Coexistence with radiolocation in 5 GHz
  DA2GC in 5 GHz with beamforming antennas
  DA2GC in 5 GHz with fixed antennas
  Revision of EN 301 893 for compliance with the new Radio Equipment Directive
EN 301 893 - 5 GHz high performance RLAN – Comment Resolution

## Slide 4: Summary
Work Items approved
  ETSI Technical Report (TR) on Coexistence with EESS in 5 GHz
  ETSI TR on Coexistence with ITS and Road Tolling in 5 GHz
  ETSI TR on Coexistence with radiolocation in 5 GHz
  DA2GC in 5 GHz with beamforming antennas
  DA2GC in 5 GHz with fixed antennas
WI for EN 301 893 RED compliance includes final resolution of paragraph 4.8.3.2 LBT for Load Based Devices
EN 301 893 v1.7.3 (to become v1.8.1) was approved
  Paragraph 4.8.3.2 maintains the wording from v1.7.1
  Adds an alternate based on inputs from the Wi-Fi industry

## Slide 5: Revision of EN 301 893
The issue with Paragraph 4.8.3.2
  LBT for Load Based Devices of v1.7.1 provided sufficient “adaptivity” to meet EC requirements while 802.11 was the only technology in the band
  The introduction of other technologies in compliance with 4.8.3.2 could severely disadvantage Wi-Fi
    CableLabs, Broadcom and WFA submitted simulations showing this
    Wi-Fi could virtually be excluded where v1.7.1 compliant devices operated
  Exponential backoff, the primary Wi-Fi to Wi-Fi coexistence mechanism not in the text
New DFS test requirement, test uncertainties made approval of v1.7.x necessary at this time

## Slide 6: The Players
LAA-LTE representation (Q/E/N)
  Qualcomm (Jamshid Khun Jush)
  Ericsson (Enrico Brancaccio)
  Nokia Networks (Esa Barck)
IEEE 802.11 representation
  Broadcom (David Boldy)
  Cisco (Andrew Myles)
  Wi-Fi Alliance (Octavian Popescu)
  CableLabs (Volker Leisse)
  Microsoft (Scott Blue)
  Mediatek (Rich Kennedy)

## Slide 7: The Arguments
IEEE 802.11
  V1.7.1 leaves Wi-Fi vulnerable to unfair sharing
  Simulations by CableLabs, WFA and Broadcom clearly demonstrate this
  Although proposed changes to Paragraph 4.8.3.2 still need to be improved to ensure fair sharing, this first step is needed so that Q/E/N LAA-LTE planning is based on a fair approach, not v1.7.1
Q/E/N
  No changes should be made until a final solution is available
  Not yet known what LAA-LTE is until their simulations are done, so how can IEEE 802.11 know they will be disadvantaged
  Keep v1.7.1 Paragraph 4.8.3.2

## Slide 8: The Inconsistencies
Q/E/N requested delays , but v1.8.1 with new DFS changes had to be approved at the end of this meeting
Q/E/N stated that LAA-LTE is not yet known, but news during the week indicated that one vendor started device fabrication, Ericsson and T-Mobile announced 2015 availability
  http://www.computerworld.com/article/2861352/ericsson-pushes-plan-to-send-wireless-apps-over-unlicensed-5ghz-spectrum.html
Q/E/N simulation introduced late in the week showed 802.11 advantage over v1.7.1, but utilized 802.11a at 16 Mbps, not 802.11ac at more typical data rates
Q/E/N stated that their concerns were supported by eight EU regulators; all eight were identical in every way, including formatting and typos

## Slide 9: Other Issues
The UK regulator said Ofcom “…had acted as a post box in this” so the comments were an echo of the companies active on the UK market (therefore stakeholders), not necessarily reflecting the regulator’s views
Q/E/N accused the Chair of “…all week blackmailing the group…” in response to his statement that if this was not decided, BRAN would not meet its requirement to have a new draft
When Qualcomm denied that its representatives had been telling customers that LAA would “dominate the band”, one of those customers, Microsoft, rebutted the denial

## Slide 10: The Results
The group approved v1.7.3 (to become v1.8.1) with both the v1.7.1 and Wi-Fi industry proposal as alternatives for Paragraph 4.8.3.2, in spite of the Q/E/N effort to renege on the agreement at the last moment
The first draft of the new version will not be written until June of 2015, by request of Q/E/N, instead of delaying all work for 6 months as Q/E/N requested
The new WI, for RED compliance will resolve the 4.8.3.2 duality well before June 2017, when EN 301 893 is out of force
For the next 18 months v1.7.1 vulnerabilities will remain in the Harmonised Standard

## Slide 11: References
Approved v1.7.3 for National voting:
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000073r1_EN_301_893_HS_5_GHz_RLANs_for_national_voting.zip
The New Work Item
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000087r5_Revision_of_EN_301_893_to_become_a_HS_under_the_new_RE-Direc.zip
Minutes of the meeting:
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000092r1_Minutes_of_the_RCWG_sessions_during_BRAN_81.doc