## Slide 1: Unlicensed LTE/WiFi Coexistence Testbed
Date: 2015-07-06
Authors:

## Slide 2: Abstract
Propose an Unlicensed-LTE/Wi-Fi testbed for coexistence characterization.

## Slide 3: Intro to Unlicensed-LTE testbed
Goal was to design a RF environment that was flexible for handling variety of test Unlicensed LTE/LTE-LAA/LTE-U/Wi-Fi scenarios.
Based on our understanding the requirements for a wireless contention test bed are:
  High Isolation from external devices
  Good control over power levels across devices
  Multipath Environment to test MIMO STA’s
  Ability to test real applications (VoIP, Video streaming, file transfer, etc)
  Flexibility to test high channel load environments
  Repeatability and in a lab environment
Focused on simple scenario:
  Wi-Fi AP-STA baseline with added Wi-Fi or LTE eNB traffic

## Slide 4: Coexistence Testbed with multipath
OTA
Wi-Fi STAs
Ethernet, HDMI, USB Ports
802.11 AP
Ethernet
Ethernet
MIMO RF Splitter (8:4)
Wi-Fi sniffer
Multi-Path Emulation
LTE eNB
Wi-Fi
LTE
4
LTE STAs
LTE monitor
4
Attenuator
Attenuator
Goals:
-OTA Coexistence testing
-Multi Path Emulation (Can be bypassed)
-Wi-Fi traffic to clients benchmarked before and after LTE introduced
-Wi-Fi sniffer helps diagnose channel loading/packet timing
-Can be used to test real life applications (video streaming, VoIP, etc).
-Attenuation helps tune power received on STA’s.
-Splitter enables testing of two 4 stream Wi-Fi AP’s or a 4x4 Wi-Fi AP with a 2x2 LTE device.

## Slide 5: Coexistence Testbed w/o multipath
OTA
Wi-Fi STAs
Ethernet, HDMI, USB Ports
802.11 AP
Ethernet
Ethernet
Wi-Fi sniffer
LTE eNB
Wi-Fi
LTE
Attenuator
6-8
LTE STAs
LTE monitor
4
2-4
Goals:
-Similar to multipath testbed, but without splitters.
-AP and eNB couple OTA in top box via antennas.

## Slide 6: Extra Slides

## Slide 7: Possible STA arrangement
10 dB loss
Absorptive foam provides RX RSSI diversity to help test receiver sensitivity.

## Slide 8: Multiple Small Cell Testbed
LTE-U Indoor Simulation Scenarios (SI5-8)
-Based on test scenarios provided by 3GPP (See 1)
-Chaining chambers expands wireless loading/environment
-Multiple AP’s, Small Cells operating co-channel

## Slide 9: Multiple Small Cell Testbed
Wi-Fi
LTE
Wi-Fi/LTE STAs
Attenuator
Attenuator
Wi-Fi/LTE STAs
Wi-Fi
LTE
AP Box 1
AP Box 2
Client Box 1
Client Box 2
Attenuator
AP Box 3
Client Box 3
Wi-Fi
LTE
Wi-Fi/LTE STAs

## Slide 10: Possible Multiple Small Cell/Enterprise loading configuration
RF daisy-chain coupling to emulate space among AP/eNB pairs

## Slide 11: References
[1] LTE-LAA 3GPP Document 36.889-011