## Slide 1: Coexistence Management Considering Interference Alignment
Date: 2015-11-06
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:

## Slide 2: Abstract
This document proposes a general method that optimize the utilization of spectrum among secondary users (SUs) while maintaining the protection to primary users (PUs) based on interference alignment (IA).

## Slide 3: Objective of simulation
In this document, we show the simulation results for evaluating such new scenarios where interference alignment is used at secondary users.
By using the interference alignment more secondary users can be accommodated while maintaining protection to primary users (e.g., incumbent or PALs in 3.5GHz scenarios).
Channel information can be shared among SUs to provide better performance.

## Slide 4: Simulation Scenario
Multiple SSs coexist.
The radius of the whole system is set as 200 m, and the radius of each Secondary Radio System (SRS) is set as 20 m.
The number of the transmitting antennas is set as 4-8.
Rayleigh channel model and the free space path loss are assumed.
The complete CSI is known at SU’s transmitter .

## Slide 5: Simulation Parameters
Symbol | Definition | Value
f | Frequency | 5 GHz
NF | Noise Floor | -120 dBm
 | Number of transmitting antennas | 4
 | Number of receiving antennas | 2
R | Radius of Secondary radio system (SRS) | 200 m
length | Distance between transmitting antennas | 0.5λ
d | Distance between SBS | 1 m~400 m

## Slide 6: Simulation Result 1: Allowed number of users
Tolerable INR with coexisting users (dB)
When the number of transmitted antennas increases, the allowed access number of users is significantly improved.
The total allowed number of users achieves a significant improvement using IA-based channel admission control algorithm.
Note that co-channel interference among users is not considered in this figure

## Slide 7: Reference
[1] IEEE 802.19-15/0032r0, “The new coexistence use cases for IEEE 802.19.1”
[2] Nosrat-Makouei, Behrang, Jeffrey G. Andrews, and Robert W. Heath Jr. "A simple SINR characterization for linear interference alignment over uncertain MIMO channels." Information Theory Proceedings (ISIT), 2010 IEEE International Symposium on. IEEE, 2010, pp: 2288-2292
[3] Vin, H., Pawan Goyal, and Alok Goyal. "A statistical admission control algorithm for multimedia servers." Proceedings of the second ACM international conference on Multimedia. ACM, 1994

## Slide 8: Annex: Flowchart and information exchange
The threshold of the SUs’
number under the channel
state can be calculated to
deal with frequent changes
in the network, such as the
SUs’ accessing or leaving
the network.

## Slide 9: Simulation Result 2: BER performance
IA can significantly improve the BER performance of PU.
When the PU is working, the SU’s performance significantly decreases but QoS can also be ensured by IA.