## Slide 1: Proposed feedback from IEEE 802 on 3GPP LAA CRs
18 Jan 2015
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: IEEE 802 needs to respond to 3GPP’s request for a review of LAA with a variety of coexistence concerns
The LAA channel access procedures of most interest are specified in clause 15 of 3GPP R1-157922
While LAA channel access is similar to 802.11, there are differences that raise coexistence concerns
... on an evaluation of LAA
3GPP RAN has requested IEEE 802 to comment on the LAA CRs
It is likely that IEEE 802 responses to the 3GPP RAN request will be required by early April 2015
IEEE 802 should start the CR review in January 2016, and plan to approve a response in March 2016
IEEE 802 needs to get to work …

## Slide 3: 3GPP RAN has requested IEEE 802 to comment on the LAA CRs
  During the 3GPP LAA Workshop in August 2015, the RAN Chair committed to liaising the LAA CRs to IEEE 802 and Wi-Fi Alliance for comment once they were approved by 3GPP RAN
  3GPP RAN approved the LAA CRs in December, and it sent the following liaison to IEEE 802 and Wi-Fi Alliance in December 2015
    3GPP TSG RAN would like to inform IEEE 802 LMSC and the Wi-Fi Alliance that it has approved the baseline CRs implementing the LAA feature in the 3GPP specs.
    The CRs are provided in the attachment.
    3GPP TSG RAN welcomes any further feedback from IEEE 802 LMSC and the Wi-Fi Alliance on LAA
    Potential corrections should be proposed directly to the relevant WGs (preferably with accompanying documents clearly articulating the motivation for the change).

## Slide 4: It is likely that IEEE 802 responses to the 3GPP RAN request will be required by early April 2015
  During the 3GPP LAA Workshop in August 2015, it was indicated that substantive suggestions for changes to the CRs would need to be made by April 2016, but parameter changes could be made after that date
    Substantive changes were characterised as those that have an impact on LAA implementations’ hardware
  The liaison from 3GPP RAN did not indicate any dates by which submissions are required, but did indicate the dates of upcoming 3GPP meetings as follows:
    RAN1 #84 5-19 Feb 16 Mata, Malta
    RAN #71 7 -10 Mar 16 Goteborg, Sweden
    RAN1 #84bis 11-15 Apr 16 South Korea
    RAN1 #85 23 -27 May 16 China
    RAN #72 13-16 Jun 16 South Korea

## Slide 5: IEEE 802 should start the CR review in January 2016, and plan to approve a response in March 2016
Dec
Jan
Feb
Mar
Apr
RAN1 #84
RAN #71
RAN1 #84bis
802 interim
802 plenary
Start CR review?
Finish CR review?

## Slide 6: The LAA channel access procedures of most interest are specified in clause 15 of 3GPP R1-157922
15 Channel Access Procedures for LAA
  15.1 Downlink Channel Access Procedures
    15.1.1 Channel Access procedure for transmission(s) including PDSCH
    15.1.2 Channel Access procedure for transmissions including discovery signal transmission(s) and not including PDSCH
    15.1.3 Contention Window Adjustment Procedure
    15.1.4 Energy Detection Threshold Adaptation Procedure
    15.1.5 Channel Access procedure for transmission(s) on multiple channels
      15.1.5.1 Type A multi-channel access procedures
      15.1.5.2 Type B multi-channel access procedure
Normal channel access procedures
Special channel access procedures for discovery
CW adjustment procedures
Energy detection procedures
Multi-channel access procedures (two types)

## Slide 7: While LAA channel access is similar to 802.11, there are differences that raise coexistence concerns
LAA uses parameters and structures for downlink traffic similar to those used in 802.11 EDCA
LAA defines a access engine based on collision avoidance similar to 802.11
LAA should be modified to better align its access mechanism with 802.11
LAA must reduce Tmcot,[3,4] to 6ms when the channel may contain other technologies
LAA must specify access at a priority level is only available to same & higher priority traffic
LAA must specify limits to the special DRS access mechanism
LAA must not transmit energy solely to stop other systems from accessing the channel
IEEE 802 would appreciate a justification & explanation of the selection of the value of Z
LAA should be modified to align it better with 802.11 EDCA for Ninit = 0
LAA should be modified to align it better with 802.11 EDCA wrt wrt the defer period
LAA should be modified to avoid “head-of-line-blocking”
… but IEEE 802 has some high priority concerns related to differences
LAA define a similar access engine to 802.11 in many respects
… and lower priority requests

## Slide 8: LAA uses parameters and structures for downlink traffic similar to those used in 802.11 EDCA
  The LAA defer period (Td) is similar to 802.11 AIFS
  The LAA slot period (Ts) is the same length (9us) as a 802.11 slot
    An LAA slot also has a similar internal structure to an 802.11 slot, allowing at least 4us for energy detection
  The initial part (Tf) of the LAA defer period is the same length (16us) as 802.11 SIFS
    The internal structure of LAA’s Tf is slightly different to 802.11 because it includes a slot at the start of the period
  Each of LAA four priority levels are defined using similar access parameters and similar default values as 802.11 EDCA APs
    The number of slots in a defer period after Tf is mp
    CWp is used with a min of CWmin,p & max of CWmax,p
    CWp is doubled when a collision is detected
    Tmcot,p is the maximum transmission time (different values from 802.11)

## Slide 9: LAA defines a access engine based on collision avoidance similar to 802.11
LAA defines a basic access method for an eNB to access the channel for downlink traffic with priority level of p
  set N = Ninit, where Nint is a random number uniformly distributed between 0 and CWp ;
  if N>0 and the eNB chooses to decrement the counter, set N=N-1;
  sense the channel for an additional slot duration, and if the additional slot duration is idle, go to step 4; else, go to step 5;
  if N=0, stop; else, go to step 2.
  sense the channel during the slot durations of an additional defer duration Td ;
  if the channel is sensed to be idle during the slot durations of the additional defer duration Td , go to step 2; else, go to step 5;

## Slide 10: Suggestion: LAA should be modified to align it better with 802.11 EDCA for Ninit = 0
Observation by IEEE 802
  Suppose Ninit = 0 for a particular access LAA attempt, and CW is randomly chosen to be 0 in 802.11
  In 802.11 EDCA, the channel will be accessed after SIFS + 3 slots (or 43us) for normal priority traffic
  In LAA, the channel will be accessed after Tf + (mp + 1) x Tsl (or 16 us + 4 slots = 52 us for equivalent priority 3 traffic)
    Step 3) in the LAA algorithm is the source of the extra slot
  Note: this issue has no adverse effect on 802.11, but does have a minor adverse affect on LAA access
Low priority suggestion to 3GPP RAN
  IEEE 802 suggests 3GPP modify LAA to align its access mechanism better with that of 802.11 EDCA

## Slide 11: Suggestion: LAA should be modified to align it better with 802.11 EDCA wrt the defer period
Observation by IEEE 802
  In LAA, if a countdown is interrupted by a transmission, the access algorithm samples the medium in quantum's of Td
  This means that LAA could take up extra 43 us deferring (when p = 3) compared to 802.11 before it resumes its countdown
  Note: this issue it has no adverse effect on 802.11, but does have a minor adverse affect on LAA access
Low priority suggestion to 3GPP RAN
  IEEE 802 suggests 3GPP modify LAA to align its access mechanism better with that of 802.11 EDCA wrt the defer period

## Slide 12: Suggestion: LAA should be modified to avoid “head-of-line-blocking”
Observation by IEEE 802
  LAA appears to only define the use of a single access engine rather than an access engine per priority level
  Given no alternative is described, it also appears that the access engine cannot be interrupted while access is being sought for a particular priority sub-frame
  The affect is that LAA will suffer from “head-of-line-blocking”
    “Head-of-line-blocking” is when a low priority sub-frame taking significant period to access the channel blocks a high priority sub-frame in the same device
  Note: this issue has no adverse effect on 802.11, but does on LAA
Low priority suggestion to 3GPP RAN
  IEEE 802 suggests 3GPP modify LAA to avoid “head-of-line blocking”, possibly by using 802.11’s multi-engine priority access mechanism

## Slide 13: Request: LAA should be modified to better align its access mechanism with 802.11
Observation by IEEE 802
  The LAA spec defines a back off mechanism in clause 15.1.1
  However, it is ambiguous as to when the back off procedure is executed
  One interpretation of the text is that a back off occurs when a frame is queued for transmission
  In this case, LAA will have a disadvantage compared 802.11 because an 802.11 system can transmit on the next slot boundary as long as the medium is free after a previous post transmission back off
  A second interpretation is that LAA will perform a post transmission back off, similar to 802.11
  A variety of more serious issues arise under this second interpretation when a LAA sub-frame is queued for transmission
  …

## Slide 14: Request: LAA should be modified to better align its access mechanism with 802.11
  …
  In this case, LAA specifies that transmission can start after sensing the channel is idle during all the slots in an additional defer period, Td
  This results in a variety of issues
    Issue 1 (minor): transmission will not occur on a slot boundary, converting a slotted ALOHA style system into a less efficient ALOHA style system
    Issue 2 (minor): the defer period in LAA is unnecessarily long, noting that 802.11 will transmit on the next slot boundary (<9+4 us in practice), whereas LAA will be delayed by Td (43us for p=3)
    Issue 3 (major): the spec states that LAA can transmit after finding the channel to be free for a defer period, and suggests that it can keep searching for a defer period; alignment with 802.11 requires a full back off if the channel is determined not to be free when a frame is queued; this gives LAA a significant advantage over 802.11
  …

## Slide 15: Request: LAA should be modified to better align its access mechanism with 802.11
  …
High priority request to 3GPP RAN
  IEEE 802 requests 3GPP modify LAA to:
    Make it clearer that that a post transmission back off is required after every transmission
    Specify that an LAA system can transmit immediately on any slot boundary after the post transmission back off, unless the channel is not free or is in a defer period; in these latter cases, LAA must specify the execution of a new back off procedure
  The bottom line is that 3GPP must align the LAA access engine better with that of 802.11 to minimise any possibility of coexistence issues

## Slide 16: Request: LAA must reduce Tmcot,[3,4] to 6ms when the channel may contain other technologies
Observation by IEEE 802
  In LAA, Tmcot,p is 8ms for the typical priority level (p = 3) when the channel may contain non LAA technologies
  The vast majority of 3GPP reported in TR XXX were undertaken using a Tmcot,p of 4ms
  At least some of few simulations using a higher Tmcot,p showed an adverse affect on LAA/802.11 coexistence, particularly with 802.11 voice
  At least one regulator at ETSI BRAN expressed particular concern for competition reasons about any possibility of LTE based systems adversely affecting 802.11 voice
  …

## Slide 17: Request: LAA must reduce Tmcot,[3,4] to 6ms when the channel may contain other technologies
  …
High priority request to 3GPP RAN
  IEEE 802 requests 3GPP reduce the Tmcot,[3,4] in LAA to 6ms whenever the channel may contain non LAA technologies, until there is future consensus between IEEE 802, 3GPP RAN and other stakeholders that higher values have no adverse affect on 802.11/LAA coexistence (particularly voice)
  This request only applies to LAA downlink traffic from the eNB; there are ongoing productive discussions in 3GPP and ETSI BRAN about various Tmcot,p mechanisms for uplink traffic grants

## Slide 18: Request: LAA must specify access at a priority level is only available to same & higher priority traffic
Observation by IEEE 802
  In 802.11, a TxOP gained using particular priority level parameters can only be used to transmit frames of that priority or higher priorities
  In contrast, the LAA spec does not appear to define how traffic from multiple priorities are multiplexed in the same transmission
  Documents made available to ETSI BRAN suggest that LAA will allow lower priority traffic to fill the remainder of a sub-frame if all higher priority traffic has been transmitted
  The argument was made during ETSI BRAN discussions on this topic was that the LAA sub-frame is of fixed length and it is better to fill the remainder of the LAA sub-frame with something rather than waste it
  …

## Slide 19: Request: LAA must specify access at a priority level is only available to same & higher priority traffic
  …
  The counter argument is that the LAA sub-frame should use lower priority access parameters if it carries any lower priority traffic
High priority request to 3GPP RAN
  IEEE 802 requests 3GPP specify immediately in LAA that access using parameters for a particular priority level is available to traffic for that priority level and higher priority levels, but not lower priority levels
    3GPP may want to consider solving this problem by allowing LAA sub-frames to complete early if there is not sufficient traffic to fill the entire sub-frame
    Alternatively, LAA could be defined to use the access parameters corresponding to the lowest priority traffic in the sub-frames
  IEEE 802 requests 3GPP that the specification of how traffic from multiple priorities are multiplexed in the same transmission be defined in the MAC specification (TS 36321)

## Slide 20: Request: LAA must specify limits to the special DRS access mechanism
Observation by IEEE 802
  LAA specifies that a Discovery Reference Signal (without PDSCH) may be transmitted after sensing the medium is free for 25us, using an ED Threshold of 5 dB less than normal
    This approach recognises the high importance of DRS signals in LTE
  This specification should have limited adverse affect on 802.11/LAA coexistence if the DRS is transmitted, as expected by many, every 40/80/160ms
  However, it is also possible for an eNB to configure different DRS offsets for different UEs
  Hence, while each UE may be getting the DRS at a very low rate, the eNB may, in reality, be transmitting DRS more often than once every 40 ms/80ms/160ms
  …

## Slide 21: Request: LAA must specify limits to the special DRS access mechanism
  …
  In this case, 802.11/LAA coexistence is much more likely to be adversely affected
High priority questions and request to 3GPP RAN
  IEEE 802 requests responses from 3GPP RAN to the following questions:
    Are all served UEs are expected to be configured with identical DRS offset?
    How often is an eNB expected to transmit a DRS?
  IEEE 802 also requests that the LAA be modified to include reasonable limits to the how often the channel may be accessed using the DRS mechanism
    IEEE 802 would be happy to discuss appropriate limits with 3GPP RAN

## Slide 22: Request: LAA must not transmit energy solely to stop other systems from accessing the channel
Observation by IEEE 802
  In LAA, there is delay of 0-1 ms between gaining access to the channel and the start of the sub-frame, which is a result of LAA sub-frames always being aligned to 1 ms boundaries
    The delay is 0.5 ms if partial sub-frames are used
  The only way for the LAA system to stop another system from accessing the channel during this delay is to transmit energy on the channel
  This energy represents a form of interference because its sole purpose is to stop other systems from accessing the channel
  As noted during the IEEE 802 submission to the 3GPP LAA Workshop, such interference is contrary to the well accept principle of unlicensed spectrum to not cause unnecessary interference to others
  …

## Slide 23: Request: LAA must not transmit energy solely to stop other systems from accessing the channel
  …
  Such interference is also probably against the rules for unlicensed spectrum in many regulatory domains; such a rule is currently under discussion in ETSI BRAN
High priority request to 3GPP RAN
  IEEE 802 requests that LAA be modified so that LAA never sends energy to solely to stop other systems accessing the channel; any transmission must have legitimate data or management purposes
  Options to satisfy this request include:
    Allowing (partial) sub-frames to start immediately after channel access
    Deferring sending energy in a channel until the LAA device is ready to transmit
    …

## Slide 24: Request: IEEE 802 would appreciate a justification & explanation of the selection of the value of Z
Observation by IEEE 802
  In clause 15.1.3, it is specified that LAA increases all CWp values when 80% of acknowledgements (Z) are NACKs
    Note: the details of the calculation of this percentage are not well understood by many IEEE 802 participants because of use of LTE specific terminology
  This percentage seems to be very high, and the justification is unclear
    A high percentage means that collisions at many UEs will be ignored and thus those UEs and their neighbours will not benefit from the LAA back off mechanisms
High priority request to 3GPP RAN
  IEEE 802 requests that 3GPP explain and justify the selection of the value of Z, and particularly why this value does not have an adverse affect on 802.11 devices

## Slide 25: Multi-channel
<an analysis of multi-channel will be added here>