## Slide 1: Proposal on proxy coexistence service for moving WSO
Date: 2016-01-20
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
This document proposes proxy coexistence service for moving WSO as a new functionality of coexistence manager.

## Slide 3: Background
As one of deployment scenarios, we can assume the scenario that:
  One CM manages one specific geographic region; and
  WSO (White Space Object) with CE (Coexistence Enabler) has mobility.
In such a scenario, issue will be occurred at border.
  WSO needs to change its serving CM (CM A) to the other CM (CM B) when the WSO moves across the region.

## Slide 4: Background (graphic)
CM B for region B
(Destination CM)
CM A for region A
(Source CM)
Region A
Region B
WSO w/ CE
WSO w/ CE

## Slide 5: Problem
Moving WSO (w/ CE) might be unable to be served coexistence service by the CM of the destination region.
  [Reason]
  There are no CM discovery and association as CE operation specified in the existing standard.
    This issue has been already raised in the other submission of mine. (19-16/0015r0)
  Frequent change of coexistence set information
    Dynamic spectrum environment around moving WSO (w/ CE) at “high speed”.
    Especially, management service is difficult to be provided.
  Destination CM Capacity for managing WSO (w/ CE)
    Destination CM cannot always start serving new entrant CE and WSO due to its capacity limitation.
Both should be solved

## Slide 6: Solution
Proxy coexistence service
  Source CM provides coexistence service to CE on behalf of destination CM.
CM B for region B
(Destination CM)
CM A for region A
(Source CM)
Region A
Region B
WSO w/ CE
Coexistence set information in region B
Coexistence set information in region B
In a normal situation, destination CM has to serve the CE and WSO moving in region B.
Move
Source CM provides coexistence service to moving WSO after retrieving coexistence set information from destination CM.

## Slide 7: Things to be defined
For information service
  Region-specific coexistence set information
    Current standard includes only the location-specific information.
    Especially for moving WSO at high speed, overhead will be reduced.
For management service
  Nothing special
    Basically, Annex D.4 (informative), where management service for moving WSO is introduced, will be utilized.
For both services
  CM discovery and association as CE operation
    See another submission 19-16/0015r0.
  Procedure for starting proxy coexistence service as CE and/or CM operation

## Slide 8: Next step
To prepare text proposal.

## Slide 9: Reference
[1] IEEE Standard Association, “IEEE Std 802.19.1-2014“, July 2014