## Slide 1: Automotive WLAN Interference Evaluation Criteria Proposal
Date: 2016-02-09
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
In this presentation a proposal for single vehicle WiFi and BT performance tests is presented
For each test a set of high level as well as lower level parameters are proposed to be measured
A proposal for the above mentioned single vehicle scenario extension to a multi vehicle scenario is also presented

## Slide 3: Testing Scenarios – A Single Vehicle
These results will be used for evaluating:
  Self interference
  Interference inflicted by the surrounding vehicles / residential / enterprise WiFi infrastructure

## Slide 4: Testing Scenarios – A Single Vehicle Cntd.
Scenario index | Num. of APs | Num. of STAs connected to each AP | Bluetooth link present | WiFi Channel number (s) | Traffic type | Comments
A | 2 | #1: 1 #2: 1 | N | Non overlapping channels | #1: Phone mirroring #2: File download | Set link mode?
B | 2 | #1: 1 #2: 1 | Y | Non overlapping channels | #1: Phone mirroring #2: File download | 
C | 2 | #1: 1 #2: 4 | Y | Same channel | #1: Phone mirroring #2: File download | Wifi self interference
D | 3 | #1: 1 #2: 4 #3: 2 | Y | 1, 6, 11 | #1: Phone mirroring #2: File download #3: YouTube stream | Wifi interferes with BT
E | 2 | #1: 2 #2: 4 | Y | Same channel | #1: File download #2: File download | AP #1 with 30dB reduced power Interference from infrastructure

## Slide 5: Testing Scenarios – Multiple Vehicles
Assumptions:
  Lane width is about 3m
  Distance between tailing vehicles is about 3m
  At least 3 adjacent lanes exist
  The vehicle with the ‘X’ is the vehicle under test and the links inside this vehicle are the primary links
  Each / all vehicles 1-8 can inflict interference on vehicle ‘X’

## Slide 6: Testing Scenarios – Multiple Vehicles Cntd.
Multi vehicle scenarios can be constructed by pairing a single vehicle scenario with the desired vehicle(s)
The primary links of the ‘X’ vehicle are tested

## Slide 7: High Level Performance Indicators
The following characteristics can be measured on the primary link(s):
  Maximal achievable throughput
  Packet error rate
  Packet jitter
  Latency

## Slide 8: Lower Level Performance Indicators
The following parameters can be measured on the primary link(s):
  RSSI
  SNR / SINR
  Transmission mode

## Slide 9: Additional Proposed Measurements
In order to better understand the nature of the interference and to be able to reconstruct it in simulation, it is suggested that a channel model for inter-vehicle interference is developed