## Slide 1: Global Availability of 5GHz Spectrum for Automotive Use
Date: 2016-05-06
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Summary of 5GHz spectrum availability around the world for automotive use cases, which are typically considered outdoor.

## Slide 3: Background
5GHz is important for automotive applications
  Provides adequate bandwidth for automotive use cases
  Less congested
  Doesn‘t interfere with Bluetooth, which is important for hands-free calling in vehicles
Global regulations are not harmonized
  Makes product certification complex (homologation)
  Some bands are indoor only in certain countries
  Automotive use is typically considered outdoor
DFS is difficult in automobiles
  Radar detection was developed with fixed access points in mind
  DFS bands not reliably available for vehicular use

## Slide 4: Spectrum at a glance
US
Europe Japan
China
SRD
DFS

## Slide 5: 5GHz spectrum (1/2)
CHANNEL NUMBER | FREQUENCY MHZ | EUROPE (ETSI) | NORTH AMERICA (FCC) | JAPAN | China
36 | 5180 | Indoors | ✔ | Indoors | ✔
40 | 5200 | Indoors | ✔ | Indoors | ✔
44 | 5220 | Indoors | ✔ | Indoors | ✔
48 | 5240 | Indoors | ✔ | Indoors | ✔
52 | 5260 | Indoors / DFS / TPC | DFS | DFS / TPC | DFS / TPC
56 | 5280 | Indoors / DFS / TPC | DFS | DFS / TPC | DFS / TPC
60 | 5300 | Indoors / DFS / TPC | DFS | DFS / TPC | DFS / TPC
64 | 5320 | Indoors / DFS / TPC | DFS | DFS / TPC | DFS / TPC
100 | 5500 | DFS / TPC | DFS | DFS / TPC | No Access
104 | 5520 | DFS / TPC | DFS | DFS / TPC | No Access
108 | 5540 | DFS / TPC | DFS | DFS / TPC | No Access
112 | 5560 | DFS / TPC | DFS | DFS / TPC | No Access
116 | 5580 | DFS / TPC | DFS | DFS / TPC | No Access

## Slide 6: 5GHz spectrum (1/2)
120 | 5600 | DFS / TPC | No Access | DFS / TPC | No Access
124 | 5620 | DFS / TPC | No Access | DFS / TPC | No Access
128 | 5640 | DFS / TPC | No Access | DFS / TPC | No Access
132 | 5660 | DFS / TPC | DFS | DFS / TPC | No Access
136 | 5680 | DFS / TPC | DFS | DFS / TPC | No Access
140 | 5700 | DFS / TPC | DFS | DFS / TPC | No Access
149 | 5745 | SRD | ✔ | No Access | ✔
153 | 5765 | SRD | ✔ | No Access | ✔
157 | 5785 | SRD | ✔ | No Access | ✔
161 | 5805 | SRD | ✔ | No Access | ✔
165 | 5825 | SRD | ✔ | No Access | ✔
CHANNEL NUMBER | FREQUENCY MHZ | EUROPE (ETSI) | NORTH AMERICA (FCC) | JAPAN | China

## Slide 7: Notes
Note 1: there are additional regional variations for countries including Australia, Brazil, China, Israel, Korea, Singapore, South Africa, Turkey, etc. Additionally Japan has access to at least one channel below 5180 MHz.
Note 2: DFS = Dynamic Frequency Selection; TPC = Transmit Power Control; SRD = Short Range Devices, 25 mW (+14dBm) max power.
Note 3: Chinese regulations from https://mentor.ieee.org/802.11/dcn/13/11-13-0329-01-00ac-updated-china-s-5ghz-spectrum-regulation.ppt

## Slide 8: Summary
No 5GHz spectrum is currently available for automotive use in Japan (without DFS)
  Regulations are under review
  New proposals may come to light later in 2016 – but may not help WLAN in cars
Europe only allows operation in 5.725-5.850 under the Short Range Device rules (25mW = 14dBm)
  This is adequate for most in-vehicle applications
  Not all mobile phones support this band
Changes to regulations will almost certainly happen going into WRC-19