## Slide 1: In-Vehicle Wireless Interference
Date: 2016-07-05
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
As the number of wireless services deployed within the typical passenger vehicle increases over time, the vehicle OEM, the various system integrators and operators must ensure that the RF environment and a wide variety of potential interference mechanisms are accounted for.
Ensuring harmonious coexistence of both licensed and unlicensed wireless services in and around the vehicle environment is a problem that is becoming more and more complex, with both greater ISM band utilization within the vehicle, near road equipment deployment, as well as further infrastructural and in-vehicle deployment of licensed wireless services.
A number potential interactions amongst these wireless services exist, some of which are outlined and discussed in this presentation.

## Slide 3: In-Vehicle Wireless Services
Unlicensed:
  Service: Frequency band(s):
  Bluetooth 2.4GHz
  Wi-Fi 2.4, 5.8GHz
  802.11 / WLAN 2.4, 5.8GHz
Licensed:
  Service: Frequency band(s):
  GNSS 1.2 to 1.6GHz
  SDARS 2.3GHz
  Cellular Various, from 700MHz, to 2.6GHz (future: 2.3, 3.5GHz?)
  Future: DSRC / V2X 5.9GHz
  Future: 802.11y 3.7GHz?

## Slide 4: Interference Mechanisms
Unlicensed  Unlicensed Service (current coverage by 802.19):
  Simultaneous channel usage (in-band interference)
  Adjacent channel de-sense (OOB spurious emissions)
  Intermodulation, e.g.:
    3rd order products of 2.4GHz and 5.8GHz ISM  900MHz ISM
Unlicensed  Licensed Service:
  Adjacent channel de-sense (OOB spurious emissions)
  Intermodulation, e.g.:
    3rd order products of 2.4GHz ISM  SDARS
    5th order products of 900 and 2.4GHz ISM  AWS D/L Cellular

## Slide 5: Interference Mechanisms (cont’d)
Licensed  Licensed Service:
  Adjacent channel de-sense (OOB spurious emissions), e.g.
    WCS band cellular  SDARS
  Intermodulation, e.g.:
    3rd order products of PCS and AWS D/L cellular  SDARS and GPS
  Bulk De-sense, e.g.:
    Overload of SDARS receiver antenna LNA from co-packaged cellular TX

## Slide 6: Interference Mechanisms (cont’d 2)
Others:
  Wi-Fi devices (noncompliant spectral OOB spectral emissions)
    Brought-in and non-vehicle (installed on street lights, etc.)
  Proximity and device level interaction
    De-sense at device  vehicle module level
    Digital device / chip clocks and switching power supply interactions

## Slide 7: Observations from 15 years of deployed SDARS service
AWS+PCS cellular intermodulation products into SDARS, GPS, and other bands
Overload of SDARS receiver antenna LNA from co-packaged cellular TX
  Interference behavior linked to, in-vehicle Wi-Fi use (cellular enabled)
Adjacent channel de-sense of SDARS service from WCS
  Coordination effort to reduce with carriers
Observed issues necessitated changes to the Sirius XM SDARS receiver antenna specifications over time. However, lifecycle differences between the vehicular and cellular domains make it challenging to create an efficient co-existence environment.

## Slide 8: Future Challenges, as SXM sees it, in priority order:
  Further proliferation of cellular networks and vehicular use cases may create additional intermodulation modes
  Proximity and device level interaction – driven by complexity
  Digital device / chip clocks and switching power supply interactions
  External vehicle Wi-Fi (co-packaged)  SDARS and GPS

## Slide 9: Discussion of Service Availability
Depending on the service use case and specifics, availability requirements can drive perceived interference mechanism severity, e.g.:
  Unlike cellular, WLAN / Wi-Fi, GPS, and non-real time, redundant delivery, or low data rate examples, SDARS requires 99%+ service availability to retain customer satisfaction at current levels, therefore additional threats are proactively investigated (since the service is less tolerating to service interruptions / audio mutes)
  Similar scenarios may exist for streaming data over Bluetooth or WLAN in the vehicle in the future