## Slide 1: CID 161 resolution Spectrum management of GCOs with different priority levels
Date: 2016-09-11
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:

## Slide 2: Abstract
This document proposes frequency allocation of systems with different priority levels

## Slide 3: Motivation/Introduction
In the multi-priority network architecture, the spectrum allocation of high-priority GCO directly affect the available spectrum left to the low-priority GCO.
In literature, the existing spectrum allocation algorithms for high-priority GCO did not consider the low-priority GCOs.
Spectrum allocation by individual CM results in:
  Co-channel interference between GCOs managed by different CMs
  Low spectrum efficiency
3

## Slide 4: System Model
4
Interference set includes the high-priority GCO (secondary system) which generates harmful interference to the low-priority GCO or gets interfered by the low-priority GCO.

## Slide 5: Formulated Problem
How to optimize the spectrum allocation for high-priority GCOs to increase the available spectrum of low-priority GCOs?
5
The available spectrum of the mth low-priority GCO (Am) is defined by:
Note: is the interference set corresponding to
the mth low-priority GCO;
is the number of total available channels
for high-priority and low-priority GCOs;
is the number of channels occupied by
high-priority GCOs in the interference set.
To avoid harmful interference to the primary system, secondary system (GCO) and primary system (PS) use different spectrum.

## Slide 6: Proposed Initial Solution/Algorithm
Interference set-based clustering and spectrum allocation
Increasing the available spectrum of low-priority GCOs can be converted to reduce the number of channels occupied by high-priority GCOs in the interference set
The number of clusters is equal to the number of channels
6
Note: is the interference set corresponding to the mth low-priority GCO is the number of clusters corresponding to the mth interference set
represent whether the ith and jth high-priority GCOs are co-channel

## Slide 7: List of Parameters
Parameters | Notation
 | Interference set corresponding to the mth low-priority GCO
 | Cluster corresponding to the mth interference set
 | Number of clusters corresponding to the mth interference set
 | Transmit power of the ith high-priority GCO
 | Transmit power of the mth low-priority GCO
 | Maximum transmit power of the high-priority GCO
 | Maximum transmit power of the low-priority GCO
 | Euclidean distance between the jth GCOtransmitter and the ith GCOreceiver
 | Euclidean distance between the ith GCOtransmitter and its desired receiver
 | Path loss exponent
 | Number of high-priority GCOs
 | Number of low-priority GCOs
 | SINR threshold of the ith high-priority GCO receiver
 | : the ith and jth GCOs are co-channel : the ith and jth GCOs are not co-channel
7

## Slide 8: Block Diagram of Proposed Solution/Algorithm
8
In p#5, GCOs that can use the same channels are packed into the same cluster as long as the SINR requirement is guaranteed.

## Slide 9: Procedure of Clustering
9
Interference Graph-based clustering
wij : the received relative interference of ith GCO from the jth GCO
wi : the received relative interference of ith GCO from other GCOs in the cluster
Note: Cs is the collection of high-priority GCOs in the sth cluster
Form an directed interference graph
G=(V, E, W)
V: Collections of high-priority GCOs
E: Collections of the edge between two GCOs
(two directed edge between any two vertex)
W: Collections of the weight (i.e., wij) in each edge
Please add high level information of “what is clustering”

## Slide 10: Simulation Scenario
10
Multiple GCOs with different priority coexist, and at a given time in each system there is only one pair of users.
The radius of each GCO is 20 m.
The transmitter is located at the center while the receiver is at the cell edge.
Low-priority GCOs are fixed, and high-priority GCOs are uniformly random distribution.

## Slide 11
Simulation Settings
Parameters | Value
Number of high-priority GCOs | 8
Number of low-priority GCOs | 1
SINR threshold (SINRth) | 15 dB
Transmit power | 0 dBm
Path loss exponent | 3
Number of the available channels | 5
11

## Slide 12
Objective of Simulation
To show our method can increase the available spectrum of the low-priority GCO
To show our method can ensure QoS requirements (e.g. SINR) of high-priority GCOs
12

## Slide 13
Simulation of Interference Set
Interference set and non-interference set
Blue: low-priority GCO
Red: high-priority GCOs
(i.e., interference set GCOs)
Black: high-priority GCOs
(i.e., non-interference GCOs)
13
Interference set GCOs mean high-priority GCOs which generate harmful interference to the
low-priority GCO or get interfered by the low-priority GCO.

## Slide 14
Simulation of Clustering (1/2)
The clustering results of proposed clustering procedure without considering interference set
= 3
Blue: Low-priority GCO
Yellow: Cluster 1
Magenta: Cluster 2
Green: Cluster 3
14
Interference set GCOs
Note: is the interference set
is the number of clusters corresponding to the interference GCOs within the
proposed approach without considering interference set

## Slide 15
The clustering results of
proposed clustering procedure considering interference set
= 2
Blue: Low-priority GCO
Yellow: Cluster 1
Magenta: Cluster 2
Green: Cluster 3
15
Interference set GCOs
Conclusion: the proposed clustering procedure considering the interference set results in more available channels for the low-priority GCO
Simulation of Clustering (2/2)
Note: is the number of clusters corresponding to the interference GCOs within
the proposed approach without considering interference set

## Slide 16
Events | Using Proposed Clustering Procedure without interference set | Using Proposed Clustering Procedure with interference set
The percentage of trial that two methods win over the sequential coloring approach [11] | 83.7% | 99%
Change the locations of the 8 high-priority GCOs (500 simulation runs), and get the probability of several events
Conclusion: The number of clusters can be reduced with the proposed clustering
procedure considering interference set (as compared to that without
considering interference set )
Simulation results (2/2)
16
[11] Q. Zhang, X. Zhu, L. Wu, and K. Sandrasegaran, “A Coloring-based Resource Allocation for OFDMA Femtocell Networks,” IEEE Wireless Communications and Networking Conference (WCNC), 2013, pp. 673-678.

## Slide 17
change the locations of the 8 GCOs (1000 simulation runs), and get the CDF of number of clusters corresponding to the interference GCOs.
Simulation of Clustering (CDF)
Conclusion: the proposed clustering procedure considering interference set shows
better performance in reducing the number of clusters corresponding to the
interference GCOs.
17

## Slide 18: Conclusion
Propose an resource allocation method for GCOs with different priority levels in order to make the spectrum allocation for high-priority GCOs so that the available frequency of low-priority GCOs is increased.
Form the cluster for the high-priority GCOs belong to the interference set firstly, then form the cluster for the high-priority GCOs not belong to the interference set.
Propose the clustering procedure about the principle of selecting the first cluster member and other cluster members. Each cluster uses the same frequency
Allocate the spectrum to high-priority GCOs based on the results of clustering. Determine the available spectrum for low-priority GCOs based on the interference set and results of clustering.
18