## Slide 1: Supplemental Document for Comment Resolution on CID89 in 1st TG Review
Date: 2016-11-08
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
This document provides supplemental information for comment resolution on CID89 in 1st TG review [1].
Basically, the concept of aggregated interference margin MI is introduced in this document.
Added calculation methodology of aggregated interference margin MI.
  Based on the number of GCO
Two types of MI are provided.
  Fixed/Predetermined margin
  Flexible margin
Comment ID | Page No. | Section | Line No. | Type (General, Editorial, Technical) | Comments | Proposed changes | Resolutions
89 | 79 | 7.2.2.9.4.1 | 15 | Technical | Calculation of MI is not specified.Should provide how to calculate. | Need proposal | wait for contributions

## Slide 3: Common concept: Maximally allowed interference level can be allocated equally to the interfering GCO.
Prioritized GCO
(Master)
Prioritized GCO
(Slave)
Target GCO
Imax-allowed
Path loss
Path loss
Path loss
Imax-allowed / 2
Imax-allowed / 2
EIRP is calculated to meet the maximally allowed interference level of receiver at the edge of service area of the prioritized GCO with considering path loss
EIRP of each GCO is calculated to meet the equally- allocated and maximally-allowed interference level of receiver at the edge of service area of the prioritized GCO with considering path loss
Target GCO
Target GCO

## Slide 4: Two types of MI
Fixed/Predetermined margin
  Based on the predetermined assumption on the maximum number of target GCOs operating simultaneously
Flexible margin
  Actual number of active target GCOs operating on the same channel as the prioritized GCO
    Case of co-channel operation only
      Just counting the number of active target GCOs operating on co-channel.
    Case of partially-overlapped spectrum operation
      At first, target GCO shall be considered as the “one” co-channel interferer, where the interference by that GCO is assumed to be Ico-channel.
      Second, actual interference level of the target GCO shall be calculated as Ipartially-overlapped.
      Then, the ratio of Ipartially-overlapped to Ico-channel (equivalent to ACIR: adjacent channel interference ratio) can be seen as the substantial number of that target GCO.
      Summation of all the target GCOs’ Ipartially-overlapped /Ico-channel (= ACIR) values can be seen as the actual number of active target GCOs operating on the same channel as the prioritized GCO.

## Slide 5: Interference cases to be considered in calculating ACIR

## Slide 6: Reference
[1] Sho Furuichi, “IEEE 802.19-16/0173r0 Comment resolution on CID89 in 1st TG review”, Nov 2016