## Slide 1: Interference Mitigation for Coexisting 802.15.4g and 802.11ah Networks
Date: 2018-05-08
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Presentation to Sub-1 GHz (S1G) Band Coexistence Interest Group of the IEEE 802.19 Working Group on Interference Mitigation for Coexisting IEEE 802.15.4g and IEEE 802.11ah networks.

## Slide 3: Background
Sub-1 GHz (S1G) band coexistence
  Deployed 802.15.4g based smart utility devices operate in the S1G band
  802.11ah, LoRa and SigFox are also designed to operate in the S1G band
  Ensure harmonious coexistence of these heterogeneous devices is crucial, especially normal function of the already deployed devices
Issue
  Spectrum allocation in S1G band is limited
  Channel hopping can be restricted
  Simulations show that 802.11ah and 802.15.4g can interfere with each other
    802.15-17/0522r2
    802.19-17/0087r3
    802.19-18/0006r1
    802.19-18/0016r1
This presentation addresses interference mitigation by providing coexistence solutions for 802.11ah

## Slide 4: Coexistence Mechanisms of 802.15.4g and 802.11ah
802.15.4g coexistence mechanism
  Define three PHY types
    MR-FSK
    MR-OFDM
    MR-O-QPSK
  Define common signaling mode (CSM) for coexistence between devices using different 802.15.4g PHYs
802.11ah S1G coexistence with non-IEEE-802.11 systems
  An S1G STA uses energy detection (ED) based CCA with a threshold of -75 dBm per MHz to improve coexistence with other S1G systems including 802.15.4 and 802.15.4g
  If a S1G STA detects energy above that threshold on its channel, then the following mechanisms might be used to mitigate interference
    Change of operating channel
    Sectorized beamforming
    Change the schedule of restricted access windows (RAW), target wake time (TWT) service periods, or subchannel selective transmission (SST) operating channels
    Defer transmission for a particular interval

## Slide 5: 802.15.4g Packet Loss Caused by 802.11ah Interference
Collision caused by the higher ED threshold of 802.11ah
Collision caused by the faster backoff of 802.11ah
  802.11ah device may start packet transmission when 802.15.4g device performs CCA-to-TX turnaround, which causes data packet collision
  802.11ah device may start packet transmission when 802.15.4g device is waiting for ACK packet, which causes ACK packet collision
Access failure caused by 802.11ah packet transmission
For example for 62.5 ksymbols/s

## Slide 6: Mitigate Interference by Higher ED Threshold of 802.11ah
If the energy level detected by 802.11ah falls in [802.15.4g Receiver Sensitivity, 802.11ah ED Threshold]
  Should 802.11ah ED-CCA report idle or busy?
    From 802.15.4g perspective, it should report busy if the energy source is 802.15.4g and reports idle otherwise
  Problem is that 802.11ah may not be able to identify the source of the energy, which could be
    802.15.4g system, far away 802.11 system and other systems
Proposed solution: α-Fairness based ED-CCA
  The α-fairness is a technique proposed for network resource sharing
  Apply this technique to wireless medium sharing between 802.11ah and 802.15.4g
    If the detected energy level is outside of [802.15.4g Receiver Sensitivity, 802.11ah ED Threshold], 802.11ah ED-CCA reports channel status as specified by 802.11ah
    Otherwise, apply probabilistic ED-CCA approach, i.e., 802.11ah ED-CCA reports channel status based on a probability generate by the α-fairness technique

## Slide 7: α-Fairness ED-CCA
Define a generalized α-Fairness utility function
where α > 0, α ≠ 1, is fairness parameter to favor 802.11ah or 802.15.4g
Pi ≥ 0 is the probability of 802.11ah ED-CCA reports channel idle
Pb ≥ 0 is the probability of 802.11ah ED-CCA reports channel busy
Mh ≥ 0 is the locally observed metric of 802.11ah network
Mg ≥ 0 is the locally observed metric of 802.15.4g network
Network metric can be packet transmission rate, packet delivery rate, etc.
α-fairness wireless medium sharing corresponds to the maximization of objective function U(Pi, Pb) subject to

## Slide 8: α-Fairness ED-CCA
According optimization theory, the above optimization problem has a unique solution as
Pi* distribution for α > 1
  where β = Mh/Mg
Observation
  If α > 1, more medium access opportunity is given the network with the smaller metric
  If α < 1, more medium access opportunity is given the network with the larger metric

## Slide 9: Mitigate Interference by Faster Backoff of 802.11ah
Issue to be addressed
  When backoff counter (BC) reaches to 0 and 802.11ah ED-CCA reports idle channel, should 802.11ah transmit or not?
Problem
  802.11ah does not know if an 802.15.4g transmission procedure is in progress
  In addition, is the channel really idle?
Proposed solution: Q-Learning based backoff for 802.11ah
  Q-learning is a reinforcement learning technique to learn the optimal action selection to maximize the accumulated reward
Q-Learning based backoff
    If BC > 0 or ED-CCA reports busy channel, the backoff process continues as specified by 802.11ah
    If BC = 0 and ED-CCA reports idle channel, apply Q-Learning to make decision, i.e, transmit or re-backoff

## Slide 10: Q-Learning Backoff
Q-Learning is formulated as
where is Q-Learning objective function
is the state reached from state s when performing action a
is action set can be taken at state
is the learning rate,
γ is the discount factor, 0 < γ < 1
Rt(s, a) is the reward obtained by performing action a at state s at time t
Define state set S as
𝑆= {𝑠1, 𝑠2 }= {𝐶ℎ𝑎𝑛𝑛𝑒𝑙 𝐼𝑑𝑙𝑒, 𝐶ℎ𝑎𝑛𝑛𝑒𝑙 𝐵𝑢𝑠𝑦}
Define action set A as
      𝐴= {𝑎1, 𝑎2 }= {𝑇𝑟𝑎𝑛𝑠𝑚𝑖𝑡, 𝐵𝑎𝑐𝑘𝑜𝑓𝑓}
Detected energy < 802.15.4g RS
802.15.4g RS <= Detected energy < 802.11ah ED Threshold

## Slide 11: Q-Learning Backoff
Defining reward is important for Q-Learning
  Define α-fairness based rewards
where is the α-fairness utility with optimal probabilities Pi* and Pb*, σ > 0 is small, and
Rational of reward design
  If the channel is idle, 802.11ah device is encouraged to transmit packet
  If the channel is idle, backoff is a generous operation to perform
  It causes interference to transmit packet when the channel is already busy
  If the channel is busy, backoff is the right action to take

## Slide 12: Locally Observed Data Packet Transmission Rate Estimation
To compute Pi* and Pb*, Mh and Mg are needed
  Mh and Mg can be provided by 802.11ah AP and 802.15.4g PANC coordination
  However, locally observed metric is more practical than network wide metric
Locally observed data packet transmission rate defined as
  Number of locally observed data packets transmissions within a time period
802.11ah locally observed data packet transmission rate
where NT11ah is the number of locally observed data packet transmissions and
NT11ah = neighbor’s packet transmissions + self packet transmissions
802.11ah device can estimate NT11ah by monitoring 802.11ah data packet transmission

## Slide 13: Locally Observed Data Packet Transmission Rate Estimation
To estimate locally observed data packet transmission rate for 802.15.4g
  Assume ratio of control and management packet transmission is low
  Assume only 802.15.4g network and 802.11ah network coexist
802.15.4g locally observed data packet transmission rate
where
Pc is the locally observed 802.11ah packet collision probability
NoP15.4g is the sum of the 802.15.4g packets and collided 802.11ah packets
Estimate NoP15.4g
  Besides successful 802.11ah packets, an 802.11ah device can detect energy of 802.15.4g packet, collided 802.11ah packet and far away 802.11ah packet
  Far away 802.11ah packet can be eliminated by monitoring ACK sent by AP

## Slide 14: Simulation Parameters
NS3 simulator
Transmission power
  13 dBm for both 802.15.4g and 802.11ah (Based on ARIB STD-T108)
Energy detection threshold
  -80 dBm for 802.15.4g
  -75 dBm for 802.11ah
Receiver sensitivity
  -88 dBm for 802.15.4g
  -77 dBm for 802.11ah
Packet payload size
  256 bytes
α=10

## Slide 15: Network Topology 1: Partial Overlapping
802.11ah-2
18 STAs
802.11ah-1
18 STAs
18 STAS
802.11ah-3
802.15.4g
55 Nodes
802.15.4g PANC: black square
802.15.4g nodes: black stars
802.11ah APs: {red, green, blue} diamonds
802.11ah STAs: {red, green, blue} dots

## Slide 16: Network Topology 2: Complete Overlapping
802.15.4g PANC: black square
802.15.4g nodes: black stars
802.11ah APs: {red, green, blue} diamonds
802.11ah STAs: {red, green, blue} dots
802.15.4g
55 Nodes
802.11ah-1
18 STAs
802.11ah-2
18 STAs
18 STAS
802.11ah-3

## Slide 17: Propagation Model
ITU-R P.1411-8 model for propagation between terminals from below roof-top height to near street level
  Lurban = 0 for suburban
11ah Receiver Sensitivity: -77dBm
15.4g Receiver Sensitivity: -88dBm
11ah ED Threshold: -75dBm
15.4g ED Threshold: -80dBm
TX power: 13dBm
920 MHz band
802.11ah: 42m
802.15.4g: 56m

## Slide 18: Low Power Radio Stations in Japan (ARIB STD-T108)
Two transmission power categories
  1mW (0 dBm) or less (for 916.6-916.8MHz and 928.15-929.65MHz)
  Greater than 1mW but less than or equal to 20mW (13 dBm) otherwise
Sending control
Transmission time control for 13 dBm transmission power
  360 seconds or less per arbitrary one hour, i.e., 10% duty cycle
  Response time is not included in the sum of TX time per arbitrary one hour

## Slide 19: Node Traffic With 10% Duty Cycle
Number of packets for 802.15.4g
  Traffic rate with PHY rate = 100 kbps
    10 kbps
  Number of packets with packet size = 256 bytes
    4.88 pkt/s (header not included)
  Packet generation rate used in simulation
    0.5 pkt/s
Number of packets for 802.11ah
  Traffic rate with PHY rate = 3 mbps and 1.2 mbps
    300 kbps and 120 kbps
  Number of packets with packet size = 256 bytes
    146.48 pkt/s and 58.59 pkt/s (header not included)
  Packet generation rate used in simulation
    3 pkt/s and 1.5 pkt/s

## Slide 20: Simulation Result 1 for Topology 1
Parameters
  802.11ah PHY rate = 3mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 3pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  Near 100% of packet delivery rate for 802.11ah network
  Near 100% of packet delivery rate for 802.15.4g network without 802.11ah
  Α-fair ED-CCA improves 802.15.4g packet delivery rate by about 4%
  Q-Learning backoff improves 802.15.4g packet delivery rate by about 7%

## Slide 21: Simulation Result 2 for Topology 1
Parameters
  802.11ah PHY rate = 3mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 3pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  802.15.4g packet delay is almost same for three methods
  Α-fair ED-CCA delays 802.11ah packet, but not much
  Q-Learning backoff delay 802.11ah packet more

## Slide 22: Simulation Result 1 for Topology 2
Parameters
  802.11ah PHY rate = 3mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 3pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  Q-Learning backoff decreases 802.11ah packet delivery rate by about 6.5%
  Near 100% of packet delivery rate for 802.15.4g network without 802.11ah
  Α-fair ED-CCA improves 802.1.5.4g packet delivery rate by about 8%
  Q-Learning backoff improves 802.1.5.4g packet delivery rate by about 7%

## Slide 23: Simulation Result 2 for Topology 2
Parameters
  802.11ah PHY rate = 3mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 3pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  802.15.4g packet delay is almost same for three methods
  Α-fair ED-CCA delays 802.11ah packet, but not much
  Q-Learning backoff delays 802.11ah packet significantly

## Slide 24: Simulation Result 3 for Topology 1
Parameters
  802.11ah PHY rate = 1.2mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 1.5pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  Near 100% of packet delivery rate for 802.11ah network
  Near 100% of packet delivery rate for 802.15.4g network without 802.11ah
  Α-fair ED-CCA improves 802.1.5.4g packet delivery rate by about 3%
  Q-Learning backoff improves 802.1.5.4g packet delivery rate by about 4%

## Slide 25: Simulation Result 4 for Topology 1
Parameters
  802.11ah PHY rate = 1.2mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 1.5pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  802.15.4g packet delay is almost same for three methods
  Α-fair ED-CCA delays 802.11ah packet, but not much
  Q-Learning backoff delay 802.11ah packet more

## Slide 26: Simulation Result 3 for Topology 2
Parameters
  802.11ah PHY rate = 1.2mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 1.5pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  Near 100% of packet delivery rate for 802.11ah
  Near 100% of packet delivery rate for 802.15.4g network without 802.11ah
  Α-fair ED-CCA improves 802.1.5.4g packet delivery rate by about 10%
  Q-Learning backoff improves 802.1.5.4g packet delivery rate by about 7%

## Slide 27: Simulation Result 4 for Topology 2
Parameters
  802.11ah PHY rate = 1.2mbps
  802.15.4g PHY rate 100kbps
  802.11ah packet generation rate = 1.5pkt/s
  802.15.4g packet generation rate = 0.5pkt/s
Observations
  802.15.4g packet delay is almost same for three methods
  Α-fair ED-CCA delays 802.11ah packet, but not much
  Q-Learning backoff delays 802.11ah packet more

## Slide 28: Summary
802.11ah and 802.15.4g can interfere with each other
Data packet delivery rate
  α-Fairness ED-CCA and Q-Learning backoff can improve 802.15.4g data packet delivery rate
  α-Fairness ED-CCA performs better when 802.11ah density is higher
  Q-Learning backoff perform better when 802.11ah density is lower
  α-Fairness ED-CCA does not have observed affect on 802.11ah network
  Q-Learning backoff affects 802.11ah network when 802.11ah density is higher
Data packet delay
  α-Fairness ED-CCA and Q-Learning backoff hardly delay 802.15.4g data packet
  α-Fairness ED-CCA causes small delay on 802.11ah packet
  Q-Learning backoff may significantly delay 802.11ah packet
Moving forward, develop coexistence technology for 802.15.4g

## Slide 29: Simulation Parameter Discussion
Transmission power
  Used settings for 802.11ah
    13 dBm
  Used settings for 802.15.4g
    13 dBm
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 30: Simulation Parameter Discussion
Energy detection threshold
  Used settings for 802.11ah
    -75 dBm
  Used settings for 802.15.4g
    -80 dBm
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g
    ?

## Slide 31: Simulation Parameter Discussion
Receiver sensitivity
  Used setting for 802.11ah
    -77 dBm
  Used setting for 802.15.4g
    -88 dBm
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 32: Simulation Parameter Discussion
PHY data rate
  Used settings for 802.11ah
    1.2 mbps
    3mbps
  Used setting for 802.15.4g
    100 kbps
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 33: Simulation Parameter Discussion
Packet payload size
  Used settings for 802.15.4g
    100 bytes
    200 bytes
    256 bytes
  Used settings for 802.11ah
    100bytes
    200bytes
    256 bytes
    500 bytes
    1000 bytes
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 34: Simulation Parameter Discussion
Packet generation rate
  Used settings for 802.11ah
    1 pkt /s
    1.5 pkt /s
    2 pkt/s
    3 pkt/s
    4 pkt/s
  Used settings for 802.15.4g
    1 pkt/60s
    1 pkt/20s
    1 pkt/2s
    2 pkt/s
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.16.5g?
    ?

## Slide 35: Simulation Parameter Discussion
Number of Networks
  Used settings for 802.11ah
    1 AP
    3 APs
  Used settings for 802.15.4g
    1 PANC
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 36: Simulation Parameter Discussion
Number of nodes/STAs per network
  Used settings for 802.11ah
    1 STA
    10 STAs
    18 STAs
    20 STAs
    50 STAs
    80 STAs
    100 STAs
  Used settings for 802.15.4g
    1 node
    10 nodes
    20 nodes
    50 nodes
    55 nodes
    80 nodes
    100 nodes

## Slide 37: Simulation Parameter Discussion
Number of nodes/STAs per network
  Suggested setting for 802.11ah?
    ?
  Suggested setting for 802.15.4g?
    ?

## Slide 38: Simulation Parameter Discussion
Overlapping of network
  Used scenarios
    802.15.4g network completely overlaps 802.11ah networks
    802.15.4g network partially overlaps 802.11ah networks
  Suggested settings?
    ?

## Slide 39: Simulation Parameter Discussion
Any other parameters?
  Duty cycle