## Slide 1: Possible 802.15.4 Mitigation Ideas for 802.15.4g and 802.11ah Coexistence
Date: 2018-05-08
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Ideas for improving coexistence between 802.15.4g based systems and 802.11ah based systems in the Sub-1 GHz (S1G) Bands. This presentations focuses on possible changes to 802.15.4 and other implementation practices which may be used in design and deployment of 802.15.4g based networks to improve coexistence with 802.11ah.
Presented in the Sub-1 GHz (S1G) Coexistence Interest Group of the IEEE 802.19 Working Group.

## Slide 3: Terminology
802.15.4g-2012 incorporated into 802.15.4-2015
PHY nomenclature differences:
  MR-FSK => SUN-FSK
  MR-OFDM => SUN-OFDM
  MR-OQPSK => SUN-OQPSK
Industry uses both sets of terms interchangeably

## Slide 4: Background
Simulation results presentations in 802.19 show the potential for interference between 802.11ah and 802.15.4g networks in the Sub-1 GHz (S1G) bands
  Affects both 802.15.4g and 802.11ah system in different ways
  Coexistence concerns in industry are significant
Simulation presentations:
    802.15-17/0522r2
    802.19-17/0087r3
    802.19-18/0006r1
    802.19-18/0016r1

## Slide 5: Background
There is extensive experience with 802.15.4g deployments
Systems based on 802.15.4g FSK PHYs widely deployed in Smart Utility, Smart City and IoT applications
Estimates of over 100M + devices operating today
Deployment pace appears to be accelerating
A variety of other radio systems operating in the S1G bands
There are a number of commonly used techniques used to improve coexistence
This presents some ideas based on real world implementations

## Slide 6: Mechanisms in the Standard
802.15.4 is optimized for low duty-cycle MAC
  Not high throughput
  MAC requires a lot of “gaps” between transmissions
  Typical applications transmit infrequently
Usual 802 type of CSMA
  Multiple “listen” modes
  CSMA using CCA based on carrier sense (like neighbor politeness)
  CSMA using energy detect (unlike neighbor politeness)
  Exponential backoff following CCA busy
  Includes Aloha modes for low duty-cycle/low channel utilization
Support for channel agility / hopping
Support for synchronous access
  Various types of TDMA, superframes,
  potentially long inactive periods.

## Slide 7: Energy Detect
802.15.4 Energy Detect (as defined in the standard)
  Energy detect threshold lower than used by other services
  CCA duration very long compared to other services
Commonly used mitigation
  Most implementations provide configurable ED level and duration
  Many deployments deviate from the standard
  Many deployments use ALOHA instead of CCA/CSMA
Standard change: Adopt what “everybody knows”
  This has been discussed in 802.15 before
    e.g. doc#15-14-0383-00-0000

## Slide 8
From doc.: <15-14-0383-00-0000>
CCA detection time
ETSI 300 328 (2.4 GHz devices) states in 4.3.2.6.3.2.3 the following limit for minimum listening time required for devices using LBT:
Before a transmission or a burst of transmissions, the equipment shall perform a Clear Channel Assessment (CCA) check using energy detect. The equipment shall observe the operating channel for the duration of the CCA observation time which shall be not less than 18 μs.
By only bounding the minimum detect time, this clause gives a media access advantage to those devices with short CCA times, such as 802.11 devices over devices with longer CCA times such as the 8 symbols (128 μs) stated in 802.15.4

## Slide 9
From doc.: <15-14-0383-00-0000>
CCA detection time
ETSI 300 220 (<1 GHz devices) states in 9.2.2.2 the following limit for minimum listening time (required for devices with transmit duty cycles > 0.1%):
The total listen time, tL, consists of a fixed part, tF, and a pseudo random part, tPS, as the following: tL = tL + tPS
a) The fixed part of the minimum listening time, tF, shall be 5 ms.
b) The pseudo random listening time tPS shall be randomly varied between 0 ms and a value of 5 ms or more in equal steps of approximately 0.5 ms
This detect time regulation of 5 – 10+ ms is significantly longer than the 8 symbols (128 μs) stated in 802.15.4

## Slide 10
From doc.: <15-14-0383-00-0000>
CCA detection time recommended change
To better accommodate regulations such as ETSI 300 328 and 300 220, and to consolidate detection times; change from using the constant aCCATime to a PIB such as macCCATime with units of μs
Most silicon implementations already provide this capability.

## Slide 11
ED threshold values
ED threshold defined as 10dB above defined minimum rx sensitivity. RX sensitivity:
Example: SUN-FSK:
Data Rate Mode | Min. RX Sensitivity | ED Threshold
50 kbps | -91.00 dBm | -81.00 dBm
100 kbps | -86.23 dBm | -76.23 dBm
150 kbps | -87.99 dBm | -77.99 dBm
200 kbps | -84.98 dBm | -74.98 dBm

## Slide 12
ED threshold values
Possible change:
Specify that ED threshold may be set higher or lower according to local regulations
Most implementations provide setting the ED threshold higher or lower than specified in 802.15.4

## Slide 13: Interference Mitigation: Channel Agility
Reduces collision probability
Current Support for channel agility / hopping
  FSK PHY characteristics suitable to hopping
  Narrow bandwidth == many channels
  Several methods defined, but only TSCH used much
  Industry “standard” methods are widely used not in the standard
Regulatory domains differ
  North America: Frequency hopping required for operation at full (1W) power
  Allowable but not widely used in Japan
  Allowed in Europe, but not as many channels
Extensions to standards
  Hopping schemes developed by industry alliances widely used
  Could be folded into the standard

## Slide 14: Persistent CSMA
802.15.4 CSMA
  Exponential backoff per channel access attempt only
  Does not specify when/if another attempt is made following CSMA failure
  No persistence – next try (initiated by higher layer) “fresh”
  Wide range if CSMA timing parameters
  Opportunity for ‘tuning’ of CSMA for sub-1GHz

## Slide 15: Deployment Practices
Use of channel hopping / agility
Recommendations for CSMA parameters
Recommendations for retransmission behaviors
Draw from industry experience

## Slide 16: Summary
A few small changes and/or guidance could be useful:
Some simple and widely used ‘tweaks’ to the standard could help
Some guidance (recommended practice?) reflecting successful deployment practices.
A very preliminary look; more study is needed!