## Slide 1: Sub-1GHz Coexistence Simulation Parameters
Date: 2018-06-11
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
An Interest Group (IG) in sub-1GHz coexistence has been established in IEEE 802.19
Simulation results [1, 2] have been presented at several IEEE meetings
This document aims to provide a consensus set of simulation parameters for subsequent simulations
The focus here is on 802.11ah and 802.15.4g operating in a shared channel, which may apply in regulatory domains where there is limited spectrum for these technologies (i.e. Japan)
This is intended for the worst case co-channel operation case, when both networks in the same vicinity are operate on the same channel

## Slide 3: Transmit Parameters
Parameter | 802.11ah | 802.15.4g
Frequency Band | 920-928 MHz | 920-928 MHz
Channel Bandwidth | 1 MHz | 400 kHz
AP Transmit Power | 13 dBm | 13 dBm
STA Transmit Power | 13 dBm | 13 dBm
Modulation | OFDM | Binary FSK
PHY Rate | 300 kb/s | 100 kb/s
Regulatory Duty Cycle Limit | 360 seconds every 3600 seconds | 360 seconds every 3600 seconds
Packet Size | 100 bytes | 100 bytes
Number of Stations | [50, 100] | [50, 100]
Network Uplink Offered Load | [1, 10] kb/s | [1, 10] kb/s

## Slide 4: Receive Parameters
Parameter | 802.11ah | 802.15.4g
RX Sensitivity | -95 dBm | -88 dBm
Carrier Sense Level | -95 dBm | -88 dBm
Energy Detection Level | -75 dBm | -78 dBm

## Slide 5: CSMA Parameters
Parameter | 802.11ah | 802.15.4g
CCA Time | 128 µs | 128 µs
Slot Time | 52 µs | 320 µs
SIFS (time till ACK) | 160 µs | 192 µs*
DIFS (minimum Idle time) | 264 µs | 1000 µs
Note: Minimum CCA Time of 128 us is set by Japan regulations
* In 802.15.4g the time from receiving a packet until sending an ACK is symbol rate dependent

## Slide 6: References
Jianlin Guo, et. al., “Interference Mitigation for Coexisting 802.15.4g and 802.11ah Networks,” IEEE 802.19-18/27r1, May 2018
Jianlin Guo, et. al., “Update on Coexistence Simulations,” 802.15.4g and 802.11ah, IEEE 802.19-18/16r1, March 2018
Std. IEEE 802.1ah, “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 2: Sub 1 GHz License Exempt Operation,” Dec 2016
Std. IEEE 802.15.4g, “Low-Rate Wireless Personal Area Networks (LR-WPANs) Amendment 3: Physical Layer (PHY) Specifications for Low-Data-Rate, Wireless, Smart Metering Utility Networks,” March 2012
ETSI TR 103 245 V1.1.1 (2014-11), ”Electromagnetic compatibility and Radio spectrum Matters (ERM); System Reference document (SRdoc); Technical characteristics and spectrum requirements of wideband SRDs with advanced spectrum sharing capability for operation in the UHF 870 - 876 MHz and 915 - 921 MHz frequency bands”