## Slide 1: Sub-1GHz Coexistence Simulation Parameters
Date: 2018-06-11
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
An Interest Group (IG) in sub-1GHz coexistence has been established in IEEE 802.19
Simulation results [1, 2] have been presented at several IEEE meetings
This document aims to provide a consensus set of simulation parameters for subsequent simulations
The focus here is on 802.11ah and 802.15.4g operating on channels with shared frequency band, which may apply in regulatory domains where there is limited spectrum for these technologies (e.g. Japan)
This is intended for the worst case co-channel operation case, when both networks in the same vicinity are operating on the channels with shared frequency band

## Slide 3: Notes
This document aims to provide a framework for simulation parameters and does not restrict the ranges of the parameters
The values of the parameter are region and/or PHY and/or use case dependent
  For example, some parameters are based on Japan regulatory and some parameters are based on SUN PHYs specified in IEEE 802.15.4g-2012 (Section 18.1 MR-FSK PHY, Section 18.2 MR-OFDM PHY, Section 18.3 MR-O-QPSK PHY).
Most of the 802.11ah parameters are fixed
Most of the 802.15.4g parameters are symbol rate dependent

## Slide 4: Transmit Parameters
Parameter | 802.11ah | 802.15.4g
Frequency Band | 920-928 MHz | 920-928 MHz
Channel Bandwidth | 1 MHz | 400 kHz
AP/PANC Transmit Power | 13 dBm | 13 dBm
STA/Node Transmit Power | 13 dBm | 13 dBm
Modulation | OFDM | Binary FSK
PHY Rate | 300 kb/s | 100 kb/s
Regulatory Duty Cycle Limit for Radio equipment* | 360 seconds every 3600 seconds | 360 seconds every 3600 seconds
AP refers radio equipment that acts as the 802.11ah access point
PANC refers radio equipment that acts as the 802.15.4g PAN coordinator
STA refers radio equipment that acts as the 802.11ah station
Node refers radio equipment that acts as the 802.15.4g station
* Japan regulatory

## Slide 5: Receive Parameters
Parameter | 802.11ah | 802.15.4g
RX Sensitivity | -95 dBm | -88 dBm
Carrier Sense Level | -95 dBm | -88 dBm
Energy Detection Level | -75 dBm | -78 dBm
Note: These parameters are PHY dependent

## Slide 6: Traffic Parameters
Parameter | 802.11ah | 802.15.4g
Packet Size | 100 bytes | 100 bytes
Number of Stations | [50, 100] | [50, 100]
Network Uplink Offered Load | [1, 10] kb/s | [1, 10] kb/s
Note: These parameters are use case dependent

## Slide 7: 802.11 and 802.15.4 Abbreviations
Abbreviation | 802.11 Definition | Usage
SIFS | Short interframe space | Time between frame and ACK
DIFS | Distributed interframe space | Minimum idle time needed to start a transmission
AIFS | Arbitration interframe space | QoS generalization of the DIFS
CW | Contention window | To draw random backoff slots
Abbreviation | 802.15.4 Definition | Usage
SIFS | Short interframe spacing | Minimum idle time after a short frame transmission process
AIFS | ACK interframe spacing | Time between frame and ACK
BE | Backoff exponent | To draw random backoff periods
CW | Contention window | Number of backoff periods to be idle before transmission

## Slide 8: CSMA Parameters
802.11ah Parameter | Value
CCA Time1 | 128 µs
Slot Time | 52 µs
SIFS (time till ACK) | 160 µs
DIFS (minimum Idle time) | 264 µs
1 Minimum CCA Time of 128 us is set by Japan regulations. In 802.11ah, CCATime ≤ 40 us.
2 For the SUN PHYs operating in the 920 or 950 MHz band, phyCCADuration is from 0 to 1000 symbols (symbol duration is 20 us for SUN-FSK PHY). For all other PHYs, it is called CCATime instead of phyCCADuration.
3 For the SUN PHYs operating in the 920 or 950 MHz band, the value is TurnaroundTime + phyCCADuration. For all other PHYs, the value is TurnaroundTime + CCATime. For SUN PHYs, TurnaroundTime is 1ms.
4 AIFS is 1ms for SUN PHYs, LECIM PHYS, or TVWS PHYs and is equal to macSIFSPeriod for other PHYs.
5 For SUN-FSK PHY, the minimum inter-frame space (called SIFS in standard) is 1ms.
802.15.4g Parameter | Value
phyCCADuration2 | 140 µs
UnitBackoffPeriod3 | 1140 µs
AIFS4 | 1000 µs
Minimum idle time5 | 1000 µs

## Slide 9: CSMA Parameters
802.11ah Parameter | Value
CWmin | 15
CWmax | 1023
CW | [CWmin, CWmax]
RetryLimit | 7
Note 1: For 802.11ah, the number of random backoff slots is drawn from a uniform distribution over the interval [0,CW] with CW = CWmin initially.
Note 2: 802.11ah performs CCA in every backoff slot.
Note 3: For 802.15.4g, the number of random backoff periods is drawn from a uniform distribution over the interval [0, 2BE-1] with BE = MinBE initially.
Note 4: 802.15.4g performs CCA after backoff completes.
Note 5: For 802.15.4g, CW = 1 for non-beacon enabled network and CW = 2 for beacon enabled network.
802.15.4g Parameter | Value
MinBE | 3
MaxBE | 5
BE | [MinBE, MaxBE]
RetryLimit | 4
CW | 1

## Slide 10: References
Jianlin Guo, et. al., “Interference Mitigation for Coexisting 802.15.4g and 802.11ah Networks,” IEEE 802.19-18/27r1, May 2018
Jianlin Guo, et. al., “Update on Coexistence Simulations,” 802.15.4g and 802.11ah, IEEE 802.19-18/16r1, March 2018
Std. IEEE 802.1ah, “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 2: Sub 1 GHz License Exempt Operation,” Dec 2016
Std. IEEE 802.15.4g, “Low-Rate Wireless Personal Area Networks (LR-WPANs) Amendment 3: Physical Layer (PHY) Specifications for Low-Data-Rate, Wireless, Smart Metering Utility Networks,” March 2012
ETSI TR 103 245 V1.1.1 (2014-11), ”Electromagnetic compatibility and Radio spectrum Matters (ERM); System Reference document (SRdoc); Technical characteristics and spectrum requirements of wideband SRDs with advanced spectrum sharing capability for operation in the UHF 870 - 876 MHz and 915 - 921 MHz frequency bands”