## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.11ax and 802.15.4 HRP_LRP Coexistence
Date Submitted: 14-June-2018
Source: Tim Harrington
Company: Pro-ID
Address: 22156 Old Santa Cruz Hwy, Los Gatos, CA 95033
Voice: +1 408 353 3675, E-Mail: Timothy.Harrington@Verizon.net
Re: 802.11 and 802.15 coexistence in 6 GHz bands
Abstract: Comments and brainstorming ideas for co-existence to improve 802.11ax CAD
Purpose: Promote coexistence analysis and positive coexistence
Notice: This document has been prepared to assist the IEEE P802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.19.

## Slide 2: Part 1: Review of doc IEEE 802.11-16/1348r3 TGax Coexistence Assurance Document and Brainstorming Ideas from May 2018 Wireless Interim

## Slide 3: Summary
802.11ax scope has been changed to include use of the 6 GHz band
Systems based on 802.15.4 UWB PHYs are widely used in the 6 GHz band
Task Group 15.4z has reviewed the CAD and provides comments and suggestions to help improve the11ax TG CAD so that there is better understanding of the coexistence characteristics

## Slide 4: 3 Coexistence with non-802.11 systems
IEEE 802.15.4 HRP UWB and LRP UWB PHYs operate in the 6 GHz band. Coexistence has not been characterized or analyzed with respect to 802.15.4 HRP UWB and LRP UWB which use Impulse Radio (IR) modulation.
With reference to CCA/CSMA as a coexistence mechanism, does the current anticipated CCA/CSMA mechanism able to detect 802.15.4 UWB signals for bands above 6 GHz; How does this affect coexistence with 802.15.4 UWB based systems?
An assessment of the impacts on 802.15.4 UWB based on the different 802.11ax channelization options would be helpful.
It would be helpful to provide analysis of 802.11ax with respect to the 802.15.4 UWB systems as both victim and assailant. This has not been done in a prior 802.11 CAD
We are aware that there has been extensive consideration of coexistence between 802.11 and 3GPP LAA systems. As this is relevant to the coexistence of 802.11ax. It would be helpful to mention it and provide a reference.

## Slide 5: 5.2 Spatial Reuse
Compare 11ax noise floor to the noise floor of HRP UWB and LRP UWB at different distances, different channel widths.

## Slide 6: 5.6 Operation in the 6 GHz Band
An analysis of Packet error rate for 802.11ax, and frame error rate or bit rate for LRP and HRP when used within a representative set of operational ranges would be useful.
Analysis of the effects of 802.11ax CSMA on UWB: How will CSMA hear HRP and LRP pulses?
How will the different bandwidth options affect UWB devices?
What are the effects at similar center frequencies, and at different frequencies for LRP UWB, HRP UWB, and 802.11ax?. What happens at the extremes?

## Slide 7: Part 2: Brainstorming Ideas from May 2018 Wireless Interim

## Slide 8: Coexistence Brainstorming
Can 802.11ax and LAA use the same power levels as UWB?
  ???
Can 802.11ax LAA use adaptive power control
  Sense UWB and restrict power?
Raise UWB power level to match 802.11ax and LAA
  Not desirable because it will shorten battery life, but could be a solution if we jointly petitioned FCC and ECC
Duty cycle for 802.11 and LAA?
  Could there be a predictable duty cycle on a local basis?
What about 3GPP LAA in the 6 GHz band
  Does 802.11ax anticipate the arrival of 3GPP LAA
Slide 8

## Slide 9: Coexistence Brainstorming
UWB scan receiver that looks for interference, and then go to a different channel
  Too costly for UWB RTLS tags
Coexistence control channel interface for scheduling
  Too costly for UWB RTLS tags
Send signal to trigger CSMA to cause 802.11ax and 3GPP LAA to back off
  Possible if these devices can be made to sense pulses
WGFM appears to be restricting 6 GHz broadband to less than 6.4125 GHz in the EU. If this were extended to 6.3 GHz, then 802.11ax would have 340 MHz of new bandwidth, and UWB centered at 6.55 GHz would have a clear channel
  Is this a possibility for 802.11ax?
Slide 9