## Slide 1: 920 MHz Status in Japan
Date: 2018-07-10
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Share the 920MHz regulation status in Japan toward simulation and use case scenario discussion

## Slide 3: Channelization in Japan
Several wireless systems operate on same frequency band which were standardized as ARIB STD-T106, T107 and T108
ARIB STD-T108 (20mW) on 920.5 ~ 928.1MHz (7.6MHz) includes 802.15.4g system, but coexistence operation with Passive System (250mW) and STD-T108 (250mW) is required for 920.5 ~ 923.5MHz (3.0MHz). So, 923.5 ~ 928.1MHz (4.6MHz) is only dedicated channels for 802.15.4g
928.0
920.6
923.4
1W ARIB STD-T106 Licensed/Registered
250mW ARIB STD-T107 Unlicensed
916.0
919.2
Passive System (RFID, etc)
1mW ARIB STD-T108 Unlicensed
20mW ARIB STD-T108 Unlicensed
250mW ARIB STD-T108 Licensed/Registered
Active System (LPWA, 802.15.4g, etc)
IEEE802.15.4g, etc
929.65
Coexistence Operation
Dedicate channels for sensor networks
①
②
③
④
⑤
Ch: 200KHz
Ch: 100KHz
MHz

## Slide 4: Current Use Cases
Current use cases in the market for each wireless system*1.
Only Specified Low-Power Radio Station (20mW, Unlicensed) for 802.15.4g and 802.11ah*2
*1: MIC is going to deregulate the current standard to meet the future use cases (Inside/Outside, Tx Time, Duty Cycle, etc)[3]
*2: IEEE 802.11ah is not specified on ARIB STD-T108 at this moment [2]
② Specified Low-Power Radio Station (Unlicensed, Passive System)
Tx Power: 250mW
Frequency: 916.7~923.5MHz
Use Cases: RFID for inside/outside
ARIB STD-T107
① Inside Radio Station
(Licensed/Registered, Passive System)
Tx Power: 1W
Frequency: 916.7~920.9MHz
Use Cases: RFID for Logistics Management, etc
ARIB STD-T106
⑤ Land Mobile Station
(Licensed/Registered, Active System)
Tx Power: 250mW
Frequency: 920.5 ~ 923.5MHz
Use Cases: LPWA for sensors (forest, bridge, etc)
ARIB STD-T108
④ Specified Low-Power Radio Station
(Unlicensed, Active System)
Tx Power: 20mW
Frequency: 920.5 ~ 928.1MHz
Use Cases: Smart Mater (Electric, Gas, Water), etc
ARIB STD-T108
③ Specified Low-Power Radio Station
(Unlicensed, Active System)
Tx Power: 1mW
Frequency: 915.9 ~ 929.7MHz
Use Cases: Home Security, Remote Control
ARIB STD-T108
[1][2][3]

## Slide 5: ARIB STD-T108 (20mW)
Specified Low-Power Radio Station (Unlicensed, Active System)*
Item |  | Parameters and functionality
Frequency Band |  | 920.5MHz ~ 928.1MHz (7.6MHz) 920.5 ~ 923.5 MHz (3.0MHz) --- Coexistence with others 923.5 ~ 928.1 MHz (4.6MHz) --- Dedicated channel for STD-T108
Channel bandwidth |  | 200KHz
Transmission Power |  | 20mW
Transmission method | Contents | Data signal
 | Modulation | Not specified
Antenna Gain |  | 3dBi or less (absolute gain). However, in case EIRP is less than the value of 3dBi plus 1mW or 20mW of antenna power, it is allowed to fill in the gap by the antenna gain
Carrier Sense (CS) and Duty Cycle | CS ≧ 5msec, 920.5 ~ 923.4 MHz | Tx Time ≦ 4sec, Wait ≧ 50ms
 | 5msec < CS ≧ 128us 920.5 ~ 928.1 MHz | Tx Time ≦ 400ms, Wait ≧ 2ms, Total Tx Time ≦ 360s/h/station
Note |  | Refer IEEE 802.15.4g for PHY parameters
[3][4]
*: MIC is going to deregulate the current standard to meet the future use cases [3]

## Slide 6: Summary
802.15.4g specified on ARIB STD-T108 (20mW) can operate on
  920.5 ~ 928.1MHz (7.6MHz) , but
    920.5 ~ 923.5MHz (3.0MHz) --- Coex. with Passive Systems and LPWA
    923.5 ~ 928.1MHz (4.6MHz) --- Dedicated channel for sensor net.
We would like the Sub 1GHz IG to consider coexistence between 802.15.4g and 802.11ah under the conditions and operational constraints noted above.

## Slide 7: References
MIC, http://www.soumu.go.jp/main_content/000544861.pdf, 2018/04/10
MIC, http://www.soumu.go.jp/main_content/000550848.pdf, 2018/05/14
MIC, http://www.soumu.go.jp/main_content/000551143.pdf, 2018/05/15
https://www.arib.or.jp/english/html/overview/doc/5-STD-T108v1_0-E1.pdf
MIC (Ministry of Internal Affairs and Communications)