## Slide 1: S1G Coexistence Simulation Update
Date: 2018-11-11
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Presentation to Sub-1 GHz (S1G) Band Coexistence Study Group of the IEEE 802.19 Working Group on Simulation Update of the Coexisting IEEE 802.15.4g and IEEE 802.11ah Using New Simulation Parameters, and Japan Regulatory on Transmission Time Control for Low Power Radio Stations (ARIB STD-T108).

## Slide 3: 802.11ah and 802.15.4g Backoff Overview
802.15.4g Backoff
802.15.4g Backoff
Backoff
counter = 0
Random Backoff Period
CCA
Busy: hold backoff counter
Clear: decrease backoff counter
Busy: Re-backoff
Clear: Transmit
Backoff
counter = 0
Random Backoff Period
CCA
Busy: Re-backoff
Clear: Transmit
Observation
  802.11ah backoff time can be very long
  802.15.4g Backoff time is bounded
Busy
DIFS

## Slide 4: Simulation Parameters and Performance Metrics
802.11ah STAs and 802.15.4g nodes
  [50, 100]
Total offered load for 802.15.4g network and 802.11ah network
  [10, 40] kb/s
Packet size
  100 bytes
PHY data rate
  300 kb/s for 802.11ah
  100 kb/s for 802.15.4g
Data packet delivery rate
Data packet latency

## Slide 5: Node Deployment
802.15.4g Node
802.11ah Node

## Slide 6: 50 Nodes, 10 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 100% of packets
  802.15.4g delivers 98.8944% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 61.6ms], 802.1.5.4g delay in [12.8ms, 110ms]

## Slide 7: 50 Nodes, 20 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9869% of packets
  802.15.4g delivers 98.4281% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 60.3ms], 802.1.5.4g delay in [12.8ms, 122.5ms]

## Slide 8: 50 Nodes, 40 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9408% of packets
  802.15.4g delivers 95.5775% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 146.1ms], 802.1.5.4g delay in [12.8ms, 125.9ms]

## Slide 9: 50 Nodes, 20 kbps for 802.11ah and 20kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9998% of packets
  802.15.4g delivers 92.3671% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 77.2ms], 802.1.5.4g delay in [12.8ms, 127.1ms]

## Slide 10: 50 Nodes, 40 kbps for 802.11ah and 20 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9852% of packets
  802.15.4g delivers 86.1796% of packet
Packet latency
  802.11ah achieves similar packet latency as 802.15.4g
  802.11ah delay in [4.8ms, 428.2ms], 802.1.5.4g delay in [12.8ms, 130.5ms]

## Slide 11: 100 Nodes, 10 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 100% of packets
  802.15.4g delivers 99.2073% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 47.4ms], 802.1.5.4g delay in [12.8ms, 116.8ms]

## Slide 12: 100 Nodes, 20 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9846% of packets
  802.15.4g delivers 98.6011% of packet
Packet latency
  802.11ah achieves shorter packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 51.9ms], 802.1.5.4g delay in [12.8ms, 118.0ms]

## Slide 13: 100 Nodes, 40 kbps for 802.11ah and 10 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9322% of packets
  802.15.4g delivers 96.0831% of packet
Packet latency
  802.11ah achieves longer packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 244.6ms], 802.1.5.4g delay in [12.8ms, 125.9ms]

## Slide 14: 100 Nodes, 20 kbps for 802.11ah and 20 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9966% of packets
  802.15.4g delivers 93.5012% of packet
Packet latency
  802.11ah achieves longer packet latency than 802.15.4g
  802.11ah delay in [4.8ms, 217.6ms], 802.1.5.4g delay in [12.8ms, 132.8ms]

## Slide 15: 100 Nodes, 40 kbps for 802.11ah and 20 kbps for 802.15.4g
Packet delivery rate
  802.11ah delivers 99.9560% of packets
  802.15.4g delivers 85.9632% of packet
Packet latency
  802.11ah achieves much longer packet latency than 802.15.4g
  802.11ah delay in [11.3ms, 1085.8ms], 802.1.5.4g delay in [12.8ms, 138.5ms]

## Slide 16: Summary
802.11ah interferes with 802.15.4g packet delivery
802.15.4g interferes with 802.11ah packet latency
802.11ah packet latency is unbounded
  CCA is required in each backoff slot
  Backoff counter decreases only if the channel is idle
802.15.4g packet latency is bounded
  CCA is not required during random backoff period
  CCA is performed after random backoff period

## Slide 17: References
Steve Shellhamer, et. al., “Sub-1GHz Coexistence Simulation Parameters” IEEE 802.19-18/39r2, September 2018
ARIB STD-T108 Version 1.0, “920MHz-Band Telemeter, Telecontrol and Data Transmission Radio Equipment”, February 2012