## Slide 1: 920 MHz Status Update in Japan
Date: 2018-11-14
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Share the 920MHz regulation status in Japan toward simulation and use case scenario discussion

## Slide 3: Channelization in Japan
Several wireless systems operate on same frequency band which were standardized as ARIB STD-T106, T107 and T108
ARIB STD-T108 (20mW) on 920.5 ~ 928.1MHz (7.6MHz) includes 802.15.4g system, but coexistence operation with Passive System (250mW) and STD-T108 (250mW) is required for 920.5 ~ 923.5MHz (3.0MHz). So, 923.5 ~ 928.1MHz (4.6MHz) is only dedicated channels for 802.15.4g
928.0
920.6
923.4
1W ARIB STD-T106 Licensed/Registered
250mW ARIB STD-T107 Unlicensed
916.0
919.2
Passive System (RFID, etc)
1mW ARIB STD-T108 Unlicensed
20mW ARIB STD-T108 Unlicensed
250mW ARIB STD-T108 Licensed/Registered
Active System (LPWA, 802.15.4g, etc)
IEEE802.15.4g, etc
929.65
Coexistence Operation
Dedicate channels for sensor networks
①
②
③
④
⑤
Ch: 200KHz
Ch: 100KHz
MHz

## Slide 4: ARIB STD-T108 (20mW)
Specified Low-Power Radio Station (Unlicensed, Active System)
for 802.15.4g and 802.11ah*2
Item |  | Parameters and functionality
Frequency Band |  | 920.5MHz ~ 928.1MHz (7.6MHz) 920.5 ~ 923.5 MHz (3.0MHz) --- Coexistence with others 923.5 ~ 928.1 MHz (4.6MHz) --- Dedicated channel for STD-T108
Channel bandwidth |  | 200KHz
Transmission Power |  | 20mW
Transmission method | Contents | Data signal
 | Modulation | Not specified
Antenna Gain |  | 3dBi or less (absolute gain). However, in case EIRP is less than the value of 3dBi plus 1mW or 20mW of antenna power, it is allowed to fill in the gap by the antenna gain
Carrier Sense (CS) and Duty Cycle | CS ≧ 5msec, 920.5 ~ 923.4 MHz | Tx Time ≦ 4sec, Wait ≧ 50ms
 | 5msec < CS ≧ 128us 920.5 ~ 928.1 MHz | Tx Time ≦ 400ms, Wait ≧ 2ms, Total Tx Time ≦ 360s/h/station
Note |  | Refer IEEE 802.15.4g for PHY parameters
[1]
*1: IEEE 802.11ah is not specified on ARIB STD-T108 at this moment [1]

## Slide 5: Deregulation of Duty Cycle for Active System
Each specified low-power radio station can transmit radio signal for 360 seconds/hour at most in the current 920MHz regulation.
MIC (Ministry of Internal Affairs and Communications) is considering deregulate the current duty cycle regulation:
  When a specified low-power radio station use multiple channels in time division, duty cycle is 720 seconds/hour.
  Duty cycle of each channel is 360 seconds/hour/station.
[2]
Current regulation
Using single channel
Total Tx Time ≦ 360sec.
Per station ≦ 360sec.
Using multiple channels
360sec.
360sec.
360sec.
100sec.
80
100
80
3600 seconds
3600 seconds
Time
Time
3600 seconds
3600 seconds
Time
Time
360sec.
360sec.
720 sec.
Using multiple channels
Using single channel
Deregulation of Duty Cycle
Total Tx Time ≦ 360sec.
Per station ≦ 360sec.
120sec.
160
90
350

## Slide 6: Summary
MIC is considering deregulation of duty cycle to 720 seconds/hour/station in the case of using multiple channels.
We would like the Sub 1GHz SG to consider the deregulation of duty cycle in the future.

## Slide 7: References
https://www.arib.or.jp/english/html/overview/doc/5-STD-T108v1_0-E1.pdf
MIC, http://www.soumu.go.jp/main_content/000551143.pdf, 2018/05/15
MIC (Ministry of Internal Affairs and Communications)