## Slide 1: 802.11ah CCA and 802.15.4g CCA
Date: 2019-01-17
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
This Documents Overviews the CCA Mechanism of IEEE 802.11ah and IEEE 802.15.4g.

## Slide 3: 802.11 Channel Sensing Overview
802.11 Channel Sensing
CS
ED
CS and ED
Virtual Carrier Sensing
Clear Channel Assessment
Network Allocation Vector
Network Allocation Vector (NAV)
  An indicator, maintained by each station, of time periods when transmission onto the wireless medium (WM) will not be initiated by the station whether or not the station’s CCA function senses that the WM is busy.
  Updated according the Duration/ID field of 802.11 frame
NAV has priority over CCA

## Slide 4: 802.15.4 Channel Sensing Overview
Clear Channel Assessment
CS
ED
CS and ED
802.15.4 Channel Sensing
No virtual carrier sensing
But allowing non-sensing
ALOHA
UWB PD

## Slide 5: 802.11-2016 Clear Channel Assessment (CCA)
The Direct Sequence Spread Spectrum (DSSS) PHY shall provide the capability to perform CCA according to both:
  A — at least one of the following options:
    CCA Mode 1
      Energy above threshold
      CCA shall report a busy medium upon detection of any energy above the ED threshold.
    CCA Mode 2
      CS only
      CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
    CCA Mode 3
      CS with energy above threshold
      CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.
and
  B — CCA Mode 6
    CCA shall report a busy medium upon detection of any energy above -62 dBm

## Slide 6: 802.11-2016 Clear Channel Assessment (CCA)
The High Rate Direct Sequence Spread Spectrum (HR/DSSS) PHY shall provide the capability to perform CCA according to both:
  A — At least one of the following options:
    CCA Mode 1
      Energy above threshold
      CCA shall report a busy medium upon detecting any energy above the ED threshold.
    CCA Mode 4
      CS with timer
      CCA shall start a timer whose duration is 3.65 ms and report a busy medium only upon the detection of a HR/DSSS PHY signal.
      CCA shall report an IDLE medium after the timer expires and no HR/DSSS PHY signal is detected.
      The 3.65 ms timeout is the duration of the longest possible 5.5 Mb/s PSDU.
    CCA Mode 5
      A combination of CS and energy above threshold
      CCA shall report busy at least while a HR/DSSS PPDU is being received with energy above the ED threshold at the antenna.
and
  B — CCA Mode 6
    CCA shall report a busy medium upon detection of any energy above –62 dBm.

## Slide 7: 802.11ah Clear Channel Assessment (CCA)
802.11ah-2016 is an amendment to 802.11-2016 with the updated CCA
802.11ah specifies two types of channelization
  Type 1 channels
    Have CCA levels set to favor protection of ongoing transmissions and range of devices, relative to type 2 channels.
  Type 2 channels
    Have CCA levels set to favor higher bandwidth and data rate transmissions, and to allow for higher reuse within the total network across different BSSs.
  To achieve this, type 2 channel CCA levels (i.e., thresholds) are defined to be higher than type 1 channel CCA levels.
There is no distinction between type 1 and type 2 channel CCA levels for CCA-Energy Detect threshold levels
  -75 dBm for the primary 1 MHz channel
  -72 dBm for the primary 2 MHz channel and the secondary 2 MHz channel
  -69 dBm for the secondary 4 MHz channel
  -66 dBm for the secondary 8 MHz channel

## Slide 8: 802.11ah CCA Sensitivity for the Primary 1 MHz Channel
For Type 1 channels, the PHY shall issue a BUSY if one of the following conditions is present in an otherwise idle primary 1 MHz channel
  The start of an S1G_1M PPDU or duplicate S1G_1M PPDU detected in the primary 1 MHz channel at or above –98 dBm within the primary 1 MHz channel with > 90% probability within a period aCCATime (< 40μs).
  Any S1G PPDU detected at or above –89 dBm within the primary 1 MHz channel with > 90% probability within a period of aCCAMidTime (< 40μs).
For Type 2 channels, the PHY shall issue a BUSY if one of the following conditions is present in an otherwise idle primary 1 MHz channel
  The start of an S1G_1M PPDU or duplicate S1G_1M PPDU detected in the primary 1 MHz channel at or above –89 dBm within the primary 1 MHz channel with > 90% probability within a period aCCATime (< 40μs).
  Any S1G PPDU detected at or above –86 dBm within the primary 1 MHz channel with > 90% probability within a period of aCCAMidTime (< 40μs).
Additionally, for both Type 1 and Type 2 channels, the device shall issue a BUSY if any received signal in the primary 1 MHz channel exceeds the CCA-ED threshold of –75 dBm within a period aCCATime (< 40μs).

## Slide 9: 802.15.4-2011 Clear Channel Assessment (CCA)
The PHY shall provide the capability to perform CCA according to at least one of the following methods:
  CCA Mode 1
    Energy above threshold
    CCA shall report a busy medium upon detecting any energy above the ED threshold
  CCA Mode 2
    Carrier sense only
    CCA shall report a busy medium only upon the detection of a signal with the modulation and spreading characteristics of IEEE 802.15.4. This signal may be above or below the ED threshold.
  CCA Mode 3
    Carrier sense with energy above threshold
    CCA shall report a busy medium only upon the detection of a signal with the modulation and spreading characteristics of IEEE 802.15.4 with energy above the ED threshold

## Slide 10: 802.15.4-2011 Clear Channel Assessment (CCA)
  CCA Mode 4
    ALOHA
    CCA shall always report an idle medium
  CCA Mode 5
    UWB preamble sense based on the SHR of a frame
    CCA shall report a busy medium upon detection of a preamble symbol
    An idle channel shall be reported if no preamble symbol is detected up to a period not shorter than the maximum packet duration plus the maximum period for acknowledgment.
802.15.4g-2012 is an amendment to 802.15.4-2011
802.15.4g added
  CCA mode 4 would typically be used in low duty cycle applications

## Slide 11: Summary
Should 802.19.3 TG look into the impact of 802.11ah and 802.15.4g CCA difference on the coexistence? e.g.,
  ED threshold???
  CCA time???
  ???