## Slide 1: IEEE 802.11ah Use Cases considered by AHPC
Date: 2019-07-16
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
Use cases of IEEE 802.11ah system considered in the 802.11ah Promotion Council (AHPC) Japan are summarized.

## Slide 3: Scenarios (1/2)
[Home]
  Home security network
  Contents synchronization between home server and cars
[Office]
  Power management
[Industry]
  Wireless sensor network backbone in process automation industry
  Efficient field work and inspection at factories
  Remote monitoring of wildlife to prevent damages of agricultural crops

## Slide 4: Scenarios (2/2)
[Infrastructure]
  Surveillance camera system using edge computing
  Advanced water pipe management
  Backup network for cellular drone
  Detecting deterioration of infrastructure by wireless vibration sensors
  [Mobility]
  Push notification customer support
  Advanced management in public transportation

## Slide 5: [Home] Home security network
Use case
Home security service may be expanded using 802.11ah to integrate the multiple home security devices.
Background
Existing home security devices such as magnetic motion sensors are using 426MHz band (in some countries) while outdoor surveillance cameras, alarming speakers are using Wi-Fi (2.4GHz and/or 5GHz) network. 802.11ah is able to integrate multiple home security devices to utilize the wireless infrastructure for home security service. It may be expected to reduce a cost and provide variety of sensors in the network.
Summary
Images

## Slide 6: [Home] Contents synchronization between home server and cars
Images
802.11ah
Synchronization of home server contents and car media library, uploading of car status info and remote setting (e.g. route navigation) via 802.11ah.
Use case
Synchronization of contents between home server and cards using 802.11ah supports fun to drive .
Background
To enjoy multimedia contents during drive, general way is to use digital media players or memory cards. The 802.11ah enables to send those data to outdoors and synchronization with car media library.
In addition, 802.11ah is able to upload and provide variety of information from the cars including drive records, diagnostics, notification of vandalism, route navigation for safety drive.
Summary

## Slide 7: [Office] Power management
Use case
Remote monitoring and control of devices in the building using 802.11ah integrated with BMES enables to save a energy .
Background
BEMS (Building Energy Management System) is being expected for cost saving based on the demand of ISO14001 and rising electricity charge.
Furthermore, individual energy management per tenants in the building will be needed additional cost saving and ISO certification.
By monitoring and controlling with 802.11ah compatible devices (e.g. computers, MFPs (Multifunction Peripherals), air conditioners, ceiling lighting units), companies can optimize usage of electricity.
Summary
Images

## Slide 8: [Industry] Wireless sensor network backbone in process automation industry
Use case
Wireless backbone for industrial wireless sensor network using 802.11ah enables to provide low cost, flexible wireless infrastructure, coexistence management in production site.
Background
Industrial wireless sensor network such as ISA100 Wireless (IEEE 802.15.4 - 2.4GHz band) are operating in the production site for process monitoring and control. And WLAN networks are running at same plant area for other purposes.
Although some applications need a wireless backhaul network to transfer the sensing data from remote I/O units in the field to a central control room, it is difficult to deploy another WLAN network due to interference.
Also wireless backhaul requires a long distance communication with higher bandwidth.
Summary
Images
Interface for remote I/O: Communicate with central control room
Wireless back bone network: Interface for WSN
Wireless sensor network(WSN)

## Slide 9: [Industry] Efficient field work and inspections at factories
Use case
Remote visual inspections are expected using 802.11ah for efficient and safe plant maintenances. It requires the large data transfer such as still images and videos for the asset condition monitoring and predictive maintenance.
Background
Mobile workforce is a important to keep a safe plant operation and improve productivity.
The Augmented Reality (AR) may become a one of the key technology for the smart manufacturing and maintenance using IP base wireless technology such as WLAN.
Summary
Images

## Slide 10: [Industry] Remote monitoring of wildlife to prevent damages to agricultural crops
Use case
Remote monitoring and alarming system using 802.11ah to prevent damages of agricultural crops by the wild life. Existing system notices only events when animals were trapped, but 802.11ah enables to identify trapped animals by visual monitoring for saving a time to find appropriate tools for catching by hunters.
Background
Crop damages by number of wildlife such as boars or deers are being increased.
In order to reduce the economic losses of agriculture business, traps and patrolling are needed.
Summary
Images

## Slide 11: [Infrastructure] Surveillance camera system using edge computing
Use case
The 802.11ah enables not only wider area of video surveillance but also sending alert and pictures when some events or system fault happened. It may be a lower investment cost against existing system.
Background
Current regulation in Japan, video surveillance system requires local backup. The 802.11ah device enables easy integration with IP base edge computing devices. Today the edge computing device sends alarms using 60GHz band when malfunction had been detected. It may be a higher costs.
Summary
Images

## Slide 12: [Infrastructure] Advanced water pipe management
Use case
The 802.11ah device enables efficient management of the water pipe lines and to improve predictive maintenance.
Background
Wireless sensor network is expected to use monitoring of the sewer pipes flow and water level.
Water pipe leakage detection is using acoustic signal. By using high frequency sound, more accurate detection can be expected, but requires higher bandwidth.
In case of LPWA, it is difficult to send large data efficiently for this purpose.
Summary
Images
802.11ah

## Slide 13: [Infrastructure] Backup network for cellular drone
Use case
The 802.11ah enables to enhance drone's usability and capability.
Background
A cellular drone provided by service providers of mobile phone may have a risk of uncontrollable under network congestion when disasters are happen.
Some drones are equipped with WLAN interface, thus operator is able to use WLAN network as a backup for drone control.
However, existing WLAN has a limitation of communication range for flying area.
Summary
Images

## Slide 14: [Infrastructure] Detecting deterioration of infrastructure by wireless vibration sensors
Use case
The 802.11ah enhances a wireless sensing for social infrastructure. It is able to collect large data such as vibrations from wide area.
Background
There are many old infrastructures and their simultaneously deterioration is becoming a serious problem. Efficient and cost effective maintenance works are required.
Some sensing and monitoring solutions have been implemented, however large size of data has not been collected enough due to a limitation of bandwidth.
Summary
Images

## Slide 15: [Mobility] Push notification for customer support
Use case
The 802.11ah enables to provide new type of advertisement solution from shops to cars. Car dealers send an advertisement messages to moving cars nearby using 802.11ah. Those information may include maintenance services based on the condition of the car.
Background
In general, breakdown maintenance or time based maintenance are popular for cars. It may not be related to an actual condition of cars or how often use cars.
In order to improve a maintenance service for safety car driving, HaLow network enables to send a notice for maintenance and/or sales promotion from car dealers.
Summary
Images
Collecting information from moving cars near a dealer and providing push notifications/recommendations.

## Slide 16: [Mobility] Advanced management in public transportation
Use case
The 802.11ah enables remote condition monitoring of pubic trains/buses and its drivers to prevent traffic accidents.
Background
The 802.11ah enables collection of driving record data from the bus/train at garage from remote office.
A traffic accident at public transportation service is sometimes caused by driver’s healthy condition.
By analyzing driving record may detect rough driving which are potential risk of accident.
Summary
Images
802.11ah link

## Slide 17: Summary
Use cases of the IEEE 802.11ah considered by AHPC are introduced.
AHPC is still calling for additional use cases.

## Slide 18: References
https://www.11ahpc.org/pdf/usecase-eng.pdf