## Slide 1: IEEE 802.19.3 Sub-1 GHz Band System Overview
Date: 2019-07-15
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
IEEE 802.19.3 TG has proposed table of contents for Recommended Practice
This document intends to propose the Sub-1 GHz frequency band system overview
  IEEE 802.11ah
  IEEE 802.15.4g
  LoRa
  SigFox
  IEEE 802.15.4w (underdevelopment)

## Slide 3: Channel width
802.11ah
  1MHz/2MHz/4MHz/8MHz/16MHx
802.15.4g
  200kHz/400kHz/600kH/800kHz/1200kHz
LoRa
  125kHz/250kHz/500kHz
SigFox
  100Hz/600Hz/1.2kHz
802.15.4w
  2.3 kHz – 19 kHz

## Slide 4: PHY
802.11ah
  OFDM
802.15.4g
  MR-FSK/MR-OFDM/MR-O-QPSK
LoRa
  CSS/FSK
SigFox
  BPSK (uplink)/GFSK (downlink)
802.15.4w
  GMSK

## Slide 5: PHY Data Rate
802.11ah
  150 kbps - 78 Mbps (for 1 spatial stream) or 346 Mbps (for 4 spatial streams)
802.15.4g
  6.25 kbps – 2.4 Mbps
LoRa
  250 bps – 50 kbps
SigFox
  100 bps – 600 bps
802.15.4w
  600 bps – 9 kbps (instantaneous)
  60 – 900 bps (effective rate)

## Slide 6: Region Dependent Spectrum Allocation
802.11ah
  902-928 MHz band in United States
  863-868 MHz band in Europe
  915-928 MHz band in Japan
802.15.4g
  902-928 MHz in United States
  169 MHz and 863-870MHz in Europe
  920-928 MHz in Japan
LoRa
  902-928 MHz in United States
  863-870 MHz in Europe
  920-923 MHz in Japan
SigFox
  915 MHz in United States
  868 MHz in Europe
  433 MHz in Asia

## Slide 7: Region Dependent Spectrum Allocation
802.15.4w
  902-928 MHz in United States
  169 MHz and 863-870MHz in Europe
  920-928 MHz in Japan

## Slide 8: Region Dependent Maximum Transmission Power
802.11ah
  1000 mW in United States
  25.12 mW in Europe
  250 mW in Japan
802.15.4g
  1000 mW in United States
  25 mW in Europe
  250 mW in Japan
LoRa
  1000 mW for some regions
  25 mW uplink in Europe, 500 mW downlink in Europe

## Slide 9: Region Dependent Maximum Transmission Power
SigFox
  25 mW uplink power in Europe
  158 mW uplink in United States
  500 mW downlink power in Europe
  1000 mW downlink power in United States
802.15.4w
  25 mW for typical use case
  Maximum 500 mW in Europe

## Slide 10: Nominal Communication Range
802.11ah
  1 km
802.15.4g
  1 km
LoRa
  20km
SigFox
  50 km
802.15.4w
  51 km

## Slide 11: Channel Access
802.11ah
  CSMA/CA
  TDMA
802.15.4g
  CSMA/CA
  TDMA
  ALOHA
LoRa
  TDMA
  ALOHA
SigFox
  ALOHA
802.15.4w
  TDMA
  ALOHA

## Slide 12: Coexistence Mechanism
802.11ah
  ED based inter-system coexistence
802.15.4g
  ED based inter-system coexistence if CCA Mode 1 or CCA Mode 3 with ED is applied. Otherwise, no ED based inter-system coexistence is provided.
    802.15.4g allows CCA Mode 1, CCA Mode 3 and CCA Mode 4 (ALOHA))
  CSM based intra-system coexistence
LoRa
  No
SigFox
  No
802.15.4w
  Frequency diversity (Channel hopping)
  Time diversity

## Slide 13: Network Topology
802.11ah
  Star
  Tree
802.15.4g
  Star
  Mesh
LoRa
  Star
SigFox
  Star
802.15.4w
  Star
  Mesh

## Slide 14: Use Scenarios
802.11ah
  Smart city
  TBD
802.15.4g
  Smart utility
  TBD

## Slide 15: Use Scenarios
LoRa
  Smart city
    Smart lighting
    Air quality and pollution monitoring
    Smart parking and vehicle management
    Facilities and infrastructure management
    Fire detection and management
    Waste management
  Industrial
    Radiation and leak detection
    Smart sensor technology
    Item location and tracking
    Shipping and transportation

## Slide 16: Use Scenarios
SigFox
  Smart city
  Smart building & Security
  Smart lighting
  Service & vehicle monitoring
  Road & structure sensors
  Agriculture and environment
  Public transport
802.15.4w
  Applications for LoRa and SigFox