## Slide 1: Coexistence Architecture Recommended for 802.11ah and 802.15.4g in Sub-1 GHz Band
Date: 2019-08-15
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
This document aims to propose coexistence architecture for 802.11ah and 802.15.4g
The architecture classifies coexistence mechanisms based on
  Network coordination
  Level of coexistence operation
This document is intended for Section 9 of the Recommended Practice being developed by 802.19.3 TG
  Based on Table of Content in document #19-19/0035r3

## Slide 3: Centralized Coexistence Operation
Assume a coordinator can communicate with both 802.11ah network and 802.15.4g network
  Collect information from networks
  Analyze information
  Make decision
Coordinator makes decision on coexistence operation
Coordinator instructs networks to perform coexistence operations
  Channel switching
  Beamforming
  RAW scheduling
  Superframe structuring
  Etc.
Coordinator can instruct a network or a group of devices or a single device to perform a coexistence operation

## Slide 4: Cooperated/Collaborated Coexistence Operation
Assume a coordinator can communicate with both 802.11ah network and 802.15.4g network
  Collect information from networks
  Relay information between networks so that 802.11ah network is aware of 802.15.4g network and 802.15.4g network is aware of 802.11ah network
Coexistence operation is performed spontaneously by a network without instruction from coordinator
However, network perform cooperated (or collaborated) operation in the sense of
  A network informs other network about coexistence operation performed, e.g., channel switching and RAW scheduling
  Other network then makes decision based on information received

## Slide 5: Distributed Network Coexistence Operation
Network level coexistence operation performed independently by a network
  There is no coordinator
  A network is aware of external interference, but is not aware of source of the interference
  All devices, i.e., STAs or nodes, in a network perform same operation
802.11ah network can perform following coexistence operations
  Channel switching
  RAW scheduling
  Beamforming
802.15.4g network can perform following coexistence operations
  Channel switching
  Superframe structuring
To decide an operation, a network can use all information available

## Slide 6: Distributed Device Coexistence Operation
Device level coexistence operation performed independently by a STA/Node
  There might be a coordinator
  A network might be aware of other network
802.11ah STA can perform following coexistence operations
  Transmission deferring such as prediction based transmission control
  α-Fairness ED-CCA
  Q-Learning based backoff
  Etc.
802.15.4g network can perform following coexistence operations
  Change backoff parameters
  Change packet size
  Etc.
To decide an operation, a device can use all information available
  Its own observations, e.g., ED detection ratio
  Information received from network, e.g., network performance of other network

## Slide 7: Coexistence Architecture Based On Network Coordination
Sub-1 GHz Band Coexistence
Distributed network coexistence
Distributed device coexistence
Coordinated coexistence
Distributed coexistence
Centralized coexistence
Cooperated network coexistence
Coexistence can be performed with or without coordination among involved networks
  Coordinated coexistence requires coordination among networks, i.e., the involved networks work collaboratively to mitigate interference
  Distributed coexistence does not need any coordination among from networks, i.e., each network/device performs coexistence operation independently

## Slide 8: Coordinated Coexistence Architecture
Coordinator coordinates networks for coexistence
Key advantages
  Global information
  Global optimization
Key disadvantages
  Coordinator availability
  Information acquisition
  Scalability
  Cost
802.11ah network
802.15.4gnetwork
Coordinator

## Slide 9: Distributed Coexistence Architecture
Key advantages
  Easy to implement
  Low communication overhead
  Flexibility
Key disadvantages
  Local information based
  Local solution
802.11ah network
802.15.4gnetwork

## Slide 10: Coexistence Architecture Based On Level of Operation
Sub-1 GHz Band Coexistence
Distributed network coexistence
Distributed device coexistence
Network level coexistence
Device level coexistence
Centralized coexistence
Cooperated network coexistence
Coexistence can be performed at network level or device level
  Network level coexistence requires all devices in a network to perform same coexistence operation, e.g., channel switching
  Device level coexistence does not need all devices in a network to perform same coexistence operation. Coexistence operation is perform by a group of devices or a single device, e.g., deferring transmission

## Slide 11: Select Coexistence Methods by 802.11ah
There are multiple coexistence methods available for an 802.11ah network/device
  Coexistence operation selection is important for an 802.11ah network/device
  This figure shows a way for selection
Coexistence Operation
Switch channel
Is channel hopping a feasible solution
Yes
Select coexistence method
No
RAW scheduling
Beam
forming
Defer TX
α-fair ED-CCA
Q-Learning backoff
Change frame size
Network support channel hopping & a better channel is available
Need network assistance
Do not need network assistance
Change PHY rate

## Slide 12: Select Coexistence Operation by 802.15.4g
There are multiple coexistence methods available for an 802.15.4g network/device
  Coexistence operation selection is also important for an 802.15.4g network/device
  This figure shows a way for selection
Coexistence Operation
Switch channel
Is channel hopping a feasible solution
Yes
Select coexistence method
No
802.11ah RAW coordination
Change CSMA/CA parameter
Change frame size
Network support channel hopping & a better channel is available
Need network assistance
Do not need network assistance
Superframe structuring
Change PHY rate