## Slide 1: Coordinated Coexistence Methods Recommended for 802.11ah and 802.15.4g in Sub-1 GHz Band
Date: 2019-08-28
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
This document aims to propose coordinated coexistence mechanisms for 802.11ah and 802.15.4g in the Sub-1 GHz band
  Centralized
  Cooperated/collaborated
The coordinated coexistence can be considered as a generalization of the 802.15.4g CSM (common signaling mode) mechanism
Coordinated coexistence assumes there is a device, e.g., a gateway or a hybrid device, that can communicate with both 802.11ah network and 802.15.4g network and therefore, can coordinate the coexistence
  802.11ah network acquires existence of 802.15.4g network via coordinator
  802.15.4g network acquires existence of 802.11ah network via coordinator
The methods are intended for Section 8 of the Recommended Practice being developed 802.19.3 TG
  Based on Table of Content in document #19-19/0035r3

## Slide 3: 802.11ah Coexistence Mechanism Overview
802.11ah defines energy detection (ED) based coexistence
  An S1G STA uses energy detection (ED) based CCA with a threshold of –75 dBm per MHz to improve coexistence with other S1G systems
  If a S1G STA detects energy above that threshold on its channel, then the following mechanisms might be used to mitigate interference:
    Change of operating channel
    Sectorized beamforming
    Change the schedule of RAW(s), TWT SP(s), or SST operating channels
    Defer transmission for a particular interval
These features can be applied to network or device
  Features 1), 2) and 3) are suitable for network
    E.g., if a STA changes operating channel by itself, it might disconnect itself from the associated network unless it intends to join a new network.
    RAWs are schedule by AP
  Features 2) and 4) are suitable for individual STA
In addition, other coexistence methods can also be applied

## Slide 4: 802.15.4g Coexistence Mechanism Overview
802.15.4g defines GSM for coexistence among devices that use different 802.15.4g PHYs
802.15.4g does not specifically address coexistence with non-802.15.4 systems
If ED is used, ED based coexistence is implicitly performed.
  802.15.4g operation return busy status if the detected energy level is above the specified ED threshold
If ED is not used, alternative coexistence methods need to be specified
Weather or not ED is enabled, other coexistence methods can also be performed, e.g.,
  Change backoff parameters
  Change frame size
  Structuring superframe

## Slide 5: Information Exchange for Coordinated Coexistence
802.11ah AP and 802.15.4g PANC shall report their operating channel information to coordinator
  Report updated channel information after channel switching
802.11ah and 802.15.4g PANC may report their traffic information to coordinator
  Report latest traffic if traffic information changes
802.11ah AP and 802.15.4g PANC may report their network information to coordinator
  Node density, node deployment, location, etc.
Coordinator may evaluate channels (or frequency bands) based on collected information
  Send information to 802.11ah APs and 802.15.4g PANCs

## Slide 6: Centralized Coexistence
Coordinator manages networks for coexistence
Coordinator can send a coexistence command to a network, a group of devices or a single device
  Network/device performs command from coordinator
Coexistence operations
  Channel hopping for a network
  RAW scheduling
  Superframe structuring
  Beamforming
  Change frame size
  TX delay
  Etc.
802.11ah network
802.15.4gnetwork
Coordinator

## Slide 7: Cooperated/Collaborated System
Document #19-19/0020r1 proposes an collaborated coexistence framework
This document summarizes a few coexistence methods of 802.11ah and 802.15.4g networks in cooperated/collaborate systems
Source: “IEEE 802.15-14-0555-13-004s-tg4s-technical-guidance-document.”, March 2016

## Slide 8: Cooperated Coexistence - Channel hopping by 802.11ah
802.11ah STAs report their observations to the associated AP, e.g.,
  ED detection ratio, i.e., number of ED detection above ED threshold in a time period, or
  Packet delivery ratio or
  Packet latency
802.11ah AP makes assessment based on STA’s reports and decides if channel switching is necessary
If channel switching is not needed, nothing to be done
If channel switching is needed, 802.11ah AP uses channel utilization information from coordinator to assess the feasibility
  If yes, i.e., a better channel is available, 802.11ah AP instructs its network for channel switching
  802.11ah AP will also inform the coordinator for the channel change after channel switching is completed
  Coordinator will then inform 802.15.4g network about channel switching so that 802.15.4g network may stay on current channel

## Slide 9: Cooperated Coexistence - Channel Hopping by 802.15.4g
Channel hopping by 802.15.4g network
  If ED is used in CSMA/CA, then similar approach as for 82.11ah network can applied by 802.15.4g network for coexistence
  If ED is not used, 802.15.4g network can use data packet delivery ratio collected nodes to make decision for channel hopping
If decision is YES, 802.15.4g PANC informs its network and coordinator for channel hopping

## Slide 10: Cooperated Coexistence When Channel hopping Is Not Feasible
Due to spectrum allocation constraint, channel hopping is not always a feasible solution
  In this case, 802.11ah network and 802.15.4g network are forced to share the spectrum
  This is real coexistence
Coexistence methods
  Cooperated RAW
    802.11ah RAW combined with 802.15.4g superframe structuring
  802.11ah sectorized beamforming

## Slide 11: Cooperated Coexistence – Cooperated RAW
802.11ah network allocates dedicated RAW for 802.15.4g network
  These RAWs are not assigned to any 802.11ah STA, so 802.11ah devices don’t transmit any packets
  802.11ah network informs 802.15.4g network via coordinator about RAW allocation
  802.15.4g network plans the usage of RAW
For beacon enabled 802.15.4g network, 802.11ah AP allocates two RAWs for 802.15.4g network
For non-beacon enabled network, 802.11ah AP may only schedule one RAW for 802.15.4g network

## Slide 12: Cooperated Coexistence – Sectorized Beamforming by 802.11ah
For 802.11ah network capable of beamforming
  802.11ah AP can determine the deployment of 802.15.4g devices based on information received from coordinator
  Instructs 802.11ah STAs to form beam away from 802.15.4g devices
802.11ah network
802.15.4gnetwork
802.11ah beam direction