## Slide 1: Distributed Coexistence Methods Recommended for 802.11ah and 802.15.4g in Sub-1 GHz Band
Date: 2019-08-28
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Introduction
This document aims to propose distributed coexistence mechanisms for 802.11ah and 802.15.4g
This document assumes that no coordination between 802.11ah network and 802.15.4g network, each network or device performs distributed coexistence control
  Network level
  Device level, with or without network assistance
These methods are intended for Section 8 of the Recommended Practice being developed 802.19.3 TG
  Based on Table of Content in document #19-19/0035r3

## Slide 3: How To Identify Existence of Other Network
Without a coordinator, it is not obvious for an 802.11ah network/802.15.4g network to be aware of existence of 802.15.4g network/802.11ah network
However, using energy detection, an 802.11ah STA/802.15.4g node can detect if a non-802.11ah/non-802.15.4g system exist
There might be other method for this purpose, e.g.,
  The ratio of channel occupancy time by its own network and total channel busy time
  Input from network
  ???

## Slide 4: Channel Switching by 802.11ah or 802.15.4g Network
802.11ah STAs/802.15.4g nodes report their observation to AP/PANC, e.g.,
  Number of ED detection above ED threshold in a time period (for 802.15.4g, if ED is employed)
  Packet delivery ratio (# of ACK/# of TX attempts)
  Packet latency (from TX process start time to ACK receiving time)
802.11ah AP/802.15.4g PANC makes assessment based on reports and decides if channel switching is necessary
If decision is YES, 802.11ah AP/802.15.4g PANC scans other channels to assess the feasibility
  If better channel is available, 802.11ah AP/802.15.4g PANC informs its network for channel switching
802.11ah STAs/802.15.4g nodes may also do channel scanning and report information to 802.11ah AP/802.15.4g PANC

## Slide 5: Distributed Beamforming and TX Delay by 802.11ah
Sectorized beamforming
  An 802.11ah STA can perform this operation if it knows 802.15.4g network deployment
Defer transmission for a particular interval
  This is the most practical method to be executed by individual 802.11ah STA
  If an 802.11ah STA is certain existence of non-802.11ah system, it can use this approach for coexistence control.

## Slide 6: α-Fairness based ED-CCA by 802.11ah
α-Fairness based ED-CCA was presented in document #19-18/0027r1
Mitigate interference by higher ED threshold of 802.11ah
If the energy level detected by 802.11ah falls in [802.15.4g Receiver Sensitivity, 802.11ah ED Threshold]
  Should 802.11ah ED-CCA report idle or busy?
    From 802.15.4g perspective, it should report busy if the energy source is 802.15.4g and reports idle otherwise
  Problem is that 802.11ah may not be able to identify the source of the energy, which could be
    802.15.4g node, far away 802.11an STA or other device
α-Fairness based ED-CCA
  If the detected energy level is within [802.15.4g Receiver Sensitivity, 802.11ah ED Threshold], 802.11ah ED-CCA reports channel status based on a probability generated by the α-Fairness technique.

## Slide 7: Q-Learning based CSMA/CA by 802.11ah
Q-Learning based CSMA/CA was presented in document #19-18/0027r1
Mitigate interference by faster CSMA/CA of 802.11ah
  When backoff counter (BC) reaches to 0 and 802.11ah ED-CCA reports idle channel, should 802.11ah transmit or not?
Problem
  802.11ah does not know if an 802.15.4g transmission process is in progress
  In addition, the channel is idle according to 802.11ah standard
Q-Learning based CSMA/CA
    If BC > 0 or ED-CCA reports busy channel, the backoff process continues as specified by 802.11ah
    If BC = 0 and ED-CCA reports idle channel, apply Q-Learning to make decision, i.e, transmit or re-backoff or defer some time

## Slide 8: Prediction Based Transmission Control by 802.11ah
The prediction based transmission control was presented in document #19-18/0085r2
802.11ah predicts upcoming 802.15.4g transmission time and suspends its transmission within a potential time period to avoid the predicted 802.15.4g transmission
Each 802.11ah device
  Records all detected transmission starting time
  Delete the time corresponding to successful 802.11ah transmissions and collided 802.11ah transmissions
  Store transmission time of 802.15.4g transmission
Using recorded 802.15.4g transmission time history to predict the upcoming 802.15.4g transmission time
Predicted Time
Time
802.11ah transmission suspension period
Predicted 802.15.4g transmission time
Current time

## Slide 9: Distributed Coexistence by 802.15.4g
Change backoff parameters
Change transmission power
Change frame size
Channel hopping
???