## Slide 1: EU Bands
Date: 2019-09-17
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Introduction into 868MHz regulation in Europe
868MHz allocations in Germany
Typical LPWAN frequencies
868MHz observations

## Slide 3: 868MHz Regulation in Europe
ETSI EN 300 220-2 defines list of bands that are EU-wide harmonized and other non EU wide harmonized bands [1]
  Harmonized: Mainly related to 863-870 MHz
  Non-harmonized (only defined in some European countries): Defines additional bands, e.g. 870-876MHz and around 915MHz
Additional bands not part of EN 300 220-2 can also be defined by individual states (see later slides), e.g. [2] for Germany

## Slide 4: General Remarks
The 868MHz band is a “Short Range” Devices (SRD) band and not an ISM band
Strict regulation wrt. transmit power, duty cycle or other signal properties
Typical limitations are 25mW EIRP transmit power and 1% duty cycle, few bands allow up to 500mW EIRP
The latest revision ETSI EN 300 220-2 also introduces polite spectrum access [1], which enables higher duty cycles in case of frequency hopping (2.7% per 200kHz portion)

## Slide 5: 868MHz Allocations in Germany
%-value gives max. duty cycle
AP: Access Point

## Slide 6: Low Power Wide Area Networks in Europe
LoRa (“The Things Network”): European frequency plan [3] uses uplink frequencies between 867.1MHz and 868.5MHz and downlink frequency 869.525MHz (high power band) with 125kHz bandwidth
SigFox: 200kHz of bandwidth between 868MHz and 869MHz [4]
802.15.4w: Would also typically use the frequencies between 868 and 870MHz

## Slide 7: 868MHz Observations
RFID and the 500mW meter band are co-located on the very same frequencies with only 200kHz bandwidth
Coexistence problems likely in scenarios with dense RFID usage (e.g. airports)
RFID / 500mW meter band and 802.11ah band are partly co-located
Lower frequency band more suitable for 802.11ah, but high 802.11ah bandwidth may limit problem in higher band
LPWANs typically use the frequencies above 868MHz and will therefore not interfere with 802.11ah

## Slide 8: Non-EU Harmonized Frequencies
General interest in additional sub-GHz frequencies for SRD and RFID
  915MHz for globally harmonized UHF RFID systems (simplified antennas with higher gain)
  870-876MHz and 915MHz for additional frequency resources
BUT: Frequencies are currently used in many states (e.g. Germany)
  ER-GSM (rail GSM)
  Defense/governmental systems

## Slide 9: Summary
868MHz SRD bands are strictly regulated in Europe
Some channels overlap with RFID and high power metering applications  potential co-existence problems
Typical LPWAN frequencies are not affected by RFID or other high power applications
Additional non EU harmonized frequencies exist, but harmonization over Europe is not achieved yet

## Slide 10: References
ETSI EN 300 220-2 (V3.2.1): Short Range Devices (SRD) operating in the frequency range 25 MHz to 1 000 MHz; Part 2: Harmonised Standard for access to radio spectrum for non specific radio equipment, June 2018, https://www.etsi.org/deliver/etsi_en/300200_300299/30022002/03.02.01_60/en_30022002v030201p.pdf
Bundesnetzagentur, Allgemeinzuteilung SRD, Vfg 5/2018, https://www.bundesnetzagentur.de/SharedDocs/Downloads/DE/Sachgebiete/Telekommunikation/Unternehmen_Institutionen/Frequenzen/Allgemeinzuteilungen/2018_05_SRD_pdf.pdf;jsessionid=BC6DFCDAA1CE08766B484CE403B9766B?__blob=publicationFile&v=2
“The Things Network” frequency plan, https://www.thethingsnetwork.org/docs/lorawan/frequency-plans.html
SIGFOX Radio Technology Keypoints, https://www.sigfox.com/en/sigfox-iot-radio-technology