## Slide 1: Contribution for Comment Resolution, P802.19.3 Initial Ballot: CID 271590, 271587
Date: 2020-10-28
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
Proposed resolution for Comment # I-20 (CID: 271590) and I17 (CID: 271587) on 19-20-0036-02.

## Slide 3: Proposed resolution: CID 271590
Deposition Status: Rejected
Deposition Detail:
  Based on Table 20-7 on IEEE 802.15.4-2015, no necessary to change sentence. On the other hand, revise CID 271587 for consistency of notation.

## Slide 4: Proposed resolution: CID 271587
Deposition Status: Revised
Deposition Detail:
  As for JP regulation, ARIB STD-T108 defines 915.9 - 929.7 MHz for both 200 kHz and 100kHz bandwidth. (916 - 928 MHz is written by center frequency for 200 kHz bandwidth for both 1mW and 20mW transmission power). However, the channel plan for IEEE 802.11ah (1MHz) has not been decided yet in Japan.
  For consistency of notation, following sentences are proposed for P 4, Section 4.2 Line 31: “Frequency band allocation is region dependent, e.g., 902-928 MHz band in United States, 863-868 MHz band in Europe and 915 - 928 MHz (TBD) in Japan.”