## Slide 1: Ideas and Discussions on IEEE 802.19.3a Recommended Practice
Date: 2025-03-10
Authors:
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Abstract
This document presents some ideas to IEEE 802.19 Working Group for coexistence recommendation updates of IEEE 802.15.4 and IEEE 802.11 systems operating in Sub-1 GHz (S1G) frequency bands.

## Slide 3: CSMA Differences in IEEE 802.15.4 and IEEE 802.11
IEEE 802.11 backoff is much faster than IEEE 802.15.4 backoff
Backoff suspension
  IEEE 802.11 applies backoff suspension: sense channel in each backoff time slot and suspends backoff counter if channel is busy
  Conventional IEEE 802.15.4 backoff does not sense channel during backoff periods and sense channel after backoff process completes
Immediate channel access
  IEEE 802.11 CSMA allows immediate channel access
    Transmit if channel idle for more than DIFS time
  IEEE 802.15.4 CSMA does not allow immediate channel access
    Performs random backoff no matter how long channel has been idle
IEEE 802.11ah Parameter | Value
CCA Time | <40 µs
Slot Time | 52 µs
Turnaround Time | <5 µs
DIFS (minimum Idle time) | 264 µs
IEEE 802.15.4g Parameter | Value
phyCCADuration | 140 µs
UnitBackoffPeriod | 1140 µs
Turnaround Time | 1000 µs
Minimum idle time | 1000 µs
CCA
CCA
CCA
…
…
CCA

## Slide 4: Some Other Differences in IEEE 802.15.4 and IEEE 802.11
IEEE 802.11ah Parameter | Value
ED Threshold | -75dbm
Carrier Sense Level | -95dbm
RX Sensitivity | -95dbm
Channel Width | 1MHz
PHY Data Rate | 300kbps
PHY Type | OFDM
IEEE 802.15.4g Parameter | Value
ED Threshold | -78dbm
Carrier Sense Level | -88dbm
RX Sensitivity | -88dbm
Channel Width | 200kHz
PHY Data Rate | 100kbps
PHY Types | FSK OFDM O-QPSK
Key IEEE 802.11 impact on IEEE 802.15.4
  Reliability, i.e., data packet discard due to backoff failure
  One IEEE 802.11 network can interfere multiple IEEE 802.15.4 networks
Key IEEE 802.15.4 impact on IEEE 802.11
  Latency due to
    Longer transmission time of 802.15.4
    Backoff suspension of 802.11

## Slide 5: Illustration of IEEE 802.15.4 Backoff Failure
Other
Devices
Data Tx
Data Tx
Data Tx
Backoff #1
Backoff #2
Backoff #3
Backoff #NBmax
CCA
・・・
802.15.4g
Device
CCA
Busy
CCA
Busy
CCA
Busy
CCA
Busy
1
2
3
NBmax
No of Backoffs (NB)
Status
Retry
Retry
Failure
Time
Time
Retry
Tx Request
CCA
CCA
CCA
Other Devices (802.11/802.15.4)
Observing
802.15.4 Device

## Slide 6: Adoption of Backoff Suspension in IEEE 802.15.4
IEEE 802.15.4 CSMA mechanism was designed for fair channel access among IEEE 802.15.4 devices
  Not well considering coexistence with more aggressive interfering devices such as IEEE 802.11 devices
Suspendable CSMA for IEEE 802.15.4 was proposed in 2023 to achieve better coexistence performance while competing for channel access with more aggressive interfering devices
  See reference [1] for details
The Suspendable CSMA has been accepted by IEEE 802.15 Working Group and included in IEEE 802.15.4-2024
What are expected impact on coexistence
  IEEE 802.15.4 reliability will be improved
    Less packet discard due to backoff failure
  IEEE 802.15.4 latency will be increased
    Longer backoff time due to backoff suspession
IEEE 802.11 performance will be impacted, but should not a lot
  See document 19-25/0006r0 for results

## Slide 7: Suspendable Non-Slotted CSMA/CA for IEEE 802.15.4
IEEE 802.15.4 Non-Slotted CSMA-CA
Suspendable Non-Slotted CSMA/CA for IEEE 802.15.4
IEEE 802.15.4 Slotted CSMA-CA
NB=0, BT = 0
BE=macMinBe
Channel idle?
NUBP = random (2BE-1) unit backoff periods
Perform active CCA within a unit backoff period
Y
NUBP = NUBP-1
NUBP = 0?
Y
Perform CCA
Channel idle?
Y
Suspendable CSMA-CA
Success
N
NB=NB+1
BE=min(BE+1, macMaxBe)
NB > macMaxCSMA Backoffs?
Y
Failure
N
N
Delay to next unit backoff period
N
Non-slotted
suspendable backoff
NUBP = Number of Unit Backoff Periods
BT=BT+aUnitBackoffPeriod
BT > MaxBT?
N
Y
MaxBT= macSuspendedCsmaMaxTime
BT = Backoff Time

## Slide 8: Suspendable Slotted CSMA/CA for IEEE 802.15.4
Suspendable Slotted CSMA/CA for IEEE 802.15.4
Channel idle?
NUBP = random (2BE-1) unit backoff periods
Perform CCA on backoff period boundary
Y
NUBP = NUBP-1
NUBP =0?
Perform CCA on backoff
period boundary
Channel idle?
Y
Success
N
NB=NB+1, CW=CW0
BE=min(BE+1, macMaxBE)
NB > macMaxCSMA Backoffs?
Y
Failure
N
N
Locate backoff period boundary
N
Slotted Suspendable Backoff
BT=BT+aUnitBackoffPeriod
BT > MaxBT?
CW = CW-1
CW=0?
N
NB=0, BT=0
CW=CW0
Slotted suspendable
CSMA-CA
BE=macMinBe
Battery Life Extension?
BE=min{2, macMinBe}
Locate backoff period boundary
N
Y
Y
N
Y
NUBP = Number of Unit Backoff Periods
BT = Backoff Time
MaxBT = macSuspendedCsmaMaxTime

## Slide 9: Ideas on Recommendation Updates in IEEE 802.19.3a
Assumptions on IEEE 802.15.4 system and IEEE 802.11 system coexistence
  IEEE 802.11 system is less affected since it is more aggressive in channel access contention
  IEEE 802.15.4 system is more affected due to its low-power low-rate functionality
Objectives (recommendations) of IEEE 802.19.3a are to improve IEEE 802.15.4 system performance
Recommendation on backoff suspension implementation in IEEE 802.15.4 systems coexisting with more aggressive systems
  Apply backoff suspension in IEEE 802.15.4 system if reliability is focus
  Don’t apply backoff suspension in IEEE 802.15.4 system if latency is focus
PHY combinations under consideration, see document 19-25/0006r0

## Slide 10: Ideas on Recommendation Updates in IEEE 802.19.3a
Case-1: IEEE 802.15.4g-FSK (400 kHz channel) and IEEE 802.11ah (1 MHz channel)
  IEEE 802.19.3 specifies recommendations without backoff suspension in IEEE 802.15.4g
  Does TG3a need to update recommendations with backoff suspension in IEEE 802.15.4g?
Case-2: IEEE 802.15.4g-FSK (400 kHz channel) and IEEE 802.11ah (4 MHz channel)
  Does TG3a need recommendations without backoff suspension in IEEE 802.15.4g?
  Does TG3a need recommendations with backoff suspension in IEEE 802.15.4g?
Case-3: IEEE 802.15.4g-OFDM (400 kHz channel) and IEEE 802.11ah (1 MHz channel)
  Does TG3a need recommendations without backoff suspension in IEEE 802.15.4g?
  Does TG3a need recommendations with backoff suspension in IEEE 802.15.4g?

## Slide 11: Ideas on Recommendation Updates in IEEE 802.19.3a
Case-4: IEEE 802.15.4g-OFDM (400 kHz channel) and IEEE 802.11ah (4 MHz channel)
  Does TG3a need recommendations without backoff suspension in IEEE 802.15.4g?
  Does TG3a need recommendations with backoff suspension in IEEE 802.15.4g?
Is there any amendment to IEEE 802.11 CSMA that can affect its coexistence behavior?
  If yes, should TG3a consider it?
Recommendations based on measurement results are valuable
  The lack of real systems presents challenges
Therefore, TG3a will mostly rely on simulation results, a lot of simulations are needed based on number of nodes, offered network load, network topology, etc.
  Should TG3a provide some guideline and strategy?

## Slide 12
IEEE Std 802.19.3-2021 specifies coexistence recommendations for IEEE 802.15.4 and IEEE 802.11 systems operating on Sub-1 GHz frequency bands
Since the publication of IEEE Std 802.19.3, both IEEE Std 802.15.4 and IEEE Std 802.11 have been amended (updated)
Some amendments (updates) can impact coexistence behavior
  E.g., IEEE Std 802.15.4-2024 adopts backoff suspension, which can affect IEEE 802.15.4 system coexistence behavior
This document present some ideas on coexistence recommendations for IEEE 802.19.3a Recommended Practice
Summary

## Slide 13: References
[1] Yukimasa Nagai, Jianlin Guo, Takenori Sumi, Kieran Parsons, Philip Orlik, Benjamin A. Rolfe and Pu Wang, Improve IEEE 802.15.4 Network Reliability by Suspendable CSMA/CA, IEEE WCNC 2024
[2] IEEE Std 802.19.3
[3] Document 19-25/0006r0
[4] Document 19-24/0042r0
[5] Document 19-24/0018r0
[6] Document 19-18/0039r1