## Slide 1
1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-10-00xx-00-sec
Title: Summary of Proposed Security Solutions
Date Submitted: March 12, 2010
Present at IEEE 802.21 March meeting
Authors: Lily Chen (NIST), Rafa Marín-López (University of Murcia), Subir Das (Telcordia Technologies), Fernando Bernal (University of Murcia), Karen Randall (Randall Consulting)
Abstract: This document summarizes the proposed solutions based on the proposals in responding 802.21a “call for proposals”.
1

## Slide 2
2
2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Background
3
The proposals received in responding of “802.21a call for proposals” have been discussed in previous 21a meetings.
The proposals are based on different assumptions and with some undefined terminologies.
In order to consider the different proposed solutions based on consistent terminologies and clear assumptions, document #41 summarized them as three main approaches.
This document decouples work item 1 and work item 2 options to understand the issues more clearly.
Based on the analysis and the Feb. 16 conference call discussion, this document summarizes the options for TGa to discuss.

## Slide 4
Summary of Proposed Solutions - Work Item 2
Work Item 2 – Protect MIH Service
I. Non MIH specific Protection
III. EAP –Authentication and Key establishment
1.Protect through IPsec
3.Protect through media specific L2 protocol e.g. 802.11
1.Protect at MIH layer
II. Protect through (D)TLS – (D) TLS over MIH
2.Protect through TLS
MIH is carried over L3
MIH is carried over L2
MIH Specific protection

## Slide 5
Work Item 2 – Option I.1: Protection through IPsec
MIH is carried over L3 – IPsec.
  IP packets between MN and PoS are protected through IPsec. The IPsec security associations may be established through IKE. MN and PoS are considered as two IP nodes.
Pros: no change to any existing protocols.
Cons: protection is not MIH specific.
Possible issue: IKE to set up may heavy weight.
21a: Allow the option
MN
PoS
IPsec
MIH
MIH over L3

## Slide 6
Work Item 2 – Option I.2: Protection through TLS
MIH is carried over L3 – TLS
  MIH messages between MN and PoS are protected through TLS. The credential used for authentication is either PSK or Certificate
Pros: no change to any existing protocols.
Cons: not MIH specific.
Possible issue: May need new port assignment
21a: Allow the option
MN
PoS
TLS
MIH
MIH over L3

## Slide 7
7
Work Item 2 – Option I.3: Protection by Transport Protocols (L2)
MIH is carried over L2 - Media Specific.
  Between MN and PoA, the protection is media specific, e.g. 802.11. However, specific PoA may not be PoS. L2’ may be a wired layer 2. The protections are only applied on L2, not L2’
Pros: no change to any existing protocols.
Cons: the protection may not be end to end.
Possible issue: security protection is not MIH specific.
21a: Allow the option
MN
PoS
L2 Protection
L2’
PoA
MIH over L2
MIH

## Slide 8
Work Item 2 – Option II: (D)TLS
MN
PoS
(D)TLS
MIH
MN and PoS establish a (D)TLS session
  It can be public key based or use a key established through other manner, say EAP or PSK.
MIH is protected through TLS.
Pros: No dependency in IETF
Cons: need to define new header in MIH and primitives
Possible issue: TLS implementation need to be updated since original MIH packets need to be treated as application data (?)
21a: Define the procedure
MIH
New MIH
MIHS header
TLS TLV
TLS record type =application data
MIH header
MIH Data
(D)TLS
MIH

## Slide 9
Work Item 2 – Option III: EAP
MN executes a service authentication through EAP. The EAP messages between MN and PoS can be carried over MIH or other protocols.
MIH is protected at MIH layer.
Pros: MIH specific protection.
Cons: Add security to MIH, change MIH messages.
Possible issue: Need service authentication credentials and authentication servers.
21a: Define new protected MIH messages.
MN
PoS
Service EAP
Protected MIH
Service AS
MSK
SMIH header
MIH Data
Encrypted
MIC

## Slide 10
Summary of Proposed Solutions - Work Item 1
Work Item 1 – Assist Secure Fast Handover
A. EAP – Over MIH between MN and PoS
B. EAP – Bundle with III in work item 2
MSA is the authenticator (L2 frame over MIH)
No new key hierarchy
New key hierarchy

## Slide 11
Work Item 1 – Option A: Proactive Authentication Through EAP - MSA is the Authenticator
Between MN and PoS, EAP is carried as L2 frames over MIH.
Pros: use original media specific key hierarchy, no change to access authentication required by MSA.
Cons: Need PoS function to
  forward proactive authentication to MSA;
  receive messages from MSA then put in MIH message and forward to MN.
Possible issue: It is not clear what issue we may have for carrying L2 frames over MIH.
21a: Identify MIH messages to carry L2 frames.
MN
PoS
Proactive EAP
MIH
Media AS
MSK/rMSK
MSA
Proactive EAP
Not 21
Proactive EAP
Not 21
New Function

## Slide 12
Work Item 1 – Option B: Bundle to Service Authentication III
Bundle media authentication with service authentication. The EAP messages between MN and PoS can be carried over MIH or other protocols.
Pros: an integrated solution.
Cons: a new key hierarchy from media point of view.
Possible issue: It requires a relationship between service AS and each media AS. It is a new trust model. On the other hand, some deployment may combine media and service access authentication together.
21a: Identify MIH messages.
MN
PoS
Service EAP
Protected MIH
Service AS
PAIK
Media 1 AS
MSA
MS-PMK
MSK or rMSK
MI-PMK
MS-PMK
PAIK
Protected L2 after HO

## Slide 13: Work Item 2 –21a Task Summary and Question
Option I – Discuss pros and cons on each IPsec, TLS, and L2 protection.
Option II – Define MIH messages to carry (D)TLS protected MIH data.
Option III – Two options about service authentication.
  Define EAP over MIH but allowing EAP to be carried by other protocols.
  Do not define the service authentication but assume a key is established between MN and PoS.
  Select supported algorithms and define new MIH header and protected format.

## Slide 14: Work Item 1 –21a Task Summary and Question
Option A – Identify MIH messages to carry L2 frames for proactive authentication. Define additional Primitives, IEs as appropriate for proactive authentications.
Option B – Define key hierarchy. (Do we have to specific Key distribution?)

## Slide 15: Proposal Tracking and Harmonization (1)
59: Use hash tree to provide source authentication for information element (Work item 2) (NIST)
Agreed not to introduce this trust model at the moment in July.
60: Add security related IEs (Work item 1) (NIST)
Need to wait to understand precisely which IEs will be needed,
62: Proactive authentication use ERP (work item 1) and Generic secure SAP to protect MIH (work item 2) (Shubhranshu, Samsung)
63: Authenticator Discovery (Dapeng, China Mobile) (Work item 1)
64: EAP-FRM (Rafa, )
Agreed that the protocol should be submitted to IETF. Introducing new EAP methods is not in the scope of 21a.
65. Packet level authentication (PLA) (Work item 2) 107 is a research paper.
It is unclear what is the packet level. It looks like IP layer. However, introducing a new IPsec is not in the scope of 21a.
66: Proactive authentication, media independent authentication, EAP over MIH (work item 1) and MIH protection (work item 2).

## Slide 16: Proposal Tracking and Harmonization (2)
May2009 | July 2009 | Sept 2009 | Nov 2009 | Jan 2010 | March2010
59 |  |  |  |  | 
60 | 60 |  |  |  | 
62 | 105t | 137 |  |  | 
63 | 103t |  | 169t, 170r |  | 
64 | 107t |  |  |  | 
65 |  |  |  |  | 
66 | 66, 102t | 142r |  |  | 
 |  | 126 | 164 | 164 | 
 |  |  |  |  | 49

## Slide 17: Proposal Tracking and Harmonization (3)
Work Item 1
  Option I – Existing protocols (11u, IETF mipshop)
  Option II – Proposal 62 and 66
  Option III – Proposal 62 and 66
Work Item 2
  Option A – Proposal 60, 62, 63, 66
  Option B – Proposal 60, 66