## Slide 1
1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-10-00xx-00-sec
Title: Protect MIH messages through Transport Protocols
Date Submitted: June 28, 2010
Present at IEEE 802.21 July meeting
Authors: Lily Chen (NIST)
Abstract: This is a presentation for the options discussed in document 21-10-0084-01-sec.
1

## Slide 2
2
2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Background
3
The MIH messages can be transported by a L2 protocol or a L3 protocol.
  802.11u is an instance for the L2 protocols.
  Some L3 scenarios are discussed in RFC 4555.
Document 21-10-0084-01-sec discusses pros and cons for security mechanisms provides through L2, IPsec, and (D)TLS.

## Slide 4
4
Protection by an L2 protocol
When MIH messages are transported through an L2 protocol, it can be protected by the mechanisms included in the L2 protocol.
  In case of using 802.11u, the protection can be TKIP or CCMP as defined in 802.11
Pros:
  No change is required to either L2 protocol or MIH.
  Possibly low overhead
Cons: security protection is not MIH specific.
MN
PoS
L2 Protection
PoA
MIH over L2
MIH

## Slide 5
Protection by IPsec
L3 – IPsec.
  IP packets between MN and PoS are protected through IPsec.
  The IPsec security associations may be established through MOBIKE to accommodate mobile node’s dynamic IP address.
Pros: no change to any existing protocols.
Cons: protection is not MIH specific.
Possible issue: MOBIKE is only defined for tunnel mode, which is less data efficient than transport mode.
MN
PoS
IPsec
MIH
MIH over L3
MOBIKE
IP header (I)
IP Payload
IPsec header
IP header (O)
Protected
IPsec in tunnel mode

## Slide 6
Protection by (D)TLS
L3 – according to RFC4555, MIH messages can be transported over TCP or UDP. TLS or DTLS can be used to protect MIH messages
Pros: no change to MIH protocol as defined in 21 is required.
Cons: protection is not MIH specific.
  But both TLS client and server can use an MIH related identifier.
Possible issue: May need new port assignment.
TLS
MIH
MIH over L3
TLS client
MN
TLS server
PoS
TLS handshake
MIH User
MIHF
TCP/UDP
RFC 4555 Architecture

## Slide 7: Summary
The protection by (D)TLS is the closest to MIH specific. However, the possible issue, new port requirement, indicates dependency on IETF.
The protection by IPsec does not require changes on IPsec. But the impact of restricting to tunnel mode supported by MOBIKE is unclear.
The protection by L2 has low overhead. But it is furthest from MIH layer.

## Slide 8: Motion
Motion to include options to protect MIH messages through transport protocols, together with pros and cons for each of them, as presented in DCN 21-10-0084-01-0sec as part of 802.21a draft specification.