## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-10-0171-00-0sec
Title: Q & A for Discussion
Date Submitted: Aug 17, 2010
Presented at IEEE 802.21a Teleconference Meeting
Authors or Source(s):
Subir Das (Telcordia )
Abstract: This document provides some answers to questions in doc #21-10-170-00-0Sec

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Comments
LLC1: Here it is already pointed which credentials can be used for the mutual authentication. See next comment.
LLC2: Here it is already pointed which credentials can be used for the mutual authentication. See next comment
Answer: There are some redundant texts and agree that it is confusing. We will delete the earlier text (referred in LLC1) and replace the “TLS Identity” heading to “TLS Credential’. See next.

## Slide 4: Comments
LLC3 : Here the mutual authentication credentials are discussed again. Is this different from the previous statement. Especially, EAP is an authentication protocol. Can we recommend to use keys established through EAP to conduct TLS authentication? It is more likely, an TLS can be used as an EAP method. Do we need to recommend the authentication credentials. Can we assume that a MN and PoS have credentials to conduct a TLS authentication.
Answer: How about if we write like this:
TLS Credential
The credential may be based on a pre-shared key or a trusted third party like certificate authority.
We can assume that MN and PoS have credentials to conduct a TLS authentication. This is more true when there is no access control

## Slide 5: Comments
LLC4: I do not think we can recommend TLS or (D) TLS based on whether MIH is reliable. Can we? We keep DTLS as an option since MIH may be carried over UDP. (At least, this is the answered provided at July meeting.)
Answer: We can possibly recommend since IETF RFC recommends to use TCP when reliability is required. For example, ES and CS. Is it not obvious that if TCP is used , one needs to use TLS and (D)TLS for UDP? What we are doing here is simply recommending the fact based on transport choice.

## Slide 6: Comments
LLC5: How to maintain this mapping? Is this in the scope of 21a? Do we need add some more details here?
Answer: A Session TLV is defined to maintain the mapping. We may need to explain this clearly.

## Slide 7: Comments
LLC6: This is very confusing. If an MIH SA is established, then we need to distinguish this SA with SA in EAP MIH authentication case.
Answer: Agree. We will define MIH SA clearly in consultation with Rafa and Fernando. Hopefully, this will also answer the two main questions at the beginning.

## Slide 8: Comments
LLC7: Again, this must be specified. Is this bootstrap TLS key to establish a MIH SA or use the record layer to protect MIH messages?
Answer: When we use MIH SA for (D)TLS based protection, it means that we use TLS record layer to protect MIH PDU carried in TLS TLV. We will clearly this when we define MIH SA.

## Slide 9: Comments
LLC8: Here whether it is TLS which carries MIH or MIH carries TLS?
Answer: MIHS PDU carries a TLS TLV and a MIH PDU carrying MIH registration message is contained in the TLS TLV as a TLS record.

## Slide 10: Comments
LLC9: If this is the handshake, then it uses MIH messages to carry TLS TLV. We assume that the messages (MIH messages) are not protected yet. Do we really need MIHS header or a regular MIH header?
Answer: Without MIHS header (that is the security indication) how the MIHF will know that it needs to treat the packet differently? For example, MIHF with TLS requires some special processing as indicated in the interaction figure at the end of the document.

## Slide 11: Comments
LLC10: Are we assuming that MIH protocol header together with MIH service specific TLVs are application data for TLS? Why do we still need MIHS header?
Answer: Again this is to indicate that the packets are security enabled and the receiving entity needs to process them separately. Otherwise how do we to keep the provision that there may be packets without security and they have to be treated differently. Also we need to keep in mind that we are not changing anything in TLS application in IETF.

## Slide 12: Comments
LLC11: Where are the protected portion?
Answer: The protected portion is TLS TLV.