## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-07-0382-00-0000
Title: Network based Distributed Mobility Approach
Date Submitted: July, 19, 2011
Authors or Source(s):
Antonio de la Oliva, Fabio Giust and Carlos J. Bernardos
Abstract: This document presents an IEEE 802.21 based mechanism to enabled network based distributed mobility management.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Network based Distributed Mobility Management
(A PMIP approach)
Antonio de la Oliva, Fabio Giust, Carlos J. Bernardos

## Slide 4: Overview
Current Mobility Management schemes (e.g., MIPv6, HMIPv6, PMIPv6,…) rely on a centralized entity as cardinal point both for data and control plane
Net-DMM is a proposal to flatten the architecture for network-based mobility
  Remove the central anchor (at least for the data path)
  Keep the mobility operations in the network nodes, e.g., PMIPv6-alike
    The involvement of Mobile Nodes is reduced to movement detection and/or handover control (e.g., with IEEE 802.21)

## Slide 5: Distributed Mobility Management (i)
Mobility operations are spread among edge routers:
  Mobility Anchor and Access Router (MAAR)
    It concentrates the functionalities of an LMA and an MAG defined in PMIPv6
    It is the first IP hop seen by Mobile Nodes (MNs)
    It is the anchor for IP flows started by a MN when attached to it. For these flows:
      It acts as standard router if the MN is still attached
      It establishes a bidirectional tunnel with the MAAR that is currently serving the MN
      Flows do not need to traverse the central node in the core network

## Slide 6: Distributed Mobility Management (ii)
Mobility operations are spread among edge routers:
  Each MAAR advertises a unique prefix to the MN upon attachment
    MN configures a different IPv6 address per each visited MAAR
      This endows edge routers to be anchor (for the prefix pool they handle)
      Mobility support is provided with finer granularity
Two approaches are presented here
  Fully distributed
    with the integration of IEEE 802.21 for handover control
  Partially distributed

## Slide 7: Full distribution
    MAARs learn about the MN’s movements by means of a dedicated control plane (IEEE 802.21 Media Independent Handover Services)
      Upon handover, a MAAR knows where the MN was previously attached and sends a PBU to the old MAAR
  The old MAAR replies with a PBA and a tunnel is established between them to recover the flow
    More than one MAAR might be anchoring ongoing flows, thus the sequence of operations is repeated once per each MAAR

## Slide 8: Full distribution
MAAR
1
MN
CN
MAAR2
MAAR3
Pref1::Addr1
MAAR
1
MN
MAAR2
MAAR3
Pref2::Addr2
Pref1::Addr1
TUNNEL
CN
CN
MAAR
1
MN
CN
MAAR2
MAAR3
Pref2::Addr2
Pref1::Addr1
PBU
PBA
MAAR
1
MN
CN
MAAR2
MAAR3
Pref2::Addr2
TUNNEL
Pref1::Addr1

## Slide 9: Partial distribution
The data plane is distributed, as each MAAR anchors the flows containing the prefixes of their pool
The Central Mobility Database plays a fundamental role for the control plane
  It stores the MNs’ mobility-related info
  At each MN’s attachment (either initial registration or handover), MAARs query the CMD to retrieve and/or update the session
  The CMD informs old MAARs as well, in order to keep the routing state at the MAARs consistent with the entries stored
  The messages are based on the PBU/PBA format, with changes and extension according to the sequence of operations adopted
    Different solutions are possible

## Slide 10: Partial distribution
MAAR1
MN
CN
MAAR2
MAAR3
Pref1::Addr1
CMD
MAAR1
MN
CN
MAAR2
MAAR3
Pref1::Addr1
CMD
Pref2::Addr2
PBU
PBA
MAAR1
MN
CN
MAAR2
MAAR3
Pref1::Addr1
CMD
Pref2::Addr2
TUNNEL
MAAR1
MN
CN
MAAR2
MAAR3
Pref1::Addr1
CMD
Pref2::Addr2
TUNNEL
CN

## Slide 11: Conclusion
Network-based DMM
  Routers at the edge (MAARs) manage the mobility on behalf of the MNs
  The central anchor is not traversed by data packets
  The degree of achieved distribution can be
    FULL: the control plane is distributed too, with the help of a dedicated protocol suite for the handover phase and movement detection (IEEE 802.21)
    PARTIAL: a central entity is needed for the control plane, playing as a MN’s mobility sessions database, which the MAARs query and update according to MNs’ events

## Slide 12: Changes Required
IEEE 802.21
  We need a way of providing the information regarding the list of previous MAARs anchoring flows to the new MAAR
This can be done extending the primitives carrying the address of the previous AR to use a list instead of just one address. MIH_N2N_HO_Query_Resources.request
IETF
  Extend PMIP signaling, and PMIP state machine to accommodate the new CMD functionality