## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0047-00-srho
Title: Simplified Protocol Header for IEEE 802.21c
Date Submitted: May 2nd , 2012
Presented at Teleconference at May 2nd, 2012
Authors or Source(s):
Hyunho Park and Junghoon Jee (ETRI), H. Anthony Chan (Huawei)
Abstract: This document describes the new simplified protocol header for IEEE 802.21c

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Characteristics of IEEE 802.21c
Packet transmission through the link of authenticated network
Fig. 1. Reference model for single radio handover from a source network to a target network
Reference: IEEE 802.21c Draft (DCN #: 21-12-0004-01-srho)

## Slide 4: Comparison between 802.21c and MIH frame encapsulation
Fig 2. Header encapsulation for MIH frame verses 802.21c
(a) MIH frame using L2 transport
MICF frame
TCP or UDP/IP hdr
L2(1) hdr
PHY(1) hdr
MICF frame
L2(1) hdr
PHY(1) hdr
L2(2) control frame
MICF hdr
TCP or UDP/IP hdr
L2(1) hdr
PHY(1) hdr
(b) MIH frame using higher layer transport
(c) IEEE 802.21c header encapsulation

## Slide 5: Interworking Protocol of WiMAX
Fig 3. Interworking protocols of WiMAX
(a) R9 protocol: protocol between MS and WiMAX SFF for Interworking between Non-WiMAX and WiMAX Access Networks
(b) Rx protocol: protocol between MS and WiMAX SFF for Wi-Fi – WiMAX Interworking
(c) Rx protocol: protocol between MS and WiFi SFF for Wi-Fi – WiMAX Interworking
Reserved (5bits) | B (1bits) | MTI (1bits)
MSID (6 bytes) |  | 
BSID (6bytes) |  | 
802.16 MAC PDU/R9 Control Message |  | 
Reserved (5bits) | B (1bits) | MTI (1bits)
MSID (6 bytes) |  | 
BSID (6bytes) |  | 
802.16MAC PDU/Rx Control Message |  | 
Reserved (5bits) | MTI (1bits)
802.11 MAC PDU/Ry Control Message | 
B | indicates if the BSID field will be included in this message. “0” indicates that the BS ID is omitted in the message and “1” indicates BS ID is included.
MTI (Message Type Indicator) | This bit indicates the type of message.”0” indicates it is Interworking Control Message (for R9, Rx, or Ry), “1” indicates Encapsulated L2 message.
MSID | This is set to the 6-byte MAC address of MS the message pertains to. For transactions not related to any specific MS, all bits shall be set to zero.
BSID | For MS to WiMAX SFF direction, BSID is set to the 6-byte Target WiMAX BS identity from MS to WiMAX SFF. For WiMAX SFF to MS direction, BSID is set to pseudo BSID of the WiMAX SFF. If the MS has the SFF BSID, the BSID field may be omitted by setting the B bit to “0”. If the BSID is not omitted, then it SHALL be set to the BSID received from the SFF.

## Slide 6: Requirements for IEEE 802.21c Protocol
Simplified protocol header is needed
  IEEE 802.21c protocol is positioned on top of the TCP/IP protocol
IEEE 802.21c protocol shall support interworking protocols (R9, Rx, and Ry) of WiMAX
  Interworking protocols of WiMAX does not have control message format yet
New IEEE 802.21c protocol should be distinguished from old protocol

## Slide 7: Fields from the Old Protocol for the New IEEE 802.21c
Filed in old header | Why it needed in the old header? | Why is it kept/not needed in the new header?
Version (4) | used to specify the version of MIH protocol used | Needed To distinguish IEEE 802.21c protocol from old IEEE 802.21 protocol
SID(4)/ Opcode (2)/ AID(10) | Identifies the MIH services, operation, and action | Needed To distinguish control messages for handover
ACK-Req (1)/ Ack-Rsp (1)/ Transaction ID (12) | used when the MIH transport used for remote communication does not provide reliable services | Not needed TCP can provide reliable transmission TCP is a popular protocol for reliable transmission If the TCP can not be used, the old MIH protocol might be used
UIR (1) | used by the MIH Information Service to indicate if the protocol message is sent in pre-authentication/pre-association state | Not needed The single radio handover protocol is transmitted through authenticated source link
M(1)/ FN (1) | Fragmentation for low layer (for L2 layer) | Not needed IP can provide fragmentation
Variable payload length (16) | Indicates the total length of the variable payload | Not needed Each payload has length filed, because the payload uses TLV. Moreover, fragmentation is processed in IP layer, and thus there is no need to have variable payload length

## Slide 8: New Simplified Protocol Design for IEEE 802.21c
Fig 4. New simplified IEEE 802.21c protocol format
Version (4) 2: IEEE 802.21c |  | Interworking Protocol Types (2) |  | BM (1) | MTI (1)
SrcID (6 bytes) |  |  |  |  | 
DstID (6bytes) |  |  |  |  | 
SID (4) | Opcode (2) |  |  |  | 
AID (10) |  |  |  |  | 
Interworking message /Encapsulated target L2 message |  |  |  |  | 

## Slide 9: Description of IEEE 802.21c Protocol Header Fields
Version | This field is used to specify the version of MIH protocol used. 0: Not to be used 1: First version 2: IEEE 802.21c 3–15: (Reserved)
Interworking Protocol Types | Indicates types of interworking protocols 0: IEEE 802.21c single radio handover content 1: ANQP of IEEE 802.11u 2: WiMAX interworking (E.g. R9 protocol) 3: ANDSF message
BM | Indicates if the BSID or MGID field will be included in this message
MTI | Indicates the type of Message 0: Interworking message 1: Encapsulated target L2 message
SrcID (6 bytes) | Source MAC address, e.g., MAC address of MS MAC address of MS when messages are transmitted from MS to target PoA MGID for Mobility GW when messages are transmitted from Mobility GW to MS
DstID (6 bytes) | Destination MAC address, e.g., BSID for target PoA when messages are transmitted from MS to target PoA MAC address of MS when messages are transmitted from Mobility GW to MS
SID | Service identifier (SID): 1: Service Management, 2: Event Service, 3: Command Service, 4: Information Service
Opcode | Operation code (Opcode): 1: Request, 2: Response, 3: Indication
AID | Indicates the action to be taken with regard to the SID

## Slide 10: Considerations for the New IEEE 802.21c
Network elements which use the new simplified protocol should use the old protocol for supporting backward compatibility
  Complexity for the network elements is not high, because most identification mechanisms of control messages can be taken from old IEEE 802.21 protocol

## Slide 11: Conclusions
Characteristics of the new IEEE 802.21c header
  Simplified protocol
  Reliability and fragmentation can be supported by TCP/IP protocol
  The new simplified can support interworking control message for WiMAX
  The new simplified delivers other interworking protocols (e.g, ANQP and ANDSF)
  IEEE 802.21c can use old IEEE 802.21 protocol
Effects of IEEE 802.21c protocol
  Improve network performance with short protocol header
  Support compatibility with other interworking protocols
The simplified protocol raises its customization chance by supporting improved network performance and compatibility with other interworking protocol

## Slide 12: References
IEEE 802.21c, “IEEE Standard for Local and Metropolitan Area Networks - Part 21: Media Independent Handover Services Amendment: Optimized Single Radio Handovers,” Jan., 2012.
WiMAX Forum, “WiMAX Forum Network Architecture - Architecture, Detailed Protocols and Procedures WiFi® and WiMAX® Access Networks,” Nov. 2010.
WiMAX Forum. “WiMAX Forum Network Architecture - Architecture, detailed Protocols and Procedures Single Radio Interworking between Non-WiMAX® and WiMAX® Access Networks,” Nov. 2010.