## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0047-02-srho
Title: Simplified Protocol Header for IEEE 802.21c
Date Submitted: May 16, 2012
Presented at IEEE 802 Interim meeting on May 16, 2012
Authors or Source(s):
Hyunho Park and Junghoon Jee (ETRI), H. Anthony Chan (Huawei), Dapeng Liu (China Mobile)
Abstract: This document describes the new simplified protocol header for IEEE 802.21c

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: MIH Protocol Format & Header
MIH Protocol General Frame Format
MIH Protocol Header Format (Header Size: 8 Octets (=8Bytes))
Mandatory

## Slide 4: Comparison between 802.21c and MIH frame encapsulation
1. (a) MIH frame using L2 transport
MIH frame
L2(1) hdr
PHY(1) hdr
L2(2) control frame
MICF hdr
TCP or UDP/IP hdr
L2(1) hdr
PHY(1) hdr
2. (a) IEEE 802.21c encapsulation of L2 control frame
MICF Payload (as an Interworking Protocol)
MICF hdr
TCP or UDP/IP hdr
L2(1) hdr
PHY(1) hdr
2. (b) IEEE 802.21c frame using higher layer transport
MIH frame
TCP or UDP/IP hdr
L2(1) hdr
PHY(1) hdr
1. (b) MIH frame using higher layer transport

## Slide 5: Interworking Protocol of WiMAX
(a) R9 protocol: protocol between MS and WiMAX SFF for Interworking between Non-WiMAX and WiMAX Access Networks
(b) Rx protocol: protocol between MS and WiMAX SFF for Wi-Fi – WiMAX Interworking
(c) Ry protocol: protocol between MS and WiFi SFF for Wi-Fi – WiMAX Interworking
Reserved (6bits) | B (1bits) | MTI (1bits)
MSID (6 bytes) |  | 
BSID (6bytes) |  | 
802.16 MAC PDU/R9 Control Message |  | 
Reserved (6bits) | B (1bits) | MTI (1bits)
MSID (6 bytes) |  | 
BSID (6bytes) |  | 
802.16MAC PDU/Rx Control Message |  | 
Reserved (7bits) | MTI (1bits)
802.11 MAC PDU/Ry Control Message | 
802.21c is required to define interfaces for WiMAX<>WiFi and WiMAX <> 3GPP SRHO using Rx, Ry, and R9 protocols
WiMAX Forum, “WiMAX Forum Network Architecture - Architecture, Detailed Protocols and Procedures WiFi® and WiMAX® Access Networks,” Nov. 2010.
WiMAX Forum. “WiMAX Forum Network Architecture - Architecture, detailed Protocols and Procedures Single Radio Interworking between Non-WiMAX® and WiMAX® Access Networks,” Nov. 2010.
Simple protocol header
  Header size= 1 Byte (excluding MSID and BSID)
Functional Requirements (IEEE 802.21c document, DCN # 21-10-0017-02-srho)

## Slide 6: Interworking Protocol of WiMAX (Cont’d)
B | indicates if the BSID field will be included in this message. “0” indicates that the BS ID is omitted in the message and “1” indicates BS ID is included.
MTI (Message Type Indicator) | This bit indicates the type of message.”0” indicates it is Interworking Control Message (for R9, Rx, or Ry), “1” indicates Encapsulated L2 message.
MSID | This is set to the 6-byte MAC address of MS the message pertains to. For transactions not related to any specific MS, all bits shall be set to zero.
BSID | For MS to WiMAX SFF direction, BSID is set to the 6-byte Target WiMAX BS identity from MS to WiMAX SFF. For WiMAX SFF to MS direction, BSID is set to pseudo BSID of the WiMAX SFF. If the MS has the SFF BSID, the BSID field may be omitted by setting the B bit to “0”. If the BSID is not omitted, then it SHALL be set to the BSID received from the SFF.

## Slide 7: Requirements for IEEE 802.21c Protocol
Different use of transport mechanism (from 802.21):
  • IEEE 802.21c protocol is positioned on top of the TCP/IP protocol
IEEE 802.21c protocol SHALL support interworking protocols (R9, Rx, and Ry) of WiMAX
The 802.21c protocol are desirable to deliver other interworking protocols (e.g, ANQP and ANDSF message)
With the different transport and different requirements from 802.21 protocol, the 802.21c protocol needs new design

## Slide 8: Considerations for Existing Fields for Designing New 21c Header
Filed in old header | Why is it kept/not needed in the new header?
Version (4) | Needed: To distinguish IEEE 802.21c protocol from old IEEE 802.21 protocol
SID(4)/ Opcode (2)/ AID(10) | Needed: To distinguish control messages for handover
ACK-Req (1)/ Ack-Rsp (1)/ Transaction ID (12) | Not needed : May use TCP to provide reliable transmission Else, may include these field into a TLV
UIR (1) | Not needed: The single radio handover protocol is transmitted through authenticated source link
M(1)/ FN (7) | Not needed: IP can provide fragmentation
Variable payload length (16) | Needed: TLV (Type –Length-Value) may not be enough to tell length of the frame

## Slide 9: New Simplified Protocol Design for IEEE 802.21c
Version (4) 2: IEEE 802.21c |  | Interworking Protocol Types (2) |  | B (1) | MTI (1)
SrcID (6 bytes) |  |  |  |  | 
DstID (6bytes) |  |  |  |  | 
SID (4) | Opcode (2) |  |  |  | 
AID (10) |  |  |  |  | 
Variable payload length (16) |  |  |  |  | 
Payload (MICF payload, Other interworking frame, or L2 encapsulation) |  |  |  |  | 
Header Size=5Bytes excluding source and destination IDs
(3Bytes saving)

## Slide 10: Description of IEEE 802.21c’s New Protocol Header Fields
Version | This field is used to specify the version of MIH protocol used. 0: Not to be used 1: First version 2: IEEE 802.21c 3–15: (Reserved)
Interworking Protocol Types | Indicates types of interworking protocols 0: IEEE 802.21c single radio handover content 1: ANQP of IEEE 802.11u 2: WiMAX interworking (E.g. R9 protocol) 3: ANDSF message
B | Indicates if the BSID field will be included in this message
MTI | Indicates the type of Message 0: Interworking message 1: Encapsulated target L2 message
SrcID (6 bytes) | Source MAC address, e.g., MAC address of MS MSID for WiMAX interworking protocol
DstID (6 bytes) | Destination MAC address, e.g., MAC address of M-GW BSID for WiMAX interworking protocol

## Slide 11: Description of IEEE 802.21c’s New Protocol Header Fields (Cont’d)
SID | Service identifier (SID): 1: Service Management, 2: Event Service, 3: Command Service, 4: Information Service
Opcode | Operation code (Opcode): 1: Request, 2: Response, 3: Indication
AID | Indicates the action to be taken with regard to the SID
Variable payload length | Indicates the total length of the variable payload embedded in this 21c protocol frame. The length of the 21c protocol header is NOT included.
SrcID (6 bytes) | Source MAC address, e.g., MAC address of MS MSID for WiMAX interworking protocol
DstID (6 bytes) | Destination MAC address, e.g., MAC address of M-GW BSID for WiMAX interworking protocol

## Slide 12: Complement for Reliability for UDP
If TCP is not used, fields for supporting reliability can be added using TLV type
  E.g.
Type =Reliability | Length =2 bytes | Ack-Req (1) | Ack-Rsp (1) | Transaction ID (12) | Reserved (2)
Value

## Slide 13: Considerations of Compatibility between IEEE 802.21 and New IEEE 802.21c
Network elements which use the new simplified protocol should use the old protocol for supporting backward compatibility
  Complexity for the network elements is not high, because most identification mechanisms of control messages can be taken from old IEEE 802.21 protocol

## Slide 14: Conclusions
The new IEEE 802.21c header
  Omits some fields which are related with reliability because these fields can be supported by TCP/IP protocol
  Includes Interworking Protocol Type field to deliver other interworking protocols (e.g, ANQP and ANDSF message)
  Can support interworking control message for WiMAX
  IEEE 802.21c can use old IEEE 802.21 protocol
Effects of IEEE 802.21c protocol
  Improve network performance with short protocol header
  Support compatibility with other interworking protocols
The simplified protocol raises its customization chance by supporting improved network performance and compatibility with other interworking protocol

## Slide 15: References
IEEE 802.21c, “IEEE Standard for Local and Metropolitan Area Networks - Part 21: Media Independent Handover Services Amendment: Optimized Single Radio Handovers,” Jan., 2012.
WiMAX Forum, “WiMAX Forum Network Architecture - Architecture, Detailed Protocols and Procedures WiFi® and WiMAX® Access Networks,” Nov. 2010.
WiMAX Forum. “WiMAX Forum Network Architecture - Architecture, detailed Protocols and Procedures Single Radio Interworking between Non-WiMAX® and WiMAX® Access Networks,” Nov. 2010.
Functional Requirements (IEEE 802.21c document, DCN # 21-10-0017-02-srho)