## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0060-00-srho
Title: PoS-based_Handover
Date Submitted: May 12th , 2012
Presented at IEEE 802.21c at May 12th, 2012
Authors or Source(s): Charles E. Perkins (Futurewei)
Abstract: This document describes the TLVs for PoS-based handovers for IEEE 802.21c

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: PoS-oriented handover optimization supported by roaming agreement
SPoS
HPoS
TPoS
Inter PoS SA
Preregistration
MN movement
AN
tAN
AN

## Slide 4: MN  PoS security
Tunneled traffic between PoSs may traverse the internet  tunnel security requirement
When MN enters a network, it gets a security association (SA) with the local PoS in the originating network (SPoS)
When MN decides to handover to a target network, the SPoS uses its existing SA to tunnel preregistration traffic to target PoS (TPoS)
SPoS also supplies derived (MN  TPoS) security association to MN and TPoS as part of preregistration

## Slide 5: MN moves: using SPoS
Handover preparation:
MN decides to move
MN acquires information about {tAN, tBS, pAN, …}
MN signals target network to complete preparation from its current point of attachment, in “originating network”
(a) MN  PoS in originating network (i.e., “SPoS”).
(b) SPoS TPoS in network of a roaming partner
Overall, MN  SPoS  TPoS  {tAN, tBS, pAN, …}

## Slide 6: MN  PoS: derived keys notation
K_hpos | key between MN and HPoS
K_spos | key between MN and SPoS
K_tpos | key between MN and TPoS
K_hspos | key between HPoS and SPoS
K_htpos | key between HPoS and TPoS
K_stpos | key between SPoS and TPoS
KDF_hspos | key distribution function between HPoS and SPoS
KDF_stpos | key distribution function between SPoS and TPoS

## Slide 7: Handover: SPoS enables MN TPoS security
SPoS provides the MN and TPoS with security credentials, possibly along with RAT type, etc.
If SPoS does not know KDFstpos, SPoS can establish it by running IKE with TPoS
SPoS sends Ktpos  TPoS
  payload = MNaddr, nonce, {Ktpos ⊕ KDFstpos (MNaddr, nonce)}
SPoS sends Ktpos  MN
  payload = TPoS, nonce, {Ktpos ⊕ KDFspos (TPoS, nonce)}

## Slide 8: Annex N (srho-secure-key-distribution)

## Slide 9: TLV for MIH_LL_Transfer.request
/* Let K_spos define security association SPoS  MN */
  TLV: MN-TPoS_setup.request to SPoS
    preferred.RATs
    nonce

## Slide 10: TLV for MIH_N2N_LL_Transfer.request
/* Let K_stPoS define security association SPoS  TPoS */
  TLV: SPoS-TPoS_setup.request for MN
    preferred.RATs
    MNaddr
    nonce
    Ktpos ⊕ KDFstpos (MNaddr, nonce)

## Slide 11: TLV for MIH_N2N_LL_Transfer.response
/* Let K_tsPoS define security association TPoS  SPoS */
  TLV: TPoS-SPoS_setup.confirm for MN

## Slide 12: Unaffected signals from Annex N
MIH_LL_Transfer.indication
/* target network processing only */
MIH_N2N_LL_Transfer.indication
/* target network processing only */

## Slide 13: TLV for MIH_LL_Transfer.response
/* Let K_sPoS define security association SPoS  MN */
  TLV: SPoS-TPoS_setup.request for MN
    selected.RAT
    TPoSaddr
    Ktpos ⊕ KDFspos (TPoSaddr, nonce)

## Slide 14: HPoS = PoS located at Home Agent
Then, MN already has required security association
  HPoS function is logically distinct from MIP
  HPoS needs security associations with all PoSs
The HPoS function offers advantages
  eliminates need for MN to run IKE with target PoS
  can enable external home agent functionality
    This could greatly simplify WiFi session continuity
  can enable private addressing for core entities

## Slide 15: Standardization requirement
Security arrangements between PoS and MNs
Security arrangements between PoSs
If HA == PoS, then new extensions in IETF [dmm?]
PoS for 3GPP
Enable external HA (external to source, target networks)

## Slide 16: Operation requirements
Roaming agreements to include inter-PoS security
If PoS is not co-located at home agent, then additional PoS security with MN (with HPoS in home network)
Location database would enable network guidance for target networks
Approach seems much easier than alternatives

## Slide 17: Characteristics of IEEE 802.21c
Packet transmission through the link of authenticated network
Fig. 1. Reference model for single radio handover from a source network to a target network
Reference: IEEE 802.21c Draft (DCN #: 21-12-0004-01-srho)