## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0119-01-srho
Title: Proposal of new SID in IEEE 802.21c
Date Submitted: Sept. 17th 2012
Presented at IEEE 802.21c TG
Authors or Source(s):
Hyunho Park (ETRI), Hyeong-Ho Lee (ETRI), Anthony Chan (Huawei)
Abstract: This contribution proposes new SID (Mobility Gateway Service) for IEEE 802.21c.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: MIH Protocol Header Format with New SID
Service identifier (SID) | Action identifier (AID)
Identifies the different MIH services, possible values are as follows: 1: Service Management 2: Event Service 3: Command Service 4: Information Service 5: Gateway Service | This indicates the action to be taken with regard to the SID When SID=5. If AID=0, L2 messages for the target network If AID=1, ANQP of IEEE 802.11u If AID=2, ANDSF message If AID=3, R9 Protocol of WiMAX If AID=4, Rx Protocol of WiMAX If AID=5, Ry Protocol of WiMAX From 6 to 500, reserved for other interworking protocols From 501 to 1023, reserved for vendor specific area

## Slide 4: Analysis in Implementation of the MN and the MGW
The MN using the other interworking protocol, such as ANQP or ANDSF messages, can interact with the MGW of IEEE 802.21c
  Even though the MN is equipped with the simple function handling “Gateway Service” (SID=5) of IEEE 802.21c, the MN can communicate with the MGW of IEEE 802.21c
The new SID for “Gateway Service” can enhance bridging mobility signaling for the MGW.
  Through the new SID, the MGW performs a proxy for interworking with other networks using ANQP or ANDSF.

## Slide 5: When AID is Zero (L2 Message Transfer)
Figure 11.5 The target PoA supports MICF.
If MN does not know the IP address of the target PoA, the MGW functions like a proxy for the MN to send the target radio L2 network entry packets to the target PoA.
Figure 11.6 The target PoA does not support MICF.
The M-GW communicates with the target POA using other control messages in order to proxy between the MN and the target POA.

## Slide 6: When AID is Larger than Zero (For the MN using other Interworking Protocols)
Interworking Protocol Message | Interworking Protocol Message
 | MICF hdr (SID=5, AID>=1)
TCP or UDP/ IP hdr | TCP or UDP/ IP hdr
L2 hdr | L2 hdr
PHY hdr | PHY hdr
Interworking Protocol Message
MICF hdr (SID=5, AID>=1)
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
MN
Other Network Entity
1. When the other network entity supports “Gateway Service”
Even though the MN using other interworking protocols is equipped with the simple function handling the new MIH service, “Gateway Service”, the MN can communicate with the MGW of IEEE 802.21c.
The PoA encapsulates interworking protocol message with the MICF hdr using the new SID, “5”.
Interworking Protocol Message
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
PoA

## Slide 7: When AID is Larger than Zero (For the MN using other Interworking Protocols)
Interworking Protocol Message | Control Message
MICF hdr (SID=5, AID>=1) | 
TCP or UDP/ IP hdr | TCP or UDP/ IP hdr
L2 hdr | L2 hdr
PHY hdr | PHY hdr
Control Message
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
MN
MGW
Other Network Entity
2. When the other network entity does not support “Gateway Service”
The MGW converts the interworking protocol message into the control message for the other network entity.
The control message can be a different interworking protocol message.
Interworking Protocol Message | Interworking Protocol Message
 | MICF hdr (SID=5, AID>=1)
TCP or UDP/ IP hdr | TCP or UDP/ IP hdr
L2 hdr | L2 hdr
PHY hdr | PHY hdr
Interworking Protocol Message
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
PoA

## Slide 8: Case Study: ANQP Delivery without the MGW and the new SID
The AP should be MIH-PoS to communicate with the IS (Information Server)
Implementation of the AP can be complicate.
Ref: 802.11/21 Network Discovery and Selection Architecture (DCN: 21-12-0025-00-0000)

## Slide 9: Case Study: ANQP Delivery with the MGW and the new SID
1. When the information server supports “Gateway Service”
  The WLAN AP as a proxy of the MN only encapsulates ANQP message with the MICF header using the new SID.
GAS (ANQP) Message | ANQP Message
 | MICF hdr (SID=5, AID>=1)
 | TCP or UDP/ IP hdr
 | L2 hdr
IEEE 802.11PHY | PHY hdr
ANQP Message
MICF hdr (SID=5, AID>=1)
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
GAS (ANQP) Message
IEEE 802.11PHY
MN
WLAN AP
(as a proxy of MN)
Media Independent Information Server

## Slide 10: Case Study: ANQP Delivery with the MGW and the new SID
2. When the information server does not support “Gateway Service”
  The WLAN AP as a proxy of the MN encapsulates only ANQP message with the MICF header using the new SID.
  The MGW converts the encapsulated ANQP message to other interworking message.
ANQP Message | Other Interworking Message
MICF hdr (SID=5, AID>=1) | 
TCP or UDP/ IP hdr | TCP or UDP/ IP hdr
L2 hdr | L2 hdr
PHY hdr | PHY hdr
Other Interworking Message
TCP or UDP/ IP hdr
L2 hdr
PHY hdr
MN
WLAN AP
(as a proxy of MN)
MGW
Other Information Server
GAS (ANQP) Message | ANQP Message
 | MICF hdr (SID=5, AID>=1)
 | TCP or UDP/ IP hdr
 | L2 hdr
IEEE 802.11PHY | PHY hdr
GAS (ANQP) Message
IEEE 802.11PHY

## Slide 11: Conclusions
With the new SID, the MN using other interworking protocols can communicate with other network entity through the PoA or MGW.
  Implementation of the MN and PoA can be simplified.
  Thus, the commercialization possibility of the IEEE 802.21c will be increased.
The new SID can enhance mobility signaling of the MGW.
  The MGW functions as a proxy with other interworking protocols to communicate with other interworking network entity.