## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-12-0127-00-srho
Title: More Discussion on “MGW vs. MIH-PoS” in IEEE 802.21c
Date Submitted: Sept. 19th, 2012
Presented at IEEE 802.21c TG
Authors or Source(s): Charlie Perkins
Abstract: This contribution shows the MGW can be replaced with the MIH-PoS because the only distinction between MGW and MIH-PoS relies on non-essential matters of terminology.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Definition of the MIH PoS in IEEE 802.21-2008
Network-side MIHF instance that exchanges MIH messages with an MN-based MIHF.
The same MIH Network Entity includes an MIH PoS for each MIH-enabled mobile node with which it exchanges MIH messages.
A single MIH PoS can host more than one MIH service.
The same MIH Network Entity can include multiple MIH Points of Service that can provide different combinations of MIH services to the respective mobile nodes based on subscription or roaming conditions.
Note that for a network entity comprising multiple interfaces, the notion of MIH PoS is associated with the network entity itself and not with just one of its interfaces.

## Slide 4: Definition of the MGW in IEEE 802.21c Draft (DCN# 21-12-0067-06-srho)
A gateway to bridge the mobility signaling between a mobile node (MN) and a target network via the source network.
To the MN, the MGW acts like a virtual point of attachment (POA) to the target network.
It enables such functions as pre-registration and proactive authentication of the MN.

## Slide 5: Relationship between MGW and MIH-PoS
MGW as an MIH-PoS
  The MGW also can receive the MIH messages, and thus operate based on the MIH messages.
Figure 11.5 The target PoA supports MICF.
If MN does not know the IP address of the target PoA, the MGW functions like a proxy for the MN to send the target radio L2 network entry packets to the target PoA.
Figure 11.6 The target PoA does not support MICF.
The M-GW communicates with the target POA using other control messages in order to proxy between the MN and the target POA.
MGW as a Proxy between the MN and the target PoA

## Slide 6: Updated definition for PoS
Network-side MIHF instance that exchanges MIH messages with an MN-based MIHF.
The same MIH Network Entity includes an MIH PoS for each MIH-enabled mobile node with which it exchanges MIH messages.
A single MIH PoS can host more than one MIH service.
For handover services, PoS entities may communicate to expedite MN protocol requests
Note that for a network entity comprising multiple interfaces, the notion of MIH PoS is associated with the network entity itself and not with just one of its interfaces.
For handover services, PoS entities may communicate with candidate PoAs to expedite MN protocol requests

## Slide 7: SPoS TPoS example
SPoS
HMGW
TPoS
Inter PoS SA
Preregistration
MN movement
AN
tAN
AN