## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-13-xxxx-00-MuGM
Title: Outline of 21-13-0002-01-MuGM
Date Submitted: January, 15th, 2013
Presented at IEEE 802.21 session #54 in Vancouver
Authors or Source(s):
Yoshikazu Hanatani, Toru Kambayashi (Toshiba)
Abstract: This is a summary of 21-13-0002-01-MuGM.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Outline
System Architecture
Overview of New Commands
Modified / New Primitives and Messages

## Slide 4: System Architecture
MIHF
MIH User
PoS: Command Center + Group Manager
MIHF
MIH User
MN
MIHF
MIH User
MN
Multicast channels
Plural Command Centers may share a Group Manager.

## Slide 5: System Architecture
PoS’s MIH User
  All device keys
    List of (Node ID, Node key)
  Group Management Database
    List of (Group ID, Group members’ ID, Master Group Key)
PoS’s MIHF
  A device key
  A signing key
  Group Information Database of PoS
    List of (Group ID, Multicast Address, Master Group Key)
MN’s MIH User
MN’s MIH MIHF
  A device key
  A verification key and a certificate.
  Group Information Database of MN
    List of (Group ID, Multicast Address, Master Group Key)

## Slide 6: Group Manipulate Overview
PoS’s MIH User:
  Decide a group ID, group members and destination identifier(s).
  Generate a master group key and a group key blocks (GKB) for those members.
PoS’s MIHF:
  Obtain the master group key.
  Find a multicast address from the destination identifier.
  Generate a signature for the group manipulate command.
  Send the group manipulate command to the multicast address.
MN’s MIHF:
  Verify the signature for the group manipulate command.
  Obtain the master group key from the GKB in the group manipulate command.
  If it fails leave the group, otherwise join the group or update the group key.
MIHF
MIH User
MN
MIHF
MIH User
PoS

## Slide 7: Group Commands: Overview
PoS’s MIH User:
  Define a destination ID and information to be sent to the group.
PoS’s MIHF:
  Find a multicast address from the destination ID.
  Generates a signature for the group command.
  (Option) Find the master group key from the destination ID, and encrypt the payload of the command.
  Sends the group command to the multicast address.
MN’s MIHF:
  Verify the signature in the group command.
  (Option) Find the master group key from the destination ID, and decrypt the payload of the group command.
  Decide the behavior for the group command.
MIHF
MIH User
MN
MIHF
MIH User
PoS

## Slide 8: Certificate Push : Overview
PoS’s MIH User:
  Decide destination IDs to which a certificate is sent.
PoS’s MIHF:
  Find the multicast address from the destination ID.
  Sends a certificate push command, which contains the certificate, to the multicast address.
MN’s MIHF:
  Verify the signature in the certificate push command.
  Install the certificate if the verification succeeds.
  Return the Ack to the PoS’s MIHF.
MIHF
MIH User
MN
MIHF
MIH User
PoS

## Slide 9: Certificate Revoke : Overview
PoS’s MIH User:
  Decide a source ID to revoke the certificate.
  Decide a destination ID to which the revoke is sent.
PoS’s MIHF:
  Find the multicast address from the destination ID.
  Sends a certificate revoke command, which contains the certificate status, to the multicast address.
MN’s MIHF:
  Revoke the certificate specified by the certificate revoke command.
MIHF
MIH User
MN
MIHF
MIH User
PoS

## Slide 10: Modified Primitives/Messages
Primitives
  MIH_Register.responce (7.4.2.3.1)
  MIH_Register.confirm (7.4.2.4.1)
  MIH_Link_Actions.request (7.4.16.1.2)
  MIH_Net_HO_Commit.request (7.4.21.1.2)
  MIH_Net_HO_Commit.indication (7.4.21.2.2)
Messages
  MIH_Link_Actions request (8.6.3.5)
  MIH_Net_HO_Commit request (8.6.3.15)

## Slide 11: New Primitives/Messages
Primitives
  MIH_Configuration_Update.request (7.4.29.1.2)
  MIH_Configuration_Update.indication (7.4.29.2.2)
  MIH_Group_Manipulate.request (7.4.30.1.2)
  MIH_Group_Manipulate.indication (7.4.30.2.2)
  MIH_Push_Certificate.request (7.4.31.1.2)
  MIH_Push_Certificate.indication (7.4.31.2.2)
  MIH_Push_Certificate.response (7.4.31.3.2)
  MIH_Push_Certificate.confirm (7.4.31.4.2)
  MIH_Revoke_Certificate.request (7.4.32.1.2)
  MIH_Revoke_Certificate.indication (7.4.32.2.2)
  MIH_Revoke_Certificate.response (7.4.32.3.2)
  MIH_Revoke_Certificate.confirm (7.4.32.2)

## Slide 12: New Messages
MIH_Configuration_Update indication (8.6.3.23)
MIH_Group_Manipulate indication (8.6.3.24)
MIH_Push_Certificate request (8.6.3.25)
MIH_Push_Certificate response (8.6.3.26)
MIH_Revoke_Certificate request (8.6.3.27)
MIH_Revoke_Certificate response (8.6.3.28)