## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-14-0006-00-SAUC
Title: Media Independent Service Use Cases for Resource Management in Heterogeneous Networks
Date Submitted: January 18th, 2014
Presented at IEEE 802.21 Session #60 – Los Angeles, USA
Authors or Source(s):
Hyunho Park(ETRI), Hyeong-Ho Lee(ETRI), Jin Seek Choi (Hanyang University, Korea Ethernet Forum) and Seung-Hwan Lee (ETRI)
Abstract: This document proposes Media Independent Service use cases for resource management in heterogeneous networks.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Coexistence Problem in Heterogeneous Networks: WLAN Example – 2.4 GHz band
Wireless communication technologies in 2.4 GHz and 5GHz bands
  In 2.4 GHz band, WLAN and Bluetooth may interfere each other.
  In 5 GHz band, WLAN and Cordless Phone may interfere each other.
WLAN
(IEEE 802.11b/g/n), Bluetooth
2.4 GHz
2.5 GHz
5.170 GHz
5.905 GHz
Cordless Phone
5.745 ~ 5.825 GHz
WLAN
(IEEE 802.11a/n/ac)
Channels of WLAN in 2.4 GHz band
  Only 3 channels are not overlapped in 2.4 GHz band.
  Channel 1, 6, and 11 are used for Wi-Fi Direct.
  An MN (Mobile Node) that operates in 2.4 GHz band can be easily interfered in a dense WLAN environment.

## Slide 4: Coexistence Problem in Heterogeneous Networks: WLAN Example – 5 GHz band
Channels of WLAN in 5 GHz band
  About 20 channels are not overlapped in 5 GHz band.
  An MN that operates in 5 GHz band can not be easily interfered compared to the MN that operates in 2.4 GHz.
  However, the MN operating in 5GHz band may be interfered by cellular link in the future.
  5GHz unlicensed band is considered as frequency band for LTE advanced.
Reference: Qualcomm, “Extending the benefits of LTE advanced to unlicensed spectrum,” Nov. 2013. (http://www.qualcomm.com/media/documents/extending-benefits-lte-advanced-unlicensed-spectrum)
5GH Unlicensed Band

## Slide 5
In 2.4 GHz band
In 5 GHz band
MN
Connected AP (Access Point)
Radio interference
MN
Connected AP
Wi-Fi Direct devices
Bluetooth device
Neighboring WLAN
Radio interference
Cordless phone
(Maybe in future)
Cellular network
Radio interference
Radio interference
Radio interference
Neighboring WLAN
Radio interference degrades QoS of wireless communications.
Coexistence Problem in Heterogeneous Networks: WLAN Example – MN affected by radio interference
(Maybe in future)
Radio interference

## Slide 6: Resource Management in Heterogeneous Networks to Provide Better QoS
Harmonizing methodologies for resource management
1. Frequency channel allocation
Selecting a frequency channel that can mitigate radio interference
Example)
2. Transmission power control
Coverage of wireless communication can be decreased by controlling transmission power.
Example)
3. Time slotting
Allocating different communications on different time slots can avoid radio interference
Example)
MN
Radio interference
Connected AP
WLAN
2.4 GHz band
2.4 GHz band
MN
Radio interference
Connected AP
WLAN
5 GHz band
2.4 GHz band
Frequency channel allocation
Bluetooth device
Bluetooth device
MN
Radio interference
Connected AP
WLAN
2.4 GHz band
2.4 GHz band
Neighboring WLAN
MN
Connected AP
WLAN
2.4 GHz band
Transmission power control
of
neighboring WLAN
Transmission power control
 Coverage control
Time
Neighboring WLAN or
other communication technology
WLAN
5 GHz band
Time
Neighboring WLAN or
other communication technology
WLAN
5 GHz band
Time slotting
Time Slot 1
Time Slot 2

## Slide 7: Resource Management in Heterogeneous Networks to Provide Better QoS (Cont’d)
Harmonizing architectures for resource management
1. Auto-configuration
AP manages its radio resources (e.g., frequency, power, and time) by itself.
AP may monitor link status (status of physical and data link layer).
2. Cooperation between APs
AP manages its radio resources by cooperating with neighboring APs.
3. Resource management by AC (Access Controller)
AC manageress radio resources of APs
Example)
Example)
Example)
WLAN AP detects radio interference in 2.4GHz band.
Bluetooth device
1
2
WLAN AP allocates its frequency band in 5 GHz.
AP
MN
AP A
AP B
(Neighboring AP)
1. I (AP A) operates in 2.4 GHz band.
2. Okay. I (AP B) will use 5 GHz band.
AP A
AP B
(Neighboring AP)
AC
Use 2.4 GHz band
Use 5 GHz band

## Slide 8: Related Works in Previous Standards
Standards | Works | Limitation to achieve radio resource management
IEEE 802.19.1 draft standard (On going) [1] | IEEE 802.19.1 draft standard specifies radio technology independent methods for coexistence among dissimilar or independently operated TV Band Device (TVBD) networks and dissimilar TV Band Devices. | IEEE 802.19.1 draft standard does not provide coexistence of devices that use 2.4 GHz and 5GHz. IEEE 802.19.1 draft standard solves the coexistence problem, but does not support resource management for providing better QoS.
IEEE 802.15.2 standard [2] | IEEE 802.15.2 standard specifies coexistence of IEEE 802.15 devices (e.g., Bluetooth device) with other wireless devices (e.g., IEEE 802.11b device) operating in unlicensed frequency bands (2.4 GHz). | IEEE 802.15.2 standard focuses on coexistence of WPAN device and WLAN device in 2.4 GHz, and thus cannot cope with radio interference in 5 GHz.
IEEE 802.11f standard [3] | IAPP (Inter-Access Point Protocol) of IEEE 802.11f enables communications between WLAN APs. | IAPP is designed for WLAN and thus cannot support the networks (e.g., Bluetooth network and cellular network) that are not WLAN. IEEE 802.11f standard does not specify use of IAPP for resource management.
IETF RFC 5415 standard [4] | CAPWAP (Control And Provisioning of Wireless Access Points) of RFC 5415 enables AC to manage WLAN APs. | CAPWAP is designed for WLAN and thus cannot support the networks (e.g., Bluetooth network and cellular network) that are not WLAN. CAPWAP operates over UDP but does not define how an MN to monitor and control link layers (physical layer and data link layer) for resource management.
Requirements for resource management in heterogeneous networks
  Resources should be allocated for the networks that use various communication technologies (e.g., WLAN and LTE operating in 5GHz band) and various frequency bands (e.g., 2.4GHz band and 5 GHz band).
  AP should manage its own resources by monitoring and controlling link layers (physical layer and data link layer).

## Slide 9: Media Independent Services Framework for Resource Management in Heterogeneous Networks
Media Independent Services Framework of IEEE 802.21 standard can be a common platform to support resource management in heterogeneous networks.
  Media Independent Services Framework of IEEE 802.21 supported seamless handover between networks using various communication technologies and various frequency bands.
  Media Independent Services Framework is appropriate for resource management in heterogeneous networks that use various communication technologies and various frequency bands.
  MIES (Media Independent Event Service) helps MN to monitor link status, and MICS (Media Independent Command Service) helps MN to control its link layers (physical layer and data link layer).
   Media Independent Services Framework enables MN to monitor and control its link layers for resource management.

## Slide 10: Media Independent Services Framework for Harmonizing Resource Management in Heterogeneous Networks
MIH user: Layer 3 or higher mobility protocol (L3MP)
MIHF: Media independent handover function
Link layer: Physical layer and data link layer
MIHF
MIH User
Link Layer
MIHF
Link Layer
MIH User
MIHF
MIH User
Link Layer
MIHF
MIH User
Link Layer
AP
MN
AC
Neighboring AP
Controlling link layer by MICS
Controlling link layer by MICS
Monitoring link status by MIES
Reporting link status by MIES
Controlling link layer of AP by sending MICS messages
Reporting link status of AP by sending MIES messages
Reporting link status of AP by sending MIES messages
Reporting link status of neighboring AP by sending MIES messages
Reporting link status of MN by sending MIES messages
AC can control resources of APs that use various communication technologies (e.g., WLAN, Wi-Fi Direct, Bluetooth, and LTE) by using MICS message.
APs can use different communication technologies and share its link status by using MIES message.

## Slide 11: Use case 1: Harmonizing Radio resource management based on link status of MN
MIHF
Based on reported link status (e.g., signal strength and data rate) of MN, AP can allocate the most appropriate resources (e.g., frequency band, transmission power, and time) for the MN to harmonize heterogeneous technologies.
AP
MIH User
Primitive to change resource allocation
MIHF
Link Layer
L1/L2
MIH User
Primitive to report
bad link status
Mobile Node (MN)
Proposed Media Independent Service Message
Media Independent Primitive or Message
Message to report link status of MN
Link Layer
L1/L2
Resource allocation is changed.
Primitive to report
MN’s bad link status
Primitive to change resource allocation

## Slide 12: Use case 2: Radio resource management based on link status of AP
MIHF
By monitoring link status of AP, AP allocates AP can allocate the most appropriate resources for MN.
AP, neighboring AP, and neighboring MN can use different communication technologies.
AP, neighboring AP, and neighboring MN
AP
Link Layer
L1/L2
MIH User
Radio interference from neighboring AP and neighboring MN
Link_Detected
MIH_Link_Detected
Primitive to change resource allocation
Primitive to change resource allocation
Resource allocation is changed.
Proposed Media Independent Primitive or Message
MIH Primitive or MIH Message
Radio interference

## Slide 13: Use case 3: Radio resource management based on link status of neighboring AP
Based on link status of neighboring AP, AP can allocate the most appropriate resources for MN.
AP and neighboring AP can use different communication technologies.
Neighboring AP
AP
Link Layer
L1/L2
MIH User
MIHF
MIH User
Report of status of link that neighboring AP uses
Primitive to change resourceallocation
Resource allocation changed.

## Slide 14: Use case 4: Radio resource management by AC
AC can allocate the most appropriate resources of AP.
AP and neighboring AP can use different communication technologies.
Neighboring AP
AP
AC
Link Layer
L1/L2
MIH User
MIHF
MIHF
MIH User
Report of resources that neighboring AP uses
AC knows that resources of AP and neighboring AP.
AC decides to change resource allocation of AP
Message to change resource allocation of AP
Primitive to change resource allocation
Resource allocation is changed.

## Slide 15: Needs of Resource Management for Other Media Independent Service Use Cases
For use case of D2D communication
  To improve QoS of D2D communication, resource management is needed.
For use case of interworking service
  Resources management of link between IWR and IWG is needed
MN A
(e.g., Jane’s MN)
MN B
(e.g., Smith’s MN)
PoS
WLAN/ WPAN/WiMAX/
Cellular Network
Request for selection of D2D communication and assignment of radio resource
Request for selection of D2D communication and resource management
Configuration information for connecting to peer node (MN A)
Connection D2D Communication
PoS
NADC (Network Assisted D2D Communication) Provider (PoS)
Request/response for peer discovery of MNs
Configuration information for connecting to peer node (MN B)
Information Server
ED
IWR
IWG
SN (e.g., 802.15.4)
Virtual Link
IN (3G, etc.)
SN: Serving Network
IN: Interworking Network
ED: End Device
IWR: Interworking Relay
IWG: Interworking Gateway
Serving Network MAC frame
Serving Network MAC entity

## Slide 16: Conclusions
This contribution presented coexistence problem in heterogeneous networks, and possible solutions for harmonizing resource management based on Media Independent Services Framework.
Media Independent Services Framework is a good platform to harmonize and federate resource management for heterogeneous APs that use various communication technologies.
Most of the Media Independent Service use cases need resource management based on Media Independent Services Framework, and thus the use case of resource management is mandatory.

## Slide 17: References
[1] IEEE P802.19.1™/D3.06, Draft Standard for TV White Space Coexistence Methods, Oct. 2013.
[2] IEEE Std. 802.15.2-2003, Part 15.2: Coexistence of Wireless Personal Area Networks with Other Wireless Devices Operating in Unlicensed Frequency Bands, Aug. 2013.
[3] IEEE Std. 802.11F ™ -2003, IEEE Trial-Use Recommended Practice for Multi-Vendor Access Point Interoperability via an Inter-Access Point Protocol Across Distribution Systems Supporting IEEE 802.11™ Operation, July 2003.
[4] IETF RFC 5415, Control And Provisioning of Wireless Access Points (CAPWAP) Protocol Specification, Mar. 2009.