## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-14-0021-00-SAUC-Handover-Use-Case
Title: 802.21.1 Handover Use Case
Date Submitted: January 22, 2014
To be presented at IEEE 802.21.1 TG, Los Angeles Wireless Interim
Authors or Source(s): Charlie Perkins
Abstract: This contribution proposes a handover management service for consideration within the 802.21.1 task group

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Handover Service
It has been decided to separate Media Independent Handover service out of the base Media Independent Services Framework document.
A new specification enabling single-radio handover (SRHO), developed within 802.21c task group, has recently been approved. Much of the SRHO specification should be included along with the handover services as specified within 802.21-2008.

## Slide 4: Handover Service features
Service continuity
Application class
Quality of service
Network discovery
Network selection
Power management
Handover policy
Proactive authentication and key establishment

## Slide 5: MIH Handover Events
MIH_Link_Handover_Imminent | L2 handover is imminent
MIH_Link_Handover_Complete | L2 handover has been completed

## Slide 6: MIH Handover Commands
MIH_Net_HO_Candidate_Query | Initiate handover
MIH_MN_HO_Candidate_Query | Initiate MN query request for candidate network
MIH_N2N_HO_Query_Resources | Query available network resources
MIH_MN_HO_Commit | Notify the serving network of the decided target network information
MIH_Net_HO_Commit | Network has committed to handover
MIH_N2N_HO_Commit | Notify target network that the serving network has committed to handover
MIH_MN_HO_Complete | Initiate MN handover complete notification
MIH_N2N_HO_Complete | Handover has been completed

## Slide 7: MIH Handover Information
MIH_Get_Information | Request to get information from repository
MIH_Push_Information | Notify the mobile node of operator policies or other information

## Slide 8: Handover examples
Mobile-initiated handover procedure
Network-initiated handover procedure
Example handover flow chart IEEE 802.11  IEEE 802.16
Example handover flow chart for Proxy Mobile IPv6
Network selection in IEEE 802.11 (WLAN) using IEEE 802.21
Abnormal case at the stage of resource availability check

## Slide 9: Type values for TLV encoding
MBB handover support | 10 | LIST (MBB_HO_SUPP)
New link identifier | 14 | LINK_TUPLE_ID
Old access router | 15 | LINK_ADDR
New access router | 16 | LINK_ADDR
IP renewal flag | 17 | IP_RENEWAL_FLAG
Mobility management support | 18 | IP_MOB_MGMT
Handover resource query list | 33 | QOS_LIST
Handover status | 34 | HO_STATUS
Handover result | 40 | HO_RESULT
Target network info | 55 | TGT_NET_INFO
List of target network info | 56 | LIST (TGT_NET_INFO)

## Slide 10: Need for coordination with 802.21m
Many handover service parameters could be renamed using more generic terms, and conceivably applicable to other use cases not related to handover
Not obvious whether such use cases are likely to exist in the future
Should pick one of the following two guidelines:
  Include handover features in handover use case, and if wider applicability is discovered, move into 802.21m
  Move as many features into 802.21m, renamed for wider applicability
Note: 802.21m was originally envisioned to reduce the burden of implementing 802.21 media independent services…