## Slide 1: 802.21+SDN integrated scenarios and new PoA-related primitives
Daniel Corujo <dcorujo@av.it.pt>
Carlos Guimarães <cguimaraes@av.it.pt>
Rui L. Aguiar <ruilaa@ua.pt>
http://atnog.av.it.pt

## Slide 2: Outline
Setting for the demo
Use Case description
Demo walkthrough
Experimental Results
Supportive PoA Primitives

## Slide 3: Setting for the Demo
Our research group (http://atnog.av.it.pt) was involved in the EU FP7 OFELIA research project (http://www.fp7-ofelia.eu)
  OpenFlow-based large-scale federated experimental testbed
We provided a set of use cases that exploited the capabilities of the testbed
  A transmission mechanism where the information flows were managed via SDN
  802.21 was used to allow preemptive flow establishment in the handover candidate point, in wireless handover scenarios

## Slide 4: Key Concepts
Leveraging SDN-based mechanisms to abstract the control of wired and wireless access networks, through the usage of OpenFlow and MIH (IEEE 802.21) protocols;
Seamless handover over the SDN-based flow creation (in this case, for a video flow)

## Slide 5: Use Case Description
Setup:
  This demo involves one MN, 2 Aps, a PoS and a Video Server
Sequence:
  The MN is initially connected to network#1, receiving video from the video server;
  While the video is streamed, the signal strength of network#1 is decreased;
  The weakening of the signal strength is detected by the MN, triggering mechanisms for detecting a better handover candidate;
  The MN initiates the handover procedure to move to network#2. Mobility is triggered by the MN and supported by the DTSA. Seamless handover is achieved thanks to EDOBRA enhancements by preemptively extending the MN’s workspaces before the execution of the handover;
  Since network#1 does not have more subscribers for the workspace, the workspace flow is removed from network#1, for added optimization.

## Slide 6: Demo Walkthrough
Demo1: Video Comparison
  http://atnog.av.it.pt/~cguimaraes/video_comparison.mp4
Here the original video is compared against the SDN flow-based distributed mechanism (named ETArch), in a handover situation
  In one window, we see ETArch supported with 802.21 mechanisms
  The other window, shows regular ETArch operation, without 802.21 assistance

## Slide 7: Demo Walkthrough
Demo2: Command Line and Performance
  http://atnog.av.it.pt/~cguimaraes/demo.ogv
Same demo as before, but under the perspective of the Mobile Node, AP1 and AP2
The left side shows the traffic passing through ‘wlan0’ and, after the handover, through ‘wlan2’
The command line window on the left side shows the MN’s MIH-User output, based on the 802.21 open-source implementation ODTONE (http://atnog.av.it.pt/odtone)
On the right side, the 1st blue terminal shows a traffic capture on AP1 (showing where the video starts), and the red terminal shows the traffic capture for AP2 (showing the video passing after the handover)
The smaller blue terminal window on AP1 illustrates the txpower reduction command that was used to trigger the handover
  i.e., simulates that the conditions in AP1 deteriorated

## Slide 8: Benefits
Using an IEEE 802.21-enabled enabled ETArch solution, the MN is able to receive content without any interruption during the handover process. This design progresses over the raw ETArch solution, where the content reception is interrupted once it needs to unregister from the previous flow through the old network and to re-register through the new network.

## Slide 9: Supportive Primitives
With SDN operation being done over network switching equipment…
  … particularly considering the AP’s when envisaging SDN supporting wireless technologies (i.e., 802.11)
… provides the incentive to consider PoA-based primitives
  … which can also be used to leverage SDN+802.21 integration

## Slide 10: Supportive Primitives
Primitives considered:
  Link Probe Client
    Used by the OpenFlow Controller to request the OpenFlow Switch to probe an associated station. It issues the switch to send a null data frame to the sattion, reporting when the frame is acknowledged.
  Station Attached
    Event sent by the OpenFlow switch to notify about the detection of the attachment of a new station.
      This event could be supported by a non-OpenFlow PoA, acting similarly to a “Link_Up”, but sent from the PoA (instead of the MN)
  Station Detached
    Event sent by the OpenFlow switch to notify about the detection of the detachment of a new station.
      This event could be supported by a non-OpenFlow PoA, acting similarly to a “Link_Going_Down” or “Link_Down” or “Link_Parameters_Change”, but sent from the PoA (instead of the MN)

## Slide 11: Primitive Details
Link Probe Client
  Request
  Response
struct ofp_probe_cliente_request {
uint32_t port_no /* OFMP_PORT message must request
statistics either for a single
port (specified in port_no) or
for all ports (if port_no == OFPP_ANY). */
link_addr sta_addr /* Link Address of the station to probe */
};
struct ofp_probe_cliente_response {
uint8_t status /* One of OFPRB_* . */
};
enum ofp_probe_status {
OFPRB_ACKNOWLEDGED = 0,
OFPRB_NOT_ACKNOWLEDGED = 1,
OFPRB_UNSPECIFIED_ERROR = 2,
};
Similar to LINK_ADDR of IEEE 802.21

## Slide 12: Primitive Details
Station Attached
struct ofp_station_attached {
uint32_t port_no /* OFMP_PORT message must request
statistics either for a single
port (specified in port_no).
OFPP_ANY not allowed. */
link_addr sta_addr /* Link Address of the station attached */
};
Similar to LINK_ADDR of IEEE 802.21

## Slide 13: Primitive Details
Station Detached
struct ofp_station_detached {
uint32_t port_no; /* OFMP_PORT message must request
statistics either for a single
port (specified in port_no).
OFPP_ANY not allowed. */
link_addr sta_addr; /* Link Address of the station dettached */
uint8_t reason; /* Reason why the link went down.
One of the OFDTC_* . */
};
enum ofp_detach_reason {
OFDTC_EXPLICIT_DISCONNECT = 0,
OFDTC_PACKET_TIMEOUT = 1,
OFDTC_NO_RESOURCE = 2,
OFDTC_NO_BROADCAST = 3,
OFDTC_AUTHENTICATION_FAILURE = 4,
OFDTC_BILING_FAILURE = 5,
};
Similar to LINK_ADDR of IEEE 802.21