## Slide 1
IEEE 802.21.1 MEDIA INDEPENDENT SERVICES
DCN: 21-14-0112-00-SAUC
Title: Considerations for MIS framework to cooperate with SDN
Date Submitted: July 11th, 2014
Presented at IEEE 802.21 Session #63 – San Diego, USA
Authors or Source(s):
Hyeong-Ho Lee(ETRI), Hyunho Park(ETRI), Jin Seek Choi (Hanyang University, Korea Ethernet Forum), and Myung-ki Shin (ETRI)
Abstract: This document presents considerations for MIS framework to cooperate with SDN (Software-Defined Networking).

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Definitions of SDN and MIS Framework
SDN (Software-Defined Networking)*
  Definition from Wikipedia [1]: Computer networking that allows network administrators to manage network services through abstraction or lower level functionality
  Definition from ONF [2]: The physical separation of the network control plane from the forwarding plane, and where a control plane controls several devices.
MIS (Media Independent Services) framework
  Framework to facilitate interworking between IEEE 802 networks for improving the user experience of mobile devices by describing the necessary
  [1] http://en.wikipedia.org/wiki/Software-defined_networking
  [2] https://www.opennetworking.org/sdn-resources/sdn-definition

## Slide 4: Comparison of SDN and MIS Framework
SDN protocol (e.g., Open Flow)
Protocol between controller and switches
Usually focuses on data path control and resource management
Popular protocol for controlling networks
MIS framework
Protocol among PoS (Point of Service), PoA (Point of Attachment), and MN (Mobile Node)
Focuses on mobility management and radio resource management
SDN Controller
SDN Switch
SDN Protocol
MN
PoA
MIS PoS
MIS Protocol
Access Controller
(MIS PoS)
Switch/
Router
(MIS PoS)

## Slide 5: Scenarios for Integrating SDN and MIS Framework
MIS Framework with functions of
data path control and resource management
SDN
MIS Framework
SDN
Extension of
MIS framework
with SDN function
3. Cooperation between
MIS framework and SDN protocol
SDN
with functions of
mobility management and radio resource management
MISF
2. Extension of
SDN protocol
With MIS function
Signalling on
mobility and
radio resource management
Signalling on
data path control and
resource management

## Slide 6: Extension of MIS Framework with SDN function
MIS framework can be one of candidate protocol for SDN because MIS framework enables integrations among network entities (i.e., PoS and PoA) and MN.
Requirements: Extension of MIS framework to control switches or routers is needed.
MIS protocol needs to compete with other SDN protocols (e.g., OpenFlow).
MN
PoA
Router/Switch (MIS PoS)
as SDN switch
MIS Framework with functions of
data path control and resource management
SDN
Access Controller (MIS PoS)
as SDN Controller
MIS Protocol with functions of
data path control and resource management

## Slide 7: 2. Extension of SDN Protocol with MIS Function
SDN protocol (e.g., OpenFlow) needs to extend its protocol for mobility and radio resource management.
Requirements: Extension of SDN protocol with MIS function (MISF) to support mobility and radio resource management
MN
PoA
SDN Controller
with MISF
SDN Protocol
with MISF
for mobility and
radio resource management
SDN Switch
SDN
with functions of
mobility management and radio resource management
MISF

## Slide 8: 3. Cooperation between MIS framework and SDN protocol
Network entities of MIS framework and SDN protocol may cooperate each other for optimizing data path control, mobility management, and resource management in both wireless and wired networks.
Requirements
  Interfaces between MIS protocol and SDN protocol are needed
SDN function and MISF can exist in the same physical network entities.
MIS Framework
SDN
Signalling on
mobility and
radio resource management
Signalling on
data path control and
resource management of wired networks
Signalling between MIS and SDN network entities
Access Controller (MIS PoS)
Router/ Switch
(MIS PoS)
SDN Controller
SDN Switch
PoA
PoA
MN
MN

## Slide 9: Conclusions
SDN and MIS framework are open platform to control networks
  SDN usually focuses on data path control and resource management of wired networks.
  MIS framework focuses on mobility management and radio resource management.
Scenarios for Integrating SDN and MIS Framework
  Extension of MIS framework with SDN function
  Extension of SDN protocol with MIS function
  Cooperation between MIS framework and SDN protocol
  Further discussions on SDN issues for IEEE 802.21.1 task group
  Cooperation between MIS framework and SDN protocol will be important in future because it shows complementary relationship between MIS framework and SDN protocol.
  For the cooperation, interfaces between MIS framework and SDN protocol should be discussed in IEEE 802.21.1 task group.

## Slide 10: References
21-14-0017-00, Daniel Corujo et. al., 802.21 for SDN-based flow handover in wireless environments.
21-14-0029-00, Daniel Corujo et. al., 802.21+SDN integrated scenarios and new PoA-related primitives.
Carlos Guimarães et. al., Empowering Software Defined Wireless Networks Through Media Independent Handover Management, Globecom 2013.
Carlos Guimarães et. al., Enhancing OpenFlow with Media Independent Management Capabilities, ICC 2014.
21-14-0060-00, Charles E. Perkins, OpenFlow PoA proposal for SDN use case