## Slide 1
IEEE 802.21.1 MEDIA INDEPENDENT SERVICES
DCN: 21-14-0122-00-SAUC
Title: Needs of Link_Resource_Report and MIS_Resource_Report primitives/messages
Date Submitted: July 17th, 2014
Presented at IEEE 802.21 Session #63 – San Diego, USA
Authors or Source(s):
Hyeong-Ho Lee(ETRI) and Hyunho Park(ETRI)
Abstract: This document presents needs of new primitives/messages (i.e., Link_Resource_Report and MIS_Resource_Report) for reporting allocated radio resources. Link_Resource_Report and MIS_Resource_Report primitives/messages are explained in “Media Independent Services Framework for Radio Resource Management in Heterogeneous Networks” (DCN: 21-14-0111-00-SAUC).

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Comparisons of Usages
Primitive/ Message | Link_Resorce_Report, MIS_Resource_Report | Link_Detected, MIS_Link_Detected | Link_Parameters_Report MIS_Link_Parameters_Report
Proposed new/ Preexisting | Proposed new primitive/ Proposed new message | Preexisting primitive/ Preexisting message (Clause 7.3.1 in IEEE 802.21-2008 Std.) | Preexisting primitive/ Preexisting message (Clause 7.3.4 in IEEE 802.21-2008 Std.)
Usages | Indicates allocated radio resources (e.g., frequency, time, and transmit power) | Implies that the MN is in the coverage area. | Indicates changes in link conditions (e.g., data rate, signal strength, and packet error rate) that have crossed specified threshold levels.
Usage comparisons with Link_Resorce_Report/ MIS_Resource_Report | - | Link_Resource_Report/MIS_Resource_Reoprt indicates allocated radio resources in access networks, but Link_Detected/MIS_Link_Detected indicates existence of MN. | Link_Resource_Report/MIS_Resource_Reoprt indicates value of allocation, but Link_Parameters_Report/ MIS_Link_Parameters_Report indicates value of measurement.
Link_Resource_Report/MIS_Resource_Report and Link_Detected/MIS_Link_Detected cannot be merged because their usages are totally different.

## Slide 4: Comparisons of MIS Type
Primitive/ Message | Link_Resorce_Report, MIS_Resource_Report | Link_Detected, MIS_Link_Detected | Link_Parameters_Report MIS_Link_Parameters_Report
MIS Type | Should be command service that has request and response to check whether the reports are sent appropriately or not. | Is event service that has unidirectional indication to present detected link. | Is event service that has unidirectional indication to present measured link parameters.
Command service and event service have different values of Service Identifier (SID) in MIS message protocol (See Table 23 of page 153) in IEEE 802.21-2008 Std. Thus, Link_Resource_Report/MIS_Resource_Report cannot be merged into Link_Detected/MIS_Link_Detected or Link_Parameters_Report/ MIS_Link_Parameters_Report.

## Slide 5: Comparisons of Parameters
Primitive/ Message | Link_Resorce_Report, MIS_Resource_Report | Link_Detected, MIS_Link_Detected | Link_Parameters_Report MIS_Link_Parameters_Report
Parameters | Parameters to present allocated radio resources are needed. Radio resources can be frequency, time, and transmit power. Examples of parameter values: identifier of allocated frequency band/channel, identifier of allocated time slot number, and identifier of allocated transmit power | LINK_DET_INFO: Indicated a detected link. LINK_DET_INFO includes signal strength of the detected link (SIG_STRENGTH) and maximum transmission rate on the detected link (LINK_DATA_RATE). See Table F.20 in page 249 in IEEE 802.21-2008 Std. | LINK_PARAM_RPT: Represents a link parameter report. LINK_PARAM_RPT includes data rate, signal strength, SINR, throughput, packet error data rate. See Table F.4 in page 231 in IEEE 802.21-2008 Std. See an example (LINK_PARAM_GEN) of LINK_PARAM_RPT in Table F.4 in page 230 in IEEE 802.21-2008 Std.
Parameters comparisons of Link_Resorce_Report/ MIS_Resource_Report | - | Parameters of Link_Resorce_Report/ MIS_Resource_Report have allocated values, but parameters of Link_Detected/ MIS_Link_Detected have measured values. | Parameters of Link_Resorce_Report/ MIS_Resource_Report have allocated values, but parameters of Link_Parameters_Report/ MIS_Link_Parameters_Report have measured values.

## Slide 6: Conclusions
Link_Resource_Report/MIS_Resource_Report and Link_Detected/MIS_Link_Detected cannot be merged because they have different usages each other.
Link_Resource_Report/MIS_Resource_Report should be command service, but Link_Detected/MIS_Link_Detected and Link_Parameters_Report/MIS_Link_Parameters_Report are event service.
Link_Resource_Report/MIS_Resource_Report have different types of parameter values from Link_Detected/MIS_Link_Detected and Link_Parameters_Report/MIS_Link_Parameters_Report.
Therefore, making new primitives/messages (i.e., Link_Resource_Report/MIS_Resource_Report) is the best solution.